## Slide 1: 11az related bits in the Extended Capabilities element
Date: 2019-01-14
Authors:

## Slide 2: Motivation/Background
A set of bits in the context of .11az needs to be added to the Extended Capabilities element
The criteria for a bit to be added to the Extended Capabilities element is “does the ISTA need this information in order to determine if a .11az negotiation should be initiated with the corresponding RSTA?”
In this presentation, we
  Identify the bits that need to be added to Extended Capabilities element

## Slide 3: Terminology
Roles
  Initiator: the implementation is an initiator (ISTA)
  Responder: the implementation is a responder (RSTA)
Ranging from an ISTA’s perspective
  Active: the implementation actively exchanges frames for ranging
  Passive: the implementation only receives/listens
Ranging Mode
  TB
  nTB
  scheduled EDCA (aka FTM): ranging over 2.4, 5 and 60 GHz using scheduled (for burst periods) and EDCA (for gaining access to the media in order to transmit FTM frames)

## Slide 4: Bit(s) in Extended Capabilities element (included in 2.4/5GHz Beacons)
Feature:
Bit-70: [FTM] Responder
  the implementation is a responder only EDCA FTM (2.4/5 GHz)
Bit-71: [FTM] initiator
  the implementation is an initiator only for EDCA FTM (2.4/5 GHz)
Bit-<ANA+1>: nTB Ranging Responder
Bit-<ANA+2>: TB Ranging Responder
Bit <ANA+3>: Secure LTF Support (support for Secure nTB and TB ranging), (.11az D0.6)
Bit-<ANA+4>: TB Passive Ranging Responder (.11az D0.6)
Bit-<ANA+5>: TB Passive Ranging Initiator (.11az D0.6)
Policy:
Bit <ANA+7>: RSTA requires PMF protected IFTMR/IFTM and LMR exchange (TB and nTB)
Color Coding: Existing bits; Proposed bits to be added

## Slide 5: nTB Ranging Responder
The implementation is a non-Trigger Based Ranging Responder
  Supports the role of a Responder for the Range Measurement procedure described in Cl. 11.22.6.4.4

## Slide 6: TB Ranging Responder
The implementation is a Trigger Based Ranging Responder
  Supports the role of a Responder for the Range Measurement procedure described in Cl. 11.22.6.4.3

## Slide 7: Secure TB and nTB Range Measurement
The implementation supports Secure Range Measurement
  Supports the Secure Range Measurement procedures described in Cl. 11.22.6.4.6
  Non-Trigger Based and/or Trigger Based, depending on the setting of nTB Ranging Responder and TB Ranging Responder bits

## Slide 8: RSTA requires PMF protected IFTMR/IFTM and LMR exchange (TB and nTB)
This is a policy (not capability)
RSTA indicates that would honor Initial Fine Timing Measurement Request from ISTAs if and only if a security context is successfully negotiated between the ISTA and RSTA.
  Security Context is established either by association or PASN
IFTMR/IFTM and LMR exchanges are ‘Integrity Protected’
Can be used with or without ‘Secure TB and nTB Range Measurement’ enabled

## Slide 9: Straw Poll
We support adding the following bits to the Extended Capabilities element:
  nTB Ranging Responder
  TB Ranging Responder
  RSTA requires PMF protected IFTMR/IFTM and LMR exchange (TB and nTB) – RSTA Policy
Y: N: Abstain:

## Slide 10: Backup