## Slide 1: Proposal for New Action Frame to Aid Mac Randomization Handling
Date: 2019-01-15
Authors:

## Slide 2: Abstract
Proposal to add a new action frame that an AP can use to query an associated STA for a unique identifier.

## Slide 3: Prior Discussions
MAC randomization has shifted from a theoretical discussion to widespread deployments
Different devices are offering MAC randomization features with different behaviors
MAC randomization causes issues for APs as they deal with associated and unassociated STAs.
This proposal seeks to help an AP with a STA that is already associated.
  Unassociated STAs are still a challenge.

## Slide 4: Allow an AP to request an ID from a STA
We propose a new action frame exchange that an AP can initiate with an associated STA to request a unique identifier from the STA for future use
The exchange would be secured and kept private.
The unique ID would not have any requirements of form
  Though an actual MAC address or serial number might be easy for implementers

## Slide 5: Request Frame Format
Requesting Network Type | Encryption Enabled
1 byte | 1 byte
Field | Value | Comment
Requesting Network Type | 1 -- Private Data Network 2 – Private Guest Network 3 – Hotspot Network 4-7 – reserved | Allows for a Network Type to which STA can then filter to determine whether or not to reply.
Encryption Enabled | 0 – Not Encrypted 1 -- Encrypted 4-7 – reserved | Allows STA to determine the encryption on the information it provides. Could blow this out to include the network encryption type.

## Slide 6: Response Frame Format
Response Code | Length (optional) | Unique ID (optional) | Time to Live (optional) | Vendor Specific (optional)
1 byte | 1 byte | variable | 2 byte | 
Field | Value | Comment
Response Code | 0 – decline to provide code 1 – Provide code 2-7 – reserved | Allows for different user preferences to be accommodated while providing useful information to the AP.
Length of Unique ID | 1 byte | Allows for efficient messages
Unique ID | No restrictions on value provided | Provide unique identifier that AP may rely upon for other identification dependent features.
Time to Live | Not included – defaults to permanent use of given ID 0 – per association 1-FFFF – time in seconds ID remains valid | Optional field with default to permanent use of ID if not specified 0000 – per association Other values are time to live for ID in seconds
Vendor Specific Options |  | Useful because vendors have not implemented rMAC in a standardized fashion

## Slide 7: Summary
AP needs more information to provide additional services when a STA uses a randomized MAC address
A message allowing an AP to query an associated STA for a unique ID with some informative parameters could be structured to allow a STA to opt in to sharing at least minimal information.
The STA could still ignore the message or decline to provide a unique identifier.