## Slide 1: Proposal for New Action Frame to Aid Mac Randomization Handling
Date: 2019-07-18
Authors:

## Slide 2: Abstract
Proposal to add a new action frame that an AP can use to query an associated STA for a unique identifier.

## Slide 3: Background
MAC randomization has shifted from a theoretical discussion to widespread deployments
Different devices are offering MAC randomization features with different behaviors
Some devices already use randomized MAC addresses when they probe by default.
Some devices allow the user to enable the use of randomized MAC addresses when a device is associated.
  With some operating systems, the random MAC may be remembered and reused for a specific SSID, and it may also age out after a period of time to be replaced by a new randomized MAC.

## Slide 4: Background
MAC randomization can cause issues for APs as they deal with associated and unassociated STAs.
A recent liaison from WBA highlighted the many uses of MAC addresses within residential and enterprise products that may be affected by MAC randomization if it is widely used after association. (11-18-1579-01)
  device steering (already potentially affected for initial association), parental controls, network access controls (PassPoint), device limits, legal intercept, diagnostics
It is important to note that because many users take advantage of the current systems, they will experience a perceived loss of utility when they are forced to log in every time because the AP or a supervising system will not recognize the STA.
  These users may view the ability to use a stored randomized MAC address as still providing them with privacy when it really does not.
This proposal seeks to help an AP with a STA that is already associated.
  Unassociated STAs are still a challenge.

## Slide 5: Allow an AP to request an ID from a STA
We propose a new action frame exchange that an AP can initiate with an associated STA to request a unique identifier from the STA for future use
The exchange would be secured and kept private.
The ID would have minimal requirements of form
  16 octets
  Large enough to allow the use of a UUID
  Not guaranteed to be unique, but if the STA replies with an ID, the STA should be motivated to make it unique
The ID Query message could be sent whether or not the STA provided a local MAC address
  Not all STAs have complied with the recommended use of a local MAC address.

## Slide 6: Request Frame Format
The Request frame allows an AP to query an associated STA for a unique identifier.
Category | ID Query Action | Vendor Specific (optional)
Octets: 1 1 Variable

## Slide 7: Response Frame Format
The Response Frame format allows the responding STA to indicate either that it will not provide an ID or that it will.
The Response includes an optional 16 octet ID field, if the STA decides to provide one.
The Response includes a Length field to allow for vendor specific information.
The Response also includes a Time To Live field so that the STA can indicate if the ID will only be good for a certain amount of time.
A Vendor Specific field is also included in the Response to allow vendor differentiation.
Octets: 1 1 1 2 16 2 Variable
Category | ID Query Action | Response | Length (optional) | ID (optional) | TTL (optional) | Vendor Specific (optional)

## Slide 8: Advertisement of Support for ID Query
To address comments brought after the past presentation, a Extended Capability bit is proposed for STAs.
The IDQuery_Support bit set to 1 indicates that a STA can support an ID Query action frame.
At a higher layer, a user may direct a STA to not share a permanent or semi-permanent identifier, so a STA may still decline to provide an ID even though it indicates support for the message.

## Slide 9: Summary
AP and larger network needs more information to provide additional services when a STA uses a randomized MAC address after associating.
A message allowing an AP to query an associated STA for a unique ID with some informative parameters could be structured to allow a STA to opt in to sharing at least minimal information.
The STA could still ignore the message or decline to provide a unique identifier.