## Slide 1: Variant Capability ERP and HT Devices
Date: 2019-08-30
CIDs addressed: LB 236 CID 2186 (with different proposed change)
r0 (January 16, 2019): Initial draft
r1 (August 30, 2019): Revision incorporating many changes based on feedback received (for which thanks); title changed

## Slide 2: Abstract
For very low power Wi-Fi IoT applications operating at 2.4 GHz, designers currently must choose between baseline 802.11 (DSSS), 11b (HR), 11g (ERP), and 11n (HT).
Each poses problems:
ERP devices are required to support 1, 2, 5.5, 11 HR/DSSS and 6, 12, and 24 Mbps rates: the OFDM rates are burdensome and the data rates are often overkill
HT adds STBC (good), but also 8 more OFDM rates, extending to 65 Mbps (very bad)
But DSSS- and HR/DSSS-only devices don’t do any OFDM preamble detect, require single-tone protection modes, increasing time on air and lowering power consumption for all devices in the BSS, including themselves
IoT applications and requirements are very heterogeneous, and Wi-Fi is widely perceived to be “high power” in this market segment.
It would be useful, and it would help promote Wi-Fi, to widen the design space to allow variant ERP and HT devices.
This presentation proposes a fully backwards compatible way of achieving this

## Slide 3: Overview and summary
An ERP or HT device that omits some higher data rate modes is indistinguishable from a device that implements all the modes but is operating at long range—which is a scenario that has always been present
The proposal permits non-AP STAs that operate at 2.4 GHz to implement any subset of rates that satisfies a streamlined set of requirements
—Just enough to mimic regular devices at long range
  1 Mbps, 2 Mbps, 6 Mbps mandatory
    All other data rates optional (subject to requirement below)
    Data rate supported  all otherwise mandatory lower rates of same type required
  STA associates as ERP or HT device—no single-tone protection asked for or given
  Short (9 ms) slot time mandatory

## Slide 4: CID 2186

## Slide 5: Summary of r1 changes, versus r0 (1/4)
Added 6 Mbps OFDM as a mandatory rate
  This is the most significant change; a result of feedback received from multiple sources
  Adding this rate greatly simplifies coexistence and interoperability: these Class 2 devices will recognize all OFDM preambles and will be able to defer properly
  Requires implementation of an OFDM modem, when one motivation of the original proposal was to allow for the possibility of avoiding that—but the fact that only 6 Mbps needs to be implemented maximizes implementer flexibility, and simplifies the requirements compared to a full OFDM modem (65 Mbps)
Changed the name “RC-HT” (“Reduced Capability” HT) to “Class 2 HT”
  r0 incorrectly assumed that short (9 ms) slot time was mandatory for all HT devices. In the March 2019 meeting, it emerged that this is not correct. Substantially all new HT devices shipped in (at least) the last 10 years have implemented short slot time, but it is still optional in the IEEE spec. The proposal retains the requirement that the new, variant, devices support short slot time, but this is now an additional requirement, so the new, variant, devices are not necessarily “reduced” capability any more.

## Slide 6: Summary of r1 changes, versus r0 (2/4)
Added analogous “Class 2” ERP devices
  r0 only had variant HT devices; one comment received was why no variant ERP? No reason, really: it can all work either way. Since it may be confusing to have an “HT” device that has no HT modes, this presentation adds the analogous Class 2 ERP modes. A class 2 device that has no HT-only modes is Class 2 ERP.
  This reasoning doesn’t extend to DSSS / HR/DSSS devices because of short slot time
Made mandatory support for short slot time in Class 2 ERP and HT devices explicit
  This was implied in the discussion in r0, but was assumed (incorrectly) to be implied by the requirement that “otherwise” the device satisfied all requirements of HT devices.

## Slide 7: Summary of r1 changes, versus r0 (3/4)
Added requirement to support all otherwise mandatory data rates of same type (single tone or OFDM) lower than any supported rate
  r0 required all variant devices to support (DSSS) 1 and 2 Mbps, and (if any OFDM mode was supported) to support (OFDM) 6 Mbps
  The underlying logic for the proposal (both r0 and r1 versions) is that rate fallback will ensure backwards compatibility and interoperability: there should be no practical distinction between Class 2 devices (which don’t implement higher modes) and regular devices at longer range (where the modes have been implemented but are not operational—which happens all the time)
  It is conceivable that under the r0 proposal, a legacy implementation’s rate fallback algorithm could be confused by the presence of gaps in the variant device’s mandatory rates. Even this should be fine (at most it might cause occasional additional attempts at unsupported rates); but on the other hand it adds virtually no additional complexity to rule out the gaps.

## Slide 8: Summary of r1 changes, versus r0 (4/4)
Added capability bits for the new functionality
  Based on feedback received on r0
  Though legacy devices will, clearly, not interpret these capability bits and should be fine anyway, newer APs will be able to figure out what’s going on, and it may help them manage their BSSs
  N.B.: no additional requirements are placed on APs as a result of these capability bits (unlike the analogous OMI case). It is useful to provide for an existing rate management scheme to be ported in its entirety from a legacy AP to a new AP, without having to worry about falling out of compliance.
Modified minimum receiver sensitivity criteria and made mandatory if mode is supported
  In r0, minimum receiver sensitivity requirements were optional
  However, this (arguably) has a knock-on effect on CCA. For example, for OFDM the STA must be able to detect start of valid PPDU at power > -82 dBm with probability > 90% and defer for the indicated duration—this requires the 6 Mbps L-SIG to be decoded.
  Minimum receiver sensitivity PPDU payload changed to 100 bytes rather than 1000

## Slide 9: Rates beyond 1, 2, 6 Mbps
Rates beyond 1, 2, 6 Mbps still not required
  We discussed whether 5.5 and/or 11 Mbps, and even some other rates, should be added as requirements, on the basis that it is a common industry practice for APs to beacon at 5.5 Mbps for efficiency reasons—even up to 24 Mbps
  But adding all of these modes would eliminate all of the rationale for this proposal, and adding some of them would eliminate most of it
    If your product must be able to associate with any possible AP, then you should design a dual-band 2.4 / 5 GHz ERP/OFDM, HT or VHT device (and soon you should design a tri-band device)
    The proposal allows for optimized, low power, low complexity IoT STAs to communicate with off-the-shelf APs--with any AP that is configured to beacon at 1, 2, or 6 Mb/s
  Also, we should be careful to preserve the full potential range of Wi-Fi IoT networks, down to 1 Mbps
    Strong feedback was received in 11mc that this is important, e.g., for competitive positioning
    Cementing 5.5 Mbps as an all-but-exclusive beacon rate would cut across this message
  APs should be able to beacon at 1 Mbps if they want to
    N.B. under both r0 and r1, APs will retain all rates that are currently mandatory

## Slide 10: Proposed change—1/12
Add at end of first paragraph of 18.1.1 (General) (D2.0 2936.13):
"In addition, a variant capability PHY based on the ERP (“ERP Class 2") is defined in this clause.“

## Slide 11: Proposed change—2/12
Add new paragraph at the end of 18.1.2 (Introduction) (D2.0 2936.25):
“A non-AP STA is a Class 2 ERP STA if it satisfies all of the following requirements and is not an ERP STA:
The STA shall operate in the 2.4 GHz band, and shall have operating channel width 20 MHz;
The STA shall support transmission and reception of DSSS 1 Mb/s and 2 Mb/s;
The STA shall support transmission and reception of ERP-OFDM 6 Mb/s;
If the STA supports HR/DSSS 11 Mb/s, then it shall support HR/DSSS 5.5 Mbps;
If the STA supports ERP-OFDM 24 Mbps then it shall support ERP-OFDM 12 Mbps;
Subject to (4) and (5), each (non-DSSS) HR/DSSS, (non-6 Mb/s) ERP-OFDM, and HT data rate is optional;
The STA shall support transmission and reception of DSSS long preamble and short preamble;
The STA shall support short slot time;
The CCA functionality for ERP-OFDM in 18.4.6(a),(b) and for HT in 19.3.19.5.4 shall be supported;
The minimum receiver sensitivity requirements of Clauses 15, 16, 18, and 19 shall apply, except that the reference PPDU length shall be 100 octets;
A class 2-ERP STA shall signal ERP capabilities during association and reassociation, and in probe requests.
In all other respects the STA shall follow the requirements of the ERP.”

## Slide 12: Proposed change—3/12
Add at end of first paragraph of 19.1.1 (Introduction to the HT PHY) (D2.0 2941.10):
"In addition, a variant capability PHY based on the HT PHY ("HT Class 2 PHY") is defined in this clause.“

## Slide 13: Proposed change—4/12
Add new paragraph at the end of 19.1.1 (Introduction to the HT PHY) (D2.0 2941.41):
“A non-AP STA is a Class 2 HT STA if it satisfies all of the following requirements and is not an HT STA or Class 2 ERP STA:
The STA shall operate in the 2.4 GHz band, and shall have operating channel width 20 MHz;
The STA shall support transmission and reception of DSSS 1 Mb/s and 2 Mb/s;
The STA shall support transmission and reception of ERP-OFDM 6 Mb/s;
If the STA supports HR/DSSS 11 Mb/s, then it shall support HR/DSSS 5.5 Mbps;
If the STA supports ERP-OFDM 24 Mbps then it shall support ERP-OFDM 12 Mbps;
If the STA supports any Nss = 1 HT MCS > 0, then it shall support all Nss =1 HT lower MCSs;
Except as noted in (5), (6) and (7), each (non-DSSS) HR/DSSS and ERP-OFDM data rate and each HT MCS is optional;
The STA shall support DSSS long preamble and short preamble;
The STA shall support short slot time;
The CCA functionality for ERP-OFDM in 18.4.6(a),(b) and for HT in 19.3.19.5.4 shall be supported;
The minimum receiver sensitivity requirements of Clauses 15, 16, 18, and 19 shall apply, except that the reference PPDU length shall be 100 octets;

## Slide 14: Proposed change—5/12
A class 2-HT STA shall signal HT capabilities during association and reassociation, and in probe requests.
In all other respects the STA shall follow the requirements of the HT PHY.”

## Slide 15: Proposed change—6/12
Add new subsection 9.4.2.142 (Supplemental ERP Capabilities Information element) (D2.0 1439.30):
9.4.2.242 Supplemental ERP Capabilities Information element
9.4.2.242.1 Supplemental ERP Capabilities Information element structure
The Supplemental ERP Capabilities Information element contains a number of fields that advertise supported MCSs of a Class 2 ERP STA. For a Class 2 ERP STA, the Supplemental ERP Capabilities element is present in Association Request, Reassociation Request, and Probe Request frames. The Supplemental ERP Capabilities Information element is defined in Figure 9-772a.
Figure 9-772a—Supplemental ERP Capabilities Information element format
The Element ID and Length fields are defined in 9.4.2.1 (General).
The structure of the Supported MCS Set field format is defined in Figure 9-772b.
Element ID | Length | Supported MCS Set
Octets: 1 1 16

## Slide 16: Proposed change—7/12
Figure 9-772b Supported MCS Set field
The Rx MCS Bitmap is encoded as follows:
Bits B0-B1 represent 1, 2 Mb/s (DSSS) respectively;
Bits B2-B3 represent 5.5, 11 Mb/s (HR/DSSS) respectively;
Bits B4-B11 represent 6, 9, 12, 18, 24, 36, 48, 54 Mb/s (ERP-OFDM) respectively.
The Tx MCS Bitmap is encoded as follows:
Bits B16-B17 represent 1, 2 Mb/s (DSSS) respectively;
Bits B18-B19 represent 5.5, 11 Mb/s (HR/DSSS) respectively;
Bits B20-27 represent 6, 9, 12, 18, 24, 36, 48, 54 Mb/s (ERP-OFDM) respectively.
Bits: 12 4 12 4
Rx MCS Bitmap | Reserved | Tx MCS Bitmap | Reserved

## Slide 17: Proposed change—8/12
Add new subsection 9.4.2.143 (Supplemental HT Capabilities Information element) (D2.0 1439.30):
9.4.2.243 Supplemental HT Capabilities Information element
9.4.2.243.1 Supplemental HT Capabilities Information element structure
The Supplemental HT Capabilities Information element contains a number of fields that advertise supported MCSs of a Class 2 HT STA. For a Class 2 HT STA, the Supplemental HT Capabilities element is present in Association Request, Reassociation Request, and Probe Request frames. The Supplemental HT Capabilities Information element is defined in Figure 9-772c.
Figure 9-772c—Supplemental HT Capabilities Information element format
The Element ID and Length fields are defined in 9.4.2.1 (General).
The Supported MCS Set field format is defined in 9.4.2.55.2 (Supported MCS Set field).
Element ID | Length | Supported MCS Set
Octets: 1 1 16

## Slide 18: Proposed change—9/12
Add new rows immediately before last row in Table-9-36 (Association Request frame body) in 9.3.3.6 (Association Request frame format) (D2.0 855.30):
43 | Supplemental ERP Capability Indication | The Supplemental ERP Capability Indication is present when dot11VariantERPCapabilityOption is true; otherwise not present
44 | Supplemental HT Capability Indication | The Supplemental HT Capability Indication is present when dot11VariantHTCapabilityOption is true; otherwise not present

## Slide 19: Proposed change—10/12
Add new rows immediately before last row in Table-9-38 (Reassociation Request frame body) in 9.3.3.8 (Reassociation Request frame format) (D2.0 861.22):
48 | Supplemental ERP Capability Indication | The Supplemental ERP Capability Indication is present when dot11VariantERPCapabilityOption is true; otherwise not present
49 | Supplemental HT Capability Indication | The Supplemental HT Capability Indication is present when dot11VariantHTCapabilityOption is true; otherwise not present

## Slide 20: Proposed change—11/12
Add new rows immediately before last row in Table-9-40 (Probe Request frame body) in 9.3.3.10 (Probe Request frame format) (D2.0 867.10):
33 | Supplemental ERP Capability Indication | The Supplemental ERP Capability Indication is present when dot11VariantERPCapabilityOption is true; otherwise not present
34 | Supplemental HT Capability Indication | The Supplemental HT Capability Indication is present when dot11VariantHTCapabilityOption is true; otherwise not present

## Slide 21: Proposed change—12/12
Add new rows immediately before last row in Table-9-94 (Element IDs) in 9.4.2.1 (General) (D2.0 979.39):
and in the last row of the same table, third column, change “56” to “59”.
Supplemental ERP Capability Information (see 9.4.2.242 (Supplemental ERP Capability Information element) | 255 | 57 | No | No
Supplemental HT Capability Information (see 9.4.2.243 (Supplemental HT Capability Information element) | 255 | 58 | Yes | No

## Slide 22: Comments—I
Interoperability:
  No real distinction between Class 2 ERP/HT devices and ERP/HT devices operating at long enough range that many data rates don’t work—this happens all the time
  Including all lower mandatory rates ensures that fallback ends up with rates that work
  If beacons are sent at a rate the Class 2 ERP/HT STA supports (e.g., 1 Mbps), and then later change to a rate the class 2 ERP/HT STA doesn’t support (e.g., 11 Mbps), the STA will associate but later drop—a corner case but again same as case where the STA is too far
Class 2 ERP/HT versus pure DSSS or HR/DSSS:
  A Class 2 ERP/HT device differs from a DSSS or HR/DSSS device as follows:
    Class 2 ERP/HT STA supports 6 Mb/s OFDM, plus all OFDM CCA
      Though the “ERP/HT” nomenclature suggests reduced capability, this can also be seen as enabling DSSS or HR/DSSS devices with extra capabilities, esp. adding 6 Mb/s OFDM
    Class 2 ERP/HT STA supports short (9 ms) slot time—not defined in Clauses 15/16 and no way to signal (APs must switch to 20 ms slot when NonERP device associates)
    Class 2 ERP/HT STA does not trigger required single-tone protection for all transmissions in the BSS (and OBSSs)

## Slide 23: Comments—II
No change to other rules:
  All devices continue to support transmission and reception of 1 Mbps and 2 Mbps DSSS, and the DSSS long preamble
  Requirements to protect pure DSSS / HR/DSSS devices remain unchanged—designers remain free to choose such devices
No additional requirements for other devices
  Class 2 ERP/HT STAs represent themselves as an ERP or HT STA; it doesn’t ask for any special treatment by AP
Advantages for Class 2 ERP or HT:
  IEEE compliant, so (in principle) can use technology from Clauses 15-19
  Standardization of requirements—high degree of flexibility, but not unlimited—eases the task of managing variant devices
  IEEE adoption helps get modes adopted in other industry organizations

## Slide 24: Motion
Motion: Add the changes shown on slides 9-21 of this document to the REVmd draft.