## Slide 1: TGbd agreed terminology and requirements
Date: 2019-01-17
Authors:

## Slide 2: Abstract
This document contains the agreed terminology to be used in the development of the next generation of IEEE 802.11p technology in IEEE 802.11bd Task Group [1]
It also reiterates the PAR requirements related to the agreed terminology [2]

## Slide 3: Terminology
  Interoperability – IEEE 802.11p devices to be able to decode at least one mode of transmission of IEEE 802.11bd devices, and IEEE 802.11bd devices to be able to decode IEEE 802.11p transmissions
  Co-existence – IEEE 802.11p devices to be able to detect IEEE 802.11bd transmissions (and hence defer from transmissions during IEEE 802.11bd transmissions causing collisions) and vice versa
  Backward compatibility – Ability of IEEE 802.11bd devices to operate in a mode in which they can interoperate with IEEE 802.11p devices
  Fairness – Ability of IEEE 802.11p devices to have the same opportunities as IEEE 802.11bd devices to access the channel

## Slide 4: IEEE 802.11bd Device Modes
TX: New PHY
11p device is aware of messages but can’t decode (coexistence)
TX: 11p messages
11p device decodes messages
(interoperate)
Mode transition
(backward compatibility)
RX: Both 11bd and 11p messages

## Slide 5: TGbd Requirement
IEEE 802.11bd amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices. [2]
In order to support the above requirement
  An IEEE 802.11bd device transmitting an IEEE 802.11p-conformant frame shall include an indication that it is an IEEE 802.11bd-capable device.
  IEEE 802.11bd capability indication enables future proof interoperability among different generations of DSRC technology.

## Slide 6: References
[1] IEEE 802.11-18/1323r2 NGV SG Use Cases
[2] IEEE 802.11-18/0861r9 IEEE 802.11 NGV SG Proposed PAR