## Slide 1: A Draft IEEE 802.11bc Use Case Document
Date: 2019-02-08
Authors:

## Slide 2
Abstract
This document contains the proposed use cases descriptions for the IEEE 802.11bc TG.

## Slide 3: Use Case 1: Stadium Video Distribution
Stakeholders
  Stadium system operators
  Stadium audience, coaches and referees
  Broadcasters, e.g., Live TV
  Manufactures of semiconductor, networking and mobile devices
Topology/Architecture
Expected Benefits:
  Ability to broadcast simultaneous information to a large number of users
  Reuse existing technology while reducing cost and implementation complexity
Service scene
  An eBCS AP provides eBCS for videos to a large number of densely located STAs, which may be mobile devices.
  An eBCS AP provides multiple eBCSs for multiple video streams, e.g.:
    live video feed/Video Highlights Replay
    Videos from different angles of the game (e.g., in soccer)
    Videos of different sport activities that take place in parallel (e.g., athletics)
Required function
Providing enhanced Broadcast Services (eBCS) for videos to a large number of densely located STAs. These STAs may be associated, or unassociated with the AP or may be low-cost STAs that do not transmit.
Contents
Server
AP
STA
STA
STA
STA
Network
STA

## Slide 4: Use Case 2: Low Power Sensor UL Broadcast
Internet
Server
STA 1
STA 2
Stakeholders
  Users of IoT devices
  IoT System Operators
  Manufactures of semiconductor, APs, networking and mobile devices
Topology/Architecture
Expected Benefits:
  Ability to broadcast information destined to the end server
  Ability to reduce cost and implementation complexity
  Ability to enable low power sensor operations
Service scene
  An eBCS AP provides forwarding service for eBCS non-AP STAs that are not associated with itself to end-servers
  eBCS STAs have pre-configured keys to enable secure message delivery
  eBCS non-AP STAs are expected to generate low rate data: e.g., 100bps short burst once a day
  eBCS APs may enforce service policy
Required function
Pre-configured IoT devices automatically connect to the end server through eBCS APs with zero setup action required
Low power IoT devices in mobility report to their servers through eBCS APs without scanning and association
Internet
Server
AP 1
STA 1
@ t=T1
AP 2
STA 1
@ t=T2
Zero Setup Sensor
Sensor on the move
AP 1
AP 2

## Slide 5: Use Case 3: Intelligent Transportation Broadcast
Topology/Architecture
Stakeholders
  Users of railway crossing and intelligent transportation system (ITS)
  Railway operators, automobile manufacturers
  Government agencies and police
  Manufactures of semiconductor, automobiles, networking and mobile devices
Expected Benefits:
  Ability to broadcast safety related information and local traveler information without delay and association to large number of STAs
  Ability to reduce cost and implementation complexity
Service scene
  For advanced railroad crossing:
    RSE provides eBCS service of arriving train info and railroad crossing warning
    PID and OBE provide eBCS service for personal and vehicle location info
  For traveler information broadcast:
    RSE provides eBCS service of local traveler info, e.g.,
Required function
Connected Vehicle Roadside Equipment (RSE), Connected Vehicle (OBE) and Personal Informational Device (PID) provide eBCS service for safety related information for railway crossing
RSE provides eBCS service for local traveler information
Adv. Railroad Crossing
Traveler Info Broadcast
Connected Vehicle
Roadside Equipment
Personal Info Device
Connected
Vehicle
Connected Vehicle
Roadside Equipment
Personal Info Device
Connected
Vehicle

## Slide 6: Use Case 4: Broadcast Services for Event Production
Stakeholders
  Event (e.g., music festival, Comic-Con) system operators
  Event directors, producers and staff
  Event attendees
  Manufactures of semiconductor, networking and mobile devices
Topology/Architecture
Expected Benefits:
  Ability to broadcast simultaneous information suitable for different groups of customer STAS, of which some group may contain a large number of users
  Reducing cost and implementation complexity for event producers and system operators as well as safety officials
Service scene
  At a large event, e.g., music festival and Comic-Con, eBCS services may be provided concurrently for multiple data streams suitable for different groups of customer STAs:
    Live video feeds for multiple stages for event attendees, directors, dressing rooms, safety advisors
    Training videos for event staffs
    Introduction videos for event attendees waiting in line
Required function
Providing enhanced Broadcast Services (eBCS) for multiple data streams suitable for different customer STAs. The number of STAs may be large and these STAs may be static or mobile.
Server
AP
STA
STA
STA
STA
Network
STA
Cameras
Production Talkback
Video Encoder
Voice Encoder

## Slide 7: Use Case 5: Multi-lingual and Emergency Broadcast
Stakeholders
  Venue (e.g., museum, conference) system operators
  Emergency Management Agencies/local governments
  general public
  Venue users (e.g., visitors or attendees)
  Manufactures of semiconductor, networking and mobile devices
Topology/Architecture
Expected Benefits:
  Ability to broadcast simultaneous information to a large number of users
  Reducing cost and implementation complexity for venue and emergency system operators
Service scene
  An eBCS AP provides eBCS for multiple sources of information, e.g., emergency information, venue information, translation in a conference, to a large number of densely located STAs, which may be static or mobile devices.
  An eBCS AP provides multiple eBCSs for the same information in different languages
Required function
Providing enhanced Broadcast Services (eBCS) for emergency and/or Multi-lingual service to a large number of densely located STAs. These STAs may be associated, or unassociated with the AP or may be low-cost STAs that do not transmit. These STAs may be static or mobile.
Contents
Server
AP
STA
STA
STA
STA
Network
STA

## Slide 8
References
[1] IEEE 11-19/0182r0, Template for TGbc Use Case Scenario slides, Jan. 2019
[2] IEEE 802.11-18/383r0, BCS Use Cases, Mar. 2018
[3] IEEE 802.11-18/0532r0, Low Power Sensor Broadcast Use Cases, Mar. 2018
[4] IEEE 802.11-18/1592r0, Possible Enhancement for Broadcast Services over WLAN, Sept. 2018
[5] IEEE 802.11-18/0561r0, Some Use Cases for Broadcast Services over WLAN, Mar. 2018
[6] IEEE 802.11-18/0771r0, Potential ITS Use Cases for BCS, Apr. 2018
[7] IEEE 802.11-18/1437r1, Broadcast Use Case from Event Producers, Sept. 2018