## Slide 1: IEEE 802.11bc Use Case Document
Date: 2019-06-11
Authors:

## Slide 2
Abstract
This document contains the use case descriptions for the IEEE 802.11bc TG.

## Slide 3: Use Case 1: Stadium Video Distribution
Stakeholders
  Stadium system operators
  Stadium audience, coaches and referees
  Broadcasters, e.g., Live TV
  Manufacturers of semiconductor, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast simultaneous information to a large number of users
  Reuse existing technology while reducing cost and implementation complexity
Service scene
  An eBCS AP provides eBCS for videos to a large number of densely located STAs, which may be mobile devices.
  An eBCS AP provides multiple eBCSs for multiple video streams, e.g.:
    live video feed/Video Highlights Replay
    Videos from different angles of the game (e.g., in soccer)
    Videos of different sport activities that take place in parallel (e.g., athletics)
Required function
Providing enhanced Broadcast Services (eBCS) for videos to a large number of densely located STAs. These STAs may be associated, or unassociated with the AP or may be STAs that do not transmit.
Contents
Server
AP
STA
STA
STA
STA
Network
STA

## Slide 4: Use Case 2: Low Power Sensor UL Broadcast
Internet
Server
STA 1
STA 2
Stakeholders
  Users of IoT devices
  IoT System Operators
  Manufacturers of semiconductor, APs, IoT devices, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast information destined to the end server
  Ability to reduce cost and implementation complexity
  Ability to enable low power sensor STA operations
Service scene
  An eBCS AP provides forwarding service for eBCS non-AP STAs that are not associated with itself to end-servers
  eBCS STAs have pre-configured keys to enable secure message delivery
  eBCS non-AP STAs are expected to generate low rate data: e.g., 100bps short burst once a day
  eBCS APs may enforce service policy
Required function
Pre-configured IoT devices automatically connect to the end server through eBCS APs with zero setup action required
Low power IoT devices in mobility report to their servers through eBCS APs without scanning and association
Internet
Server
AP 1
STA 1
@ t=T1
AP 2
STA 1
@ t=T2
Zero Setup Sensor
Sensor on the move
AP 1
AP 2

## Slide 5: Use Case 3: Intelligent Transportation Broadcast
Topology/Architecture
Stakeholders
  Users of railway crossing and intelligent transportation system (ITS)
  Railway and other transportation related operators [8]
  Government agencies and police
  Manufacturers of semiconductor, automobiles, networking and mobile devices
Expected benefits:
  Ability to broadcast transportation related information and local traveler information without delay and association to large number of STAs
  Ability to reduce cost and implementation complexity
Service scene
  For advanced railroad crossing:
    RSE provides eBCS service of arriving train info and railroad crossing warning
    PID and OBE provide eBCS service for personal and vehicle location info
  For traveler information broadcast:
    RSE provides eBCS service for local traveler info
  Intelligent Transportation broadcast streams are expected to not be time critical, e.g., a new packet is expected once a few seconds per stream
Required function
Connected Vehicle Roadside Equipment (RSE), Connected Vehicle (OBE) and Personal Informational Device (PID) provide eBCS service for transportation related information for railway crossing
RSE provides eBCS service for local traveler information
Adv. Railroad Crossing
Traveler Info Broadcast
Connected Vehicle
Roadside Equipment
Personal Info Device
Connected
Vehicle
Connected Vehicle
Roadside Equipment
Personal Info Device
Connected
Vehicle

## Slide 6: Use Case 4: Broadcast Services for Event Production
Stakeholders
  Event (e.g., music festival, Comic-Con) system operators
  Event directors, producers and staff
  Event attendees
  Manufacturers of semiconductor, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast simultaneous information suitable for different groups of customer STAs, of which some group may contain a large number of users
  Reducing cost and implementation complexity for event producers and system operators as well as safety officials
Service scene
  At large events, e.g., music festival and Comic-Con, eBCS services may be provided concurrently for multiple data streams suitable for different groups of customer STAs:
    Live audio/video feeds for multiple stages for event attendees, directors, dressing rooms, safety advisors
    Training videos for event staffs
    Introduction videos for event attendees waiting in line
Required function
Providing enhanced Broadcast Services (eBCS) for multiple data streams suitable for different customer STAs. The number of STAs may be large and these STAs may be static or mobile.
Server
AP
STA
STA
STA
STA
Network
STA
Cameras
Production Talkback
Video Encoder
Audio Encoder

## Slide 7: Use Case 5: Multi-lingual and Emergency Broadcast
Stakeholders
  Venue (e.g., museum, conference) system operators
  Emergency Management Agencies/local governments
  General public
  Venue users (e.g., visitors or attendees)
  Manufacturers of semiconductor, networking and mobile devices
Topology/Architecture
Expected benefits:
  Ability to broadcast simultaneous information to a large number of users
  Reducing cost and implementation complexity for venue and emergency system operators
Service scene
  An eBCS AP provides eBCS for multiple sources of information, e.g., emergency information, venue information, translation in a conference, to a large number of densely located STAs, which may be static or mobile devices.
  An eBCS AP provides multiple eBCSs for the same information in different languages
Required function
Providing enhanced Broadcast Services (eBCS) for emergency and/or Multi-lingual service to a large number of densely located STAs. These STAs may be associated, or unassociated with the AP or may be STAs that do not transmit. These STAs may be static or mobile.
Contents
Server
AP
STA
STA
STA
STA
Network
STA

## Slide 8: Use Case 6: VR eSports Video Distribution
Stakes holders
  Game makers/providers/players
  Game set makers
Topology/Architecture
Expected benefits
eBCS can distribute video to thousands of audience members with less bandwidth consumption than unicast.
Service scene
At the location of VR eSports games, such as arena, eBCS distributes the video that is the view of the player to the audiences.
Required function
No authentication / association of STAs with AP
Required authentication of sender
Required authenticity of AP
Video distribution latency should be less than 20ms.
Distribute video to a large number of audiences
Server
AP
Player
Audiences

## Slide 9: Use Case 7: Multi-Channel Data Distribution
Stakes holders
Museum/Concert Hall/Convention Hall/Sightseeing Venue/etc.
Topology/Architecture
Expected benefits
eBCS can be used for multi-lingual services to distribute the same information to people from multiple countries.
Service scene
An AP broadcasts the same information in different languages each in a dedicated channel.
A user can choose one of the channels
Required function
No authentication / association of STAs with AP
Required authentication of sender
Required authenticity of AP
Distribution of different data
People can choose their preferred channel.
Server
AP
Audience
Ch#1: Japanese
Ch#2: English
Ch#3: Chinese
Ch#4: Korean
…

## Slide 10: Use Case 8: Lecture room slide distribution
Stakes holders
School / University /Conference room etc.
Teacher/ Professor / Speaker
Topology/Architecture
Expected benefits
Easy distribution of slides to the audience simultaneously.
Service scene
Simultaneous distribution of slides on the screen to audience PC, Tablet, etc.
The audience do no need to download visual aids and change pages
Synchronized slide distribution to all students.
Required function
No authentication / association of STAs with AP
Required authentication of sender
Required authenticity of AP
low latency
Capacity 1000 STAs
Restrict undesired changes of contents by receiver side
Professor / Teacher/ Speaker
Student etc.
Screen
Projector with AP

## Slide 11: Use Case 9: Regional based broadcast TV service
Stakes holders
Local TV services company
Residential people and home
Topology/Architecture
Expected benefits
Low CAPEX for TV companies
Anytime, anywhere receivable services for residential people
Easy installation to disaster shelter, etc.
Service scene
Local news , TV content can be distributed to consumer BYOD devices (not TV receiver) by small local TV company.
In case of disaster, evacuation information will be distributed without any complex customer operation.
Required function
No authentication / association of STAs with AP
Required authentication of sender
Required authenticity of AP
Middle range (up to 1km) services
Local TV services
Disaster shelter
Home
Evacuation
Information
Disaster side
Reginal
services
Inhouse
services
Wi-Fi

## Slide 12: Use Case 10: AP tagged UL forwarding
Stakeholders
  IoT Users, IoT operators, tracking services, etc
  Manufactures of semiconductor, APs, networking and mobile devices
Expected benefits:
  Ability to broadcast information destined to the end server
  Ability to reduce cost and implementation complexity
  Ability to enable low power STA operations
Service scene
  An eBCS AP provides forwarding service to an end-servers for eBCS non-AP STAs that may not be associated with the AP
  An eBCS AP appends on additional information before forwarding the packet to the addressed server
Required function
Pre-configured low-cost low power tracker device automatically connects to an end server through eBCS APs in the neighborhood with zero setup action
Tracker device periodically reports to its server through eBCS APs without scanning and association
eBCS AP appends metadata (such as IP, date/time, location, RSSI etc) to the packets before forwarding to the destination server
Meta-data from an eBCS AP will be protected
Topology/Architecture

## Slide 13
References
[1] IEEE 11-19/0182r0, Template for TGbc Use Case Scenario slides, Jan. 2019
[2] IEEE 802.11-18/383r0, BCS Use Cases, Mar. 2018
[3] IEEE 802.11-18/0532r0, Low Power Sensor Broadcast Use Cases, Mar. 2018
[4] IEEE 802.11-18/1592r0, Possible Enhancement for Broadcast Services over WLAN, Sept. 2018
[5] IEEE 802.11-18/0561r0, Some Use Cases for Broadcast Services over WLAN, Mar. 2018
[6] IEEE 802.11-18/0771r0, Potential ITS Use Cases for BCS, Apr. 2018
[7] IEEE 802.11-18/1437r1, Broadcast Use Case from Event Producers, Sept. 2018
[8] The Architecture Reference for Cooperative and Intelligent Transportation (ARC-IT) WWW.ARC-IT.ORG

## Slide 14
References
[9] IEEE 11-19/472r2, TGbc Additional Use Case Scenario, May 2019
[10] IEEE 11-19/0894r1, Additional Use Case, May 2019