## Slide 1: NGV Backward Interoperability: Follow-up
Date: 2019-03-11
Authors:

## Slide 2: Introduction
Backward interop design above PHY is proposed in January meeting [1].
More analysis and simulations are provided to validate the eligibility of the proposal.

## Slide 3: Backward Interop Proposal: Recap
11p STAs and NGV STAs need to coexist and interop. in 11p operating channels (e.g. Ch172/178), based on PAR.
Propose backward interop above the PHY level [1]:
  Once a legacy 11p STA is detected by NGV STA (detection level same as regular Rx sensitivity level), 11p PPDUs shall be used by the NGV STA for OCB broadcast frame transmission.
  Otherwise, the NGV STA may choose to use NGV PPDU.
Termed as “NGV-interop rule” in the following slides.

## Slide 4: Backward Interop Proposal: Recap (cont.)
This is a cleaner solution than the PHY level backward interop designs.
  No additional PHY mode introduced, besides legacy 11p PHY & new NGV PHY.
  Avoid all legacy device PHY decoding compatibility issues (e.g. L-Length mismatches)
  No MAC level throughput degradation (e.g. by adding additional parity or repetitions)
To avoid 11p PPDU format propagation, when transmitting an 11p PPDU, NGV STA should be able to indicate whether the 11p PPDU is from a NGV device or not [2, 3].
We will evaluate the impact of the “NGV-interop rule” to 11p STAs.

## Slide 5: Impact to 11p STA: Case 1
At the early stage of NGV deployment, the number of NGV STAs is small compared to 11p vehicles .
When an NGV STA joins DSRC broadcast channel with mostly 11p STAs,
  The NGV STA first listens Twait11p to the ongoing mixed 11p/NGV traffic according to the 11p-protection period (reasonably to choose Twait11p > broadcast period 100ms).
P
N
P
P
P
P
P
P
P
P
P

## Slide 6: Impact to 11p STA : Case 1 (cont.)
Up on detecting one 11p PPDU within the protection period, the NGV STA will switch to 11p PPDU.
An NGV STA will behave the same as an 11p STA.
No impact to 11p vehicles compared to pure 11p environment.
P
N
P
P
P
P
P
P
P
P
P

## Slide 7: Impact to 11p STA: Case 2
At later stage of NGV deployment, there are less 11p vehicles on the road compared to NGV vehicles.
When an 11p STA joins DSRC broadcast channel with mostly NGV STAs,
  The 11p STA will listen to the ongoing mixed NGV/11p traffic, and backoff according to CSMA rules (EIFS or AIFS).
P
N
N
N
N
N
N
N
N
N
N

## Slide 8: Impact to 11p STA: Case 2 (cont.)
  Upon detecting legacy preamble of either NGV or 11p PPDU, backoff starts based on the detected LENGTH in LSIG field.
After gaining channel access and sending out one 11p PPDU, all neighboring NGV STAs within detection range will switch to 11p PPDU.
Negligible impact compared to pure 11p environment.
P
N
N
N
N
N
N
N
N
N
N

## Slide 9: Impact to 11p STA: Case 3
At any intermediate stage of NGV deployment, it will be a mix of case 1 and case 2.
By enforcing the NGV-interop rule [1], the impact to 11p operation will be negligible after gaining channel access.
P
N
N
N
N
N
N
N
N
N
P
P
P
N
N
N
P
P
N
P
N

## Slide 10: Discussions
11p devices may be affected for random channel access,
  A): when it just starts its 11p radio or merge into the traffic, or
  B): an NGV STA moves to its detection range within BSM period
Scenario A) happens very infrequent.
Scenario B) is also very unlikely
  NGV STA likely to have better sensitivity than 11p STA, NGV STA will switch to 11p PPDU before 11p STA hears one NGV PPDU.
  For extreme 500km/h, the relative movement of two vehicles is ~14m. This roughly translate to 1dB sensitivity difference.
The impact of NGV PPDU to 11p STA will be negligible when NGV-Interop-Rule is applied.

## Slide 11: Simulations: Setup
Simplified system level simulations
  Simulate channel contention behavior (CSMA) of one 11p STA
  Background BSM traffic from N vehicles with periodic BSM message at 10 messages/second, message size: 320Bytes
  Monte Carlo simulations with
    random location of N vehicles within [1000mX24m].
    Three traffic scenarios: N = [100 300 600] => [158 45 15]m/h average speed, according to “Two-second rule” for v2v distance.
    random BSM message time within each period (100ms) for N vehicles.
N
P
P
P
N
N
N
P
P
N
P
P
1000m
24m
N
N
N
N
P

## Slide 12: Evaluation Metrics
Evaluate the effectiveness of the “NGV-interop rule” and the impact of NGV STA percentage to the 11p STA.
Two metrics:
  TAccess: mean contention time for an 11p STA to gain channel access to send its BSM message under mixed 11p/NGV PPDU traffic.
    Covers both scenario A) and B) in slide 10.
  NBSM: mean number of BSM messages received by 11p STA in NGV PPDU format during channel contention within each period, 100ms
    Evaluate the potential missed BSM messages for 11p STA.

## Slide 13: Mean Channel Access Time
Impact to NGV STA percentage to the channel access time is negligible.
The “NGV-Interop-Rule” also has minor effect.
  NGV PPDU duration is smaller than 11p PPDU duration.

## Slide 14: Missed BSM Messages
With the “NGV-Interop-Rule” turned on, the average number of missed BSM message in NGV PPDU for an 11p STA is almost ZERO!
The heavier the traffic, the more effect is observed.

## Slide 15: Summary
The proposed NGV-Interop-Rule [1] is analyzed in more details.
System level simulation is provided to demonstrate that the effectiveness of NGV-Interop-Rule [1].
Results show that the impact to 11p STAs in the mixed NGV-11p environment is negligible.

## Slide 16: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “An NGV STA shall use 11p PPDUs for broadcast frame transmission with a TBD interval, once a legacy 11p transmission is detected.
  The 11p transmission detection sensitivity threshold is -85dBm (or make TBD for now)”

## Slide 17: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “An NGV STA shall indicate the NGV capability in MAC level, when transmitting an 11p PPDU”

## Slide 18: Appendix

## Slide 19: Detailed Simulation Settings
  Random vehicle locations within [1000m 24m]
  Pathloss models: WINNER+ B1 LOS [4]
  Tx Power = 20dBm
  CCA detection sensitivity: -85dBm
  Energy detection threshold: -65dBm
  Periodic BSM traffic at 10 messages/second per STA
  BSM message size: 320Bytes
  Access Category: 0
P
N
N
N
N
P
P
P
N
P
N
P

## Slide 20: Mean Channel Access Time

## Slide 21: Missed BSM Messages

## Slide 22: Effective NGV PPDU Percentage

## Slide 23: Reference
[1] Liwen Chu and etc., “NGV Backward-interoperability Discussions”, 11-19/0018r0.
[2] Liwen Chu and etc., “NGV Indication in Legacy PPDU”, 11-19/0086r0.
[3] Michael Fischer and etc., “Indicating NGV Capabilities in MAC Header”, 11-19/0083r0.
[4] “WINNER II Channel Models”, IST-4-027756 WINNER II, D1.1.2 V1.2