## Slide 1: LDPC Investigation for 11bd
Date: 2019-03-14
Authors:

## Slide 2: Introduction
In January meeting, LDPC was suggested as a promising PHY technology for 11bd [1, 2].
Some preliminary studies were provided together with some other PHY features.
In this contribution, we will further investigate the benefits of LDPC over BCC in 11bd.

## Slide 3: LDPC
LDPC has been adopted since 802.11n, and become mature in most WiFi products.
It is a low-hanging fruit for 802.11bd to achieve better sensitivity by adopting LDPC codes.
  The same LDPC code design as 802.11n/ac can be used.
  The coding type may be signaled in the NGV SIG field.
Prominent LDPC coding gain over BCC is demonstrated for AWGN and various 11n channel Models in [3].
We simulate LDPC vs BCC under C2C channels.
  To make apple-to-apple comparison, genie data aided channel update is implemented in both cases, so to have the same Doppler effect, and
  the same channel update latency and period are chosen for both codes.
  Pure coding gain can be evaluated in term of PER

## Slide 4: Simulations
Settings
  1x1-1SS, 10MHz DSRC channel
  Car2Car Doppler channel model [4]
  Number of data bits: 300 Bytes
  Genie-aided carrier sensing and timing
  NGV + LDPC vs 11p BCC
    NGV PPDU: 11ac 20MHz DC2, 11ac LDPC coding
      NGV PPDU has ~0.35dB worse per-tone SNR.
    Genie-aided Doppler Channel Update
      Shortest theoretical channel update delay and period for BCC
      Tracking latency of 2 symbols
      Tracking period of 1 symbol

## Slide 5: Rural LOS
11ac-LDPC shows SNR gain 1.5~4dB among all MCSs

## Slide 6: Urban Approaching LOS
11ac-LDPC shows SNR gain 1~4dB among all MCSs

## Slide 7: Urban Crossing NLOS
11ac-LDPC shows SNR gain 1~4dB among all MCSs

## Slide 8: Highway LOS
11ac-LDPC shows SNR gain 1.5~4dB among all MCSs

## Slide 9: Highway NLOS
11ac-LDPC shows SNR gain 1~4dB among all MCSs

## Slide 10: Summary
LDPC coding is revisited and evaluated under C2C channel models.
Simulations show prominent SNR gain, 1~4dB, by changing the coding from BCC to LDPC.
LDPC codes are mature in 802.11 standards and products.
Propose to add LDPC coding to 11bd standards.

## Slide 11: Reference
[1] Rui Cao and etc., “Potential PHY Designs for NGV”, IEEE 802.11-19/0016r0.
[2] Dongguk Lim and etc., “Consideration on Features for 11bd”, 802.11-19/0009r0.
[3] Aleksandar Purkovic, and etc., “LDPC vs Convolutional Codes for 802.11n applications performance comparison”, 11-04/0071r01.
[4] Prashant Sharma and etc. “Simulation of NGV Channel Models”, 11-19/0017r4

## Slide 12: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “11bd amendment shall support LDPC”
Y: 36
N: 0
A: 9

## Slide 13: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “11bd amendment shall support LDPC code, with the same coding method as defined in IEEE 802.11-2012 section 19.3.11.7 (LDPC Codes)”
Y: 30
N: 2
A: 11

## Slide 14: Motion
Move to add the following text into Section 3 of SFD:
  “802.11bd amendment shall support LDPC”
Move:
Second:
Result:

## Slide 15: Appendix: AWGN
NGV receiver uses channel smoothing across LLTF and VHT-LTF
LDPC shows 2~3dB SNR gain over BCC for 11ac OFDM format