## Slide 1: NGV Indication within Legacy 11p Unicast PPDU
Date: 2019-05-14
Authors:

## Slide 2: Recap: Identification of Source Device Type in 11p Broadcast PPDU[1]
Duration based indication in 11p broadcast PPDU was proposed:
  In Duration field of MAC header, a specific addition, e.g. ½ slot time, slot time, or SIFS, to the actual duration value is used to identify that the frame in 11p PPDU is from a NGV device.
Broadcast frame in 11p PPDU
11p STA1
Broadcast frame in 11p PPDU
NVG STA2
Duration field with value 0
Duration field with value ½ slot time
A 11p neighbor exists
Broadcast frame in NGV PPDU
NVG STA3
Only NGV neighbor exists
Duration
Only NGV neighbor exists
11p STA1
NVG STA2
NVG STA3
Duration field with value 0
Duration field with value ½ slot time
A 11p neighbor exists
Only NGV neighbor exists
½ slot
This method can be extended to unicast 11p PPDU.
  In a channel that both unicast PPDUs and broadcast PPDUs are allowed, identifying the STA’s device type can increase the chance to transmit the broadcast NGV PPDU.
11p STA1
NVG STA2
NVG STA3

## Slide 3: PPDU Format for Unicast Frame Exchange
Case-1: When either TXOP initiator or TXOP responder is 11p STA, the unicast frame (QoS Data frame, Management frame and their solicited frame) will be carried in 11p PPDU.
Case-2: NGV PPDU can be used for frame exchange between two NGV STAs.
  Before the unicast frame exchange, we assume that two STAs can exchange some information that includes STA’s device type through management frame or up layer. Otherwise duration based method can be used.
QoS Data frame
11p STA1
NVG STA2
11p STA1
NVG STA2
Ack
11p PPDU
11p PPDU
QoS Data frame
Ack
11p PPDU
11p PPDU
The neighbor needs to identify the Ack transmitter’s device type.
The neighbor needs to identify the data transmitter’s device type.

## Slide 4: Proposal Highlight
There three cases that both soliciting frame and responding frame are carried in 11p PPDUs:
  Only TXOP initiator is NGV STA.
  Only TXOP responder is NGV STA.
  Both TXOP initiator and TXOP responder are NGV STAs
The remaining TXOP duration after the frame exchange should have different values to differentiate these three cases.

## Slide 5: Remaining Duration for NGV Indication
Different remaining duration values at the end of the Ack for TXOP initiator and TXOP responder are used to identify the NGV device.
  In the following example, TXOP remaining time (at the end of Ack) of ½ slot and TXOP remaining time of 1 slot are used for initiator’s NGV indication and responder’s NGV indication respectively.
QoS Data frame
11p STA1
NVG STA2
11p STA1
NVG STA2
Ack
11p PPDU
11p PPDU
QoS Data frame
Ack
11p PPDU
11p PPDU
The value in the Duration field transmitted by initiator is SIFS + Ack’s TX time + ½ Slot time.
The value in the Duration field transmitted by responder is set to 1 slot time purposely.
NVG STA3
The value in the Duration field is ½ Slot time.
The value in the Duration field is SIFS + Ack’s TX time
STA3 figures out the TXOP remaining time is ½ Slot time. So STA2 is NGV STA.
STA3 figures out the TXOP remaining time is 1 Slot time. So STA2 is NGV STA.
NVG STA4
STA4 figures out the TXOP remaining time is ½ Slot time. So STA1 isn’t NGV STA.
11p STA1
NGV STA2
NGV STA3
NGV STA4
STA4 figures out the TXOP remaining time is 0. So STA1 isn’t NGV STA.

## Slide 6: Remaining Duration for NGV Indication (Cont’d)
When unicast 11p PPDU is allowed between two NGV STAs, a remaining duration value at the end of the Ack that is different from the remaining duration value between NGV STA and 11p STA is used to identify the NGV device.
11p STA1
NVG STA2
NGV STA1
NVG STA2
QoS Data frame
Ack
11p PPDU
11p PPDU
The value in the Duration field transmitted by initiator is SIFS + Ack’s TX time + 1.5 Slot time.
NVG STA3
The value in the Duration field is 1.5 Slot time.
STA3 figures out the TXOP remaining time is 1.5 Slot time. So STA2 is NGV STA.
NGV STA1
NGV STA2
NGV STA3
NGV STA4
NVG STA4
STA4 figures out the TXOP remaining time is 1.5Slot time. So STA1 isn’t NGV STA.

## Slide 7: Straw Poll 1
Do you support that the Duration/ID field in a group-addressed frame carry the information of whether the transmitter of the group-addressed frame is NGV device or 11p device?

## Slide 8: Straw Poll 2
Do you support that the Duration/ID field in an unicast frame carry the information of whether the transmitter of the group-addressed frame is NGV device or 11p device?

## Slide 9: Reference
[1]11-19/0086r0