## Slide 1: Performance Analysis of Outer RS Coding Scheme
Date: 2019-03-12
Authors:

## Slide 2: Abstract
Outer Reed Solomon (RS) Code was proposed in [1] and further analyzed in [2].
The following results are based on simulator [2] analyzing the influence of different performance metrics, MCS, and channels:
PER/Throughput vs. Eb/N0 or SNR:
BPSK/QPSK/16-QAM/64-QAM and different coding rates
AWGN, highway LoS and NLoS
Results show that carful selection of performance metric needed to evaluate performance gains of novel schemes.

## Slide 3: Introduction
Outer Reed Solomon (RS) code proposed in [1]:
Fig. 1 – Reed Solomon outer coding (taken from [1])

## Slide 4: Definitions
Signal-to-noise-ratio
Energy-per-bit-to-noise-ratio
with spectral efficency =
number of bits per packet number of data bits per OFDM symbol number of data symbols per OFDM symbol number of complex samples per packet

## Slide 5: Definitions
Average Packet Error Rate
Average Throughput
packet duration +,
Note: Simulations stopped after 100 packet errors or 105 packets
number of bits per packet number of complex samples per packet sampling period

## Slide 6: Spectral Efficency for Different MCS
 | R=1/2, BPSK | R=3/4, BPSK | R=1/2, QPSK | R=3/4, QPSK | R=1/2, 16-QAM | R=3/4, 16-QAM | R=2/3, 64-QAM | R=3/4, 64-QAM
Outer RS coding scheme [dB] | -3.0 | -3.1 | -3.2 | -3.4 | -3.6 | -3.9 | -4.3 | -4.6
802.11p [dB] | -2.5 | -2.7 | -2.8 | -3.0 | -3.2 | -3.5 | -3.9 | -4.1
 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5
 | R=1/2, BPSK | R=3/4, BPSK | R=1/2, QPSK | R=3/4, QPSK | R=1/2, 16-QAM | R=3/4, 16-QAM | R=2/3, 64-QAM | R=3/4, 64-QAM
 | -3.0 | -3.1 | -3.2 | -3.4 | -3.6 | -3.9 | -4.3 | -4.6
 | -2.5 | -2.7 | -2.8 | -3.0 | -3.2 | -3.5 | -3.9 | -4.1
 | 0.5 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.5

## Slide 7: AWGN (1/2)
Comparison of PER in relation to SNR and Eb/N0:
PER vs. Eb/N0 for fair comparison, accounts for additional energy on overhead
Marginal gain for BPSK/QPSK/16-QAM, significant gain only for 64-QAM

## Slide 8: AWGN (2/2)
Comparison of throughput in relation to SNR and Eb/N0:
Throughput vs. Eb/N0 for fair comparison, accounts for additional energy on overhead and channel use
Outer RS coding scheme has lower throughput for all MCS and AWGN

## Slide 9: Highway LoS (1/2)
Comparison of PER in relation to SNR and Eb/N0:
PER vs. Eb/N0 for fair comparison, accounts for additional energy on overhead
Marginal gain for BPSK/QPSK/16-QAM, significant gain only for 64-QAM

## Slide 10: Highway LoS (2/2)
Comparison of throughput in relation to SNR and Eb/N0:
Throughput vs. Eb/N0 for fair comparison, accounts for additional energy on overhead and channel use
Outer RS coding scheme has lower throughput for all MCS and Highway LoS channel

## Slide 11: Highway NLoS (1/2)
Comparison of PER in relation to SNR and Eb/N0:
PER vs. Eb/N0 for fair comparison, accounts for additional energy on overhead
Marginal gain for BPSK/QPSK(R=3/4), possibly significant gains for QPSK(R=1/2),16-QAM, 64-QAM

## Slide 12: Highway NLoS (2/2)
Comparison of throughput in relation to SNR and Eb/N0:
Throughput vs. Eb/N0 for fair comparison, accounts for additional energy on overhead and channel use
Outer RS coding scheme has lower throughput for all MCS and Highway NLoS channel

## Slide 13: Conclusions
PER vs. Eb/N0 and PER vs. SNR:
  PER vs. Eb/N0 for fair comparison: Accounts for additional energy on overhead
  Marginal gains for outer RS coding scheme for BPSK/QPSK/16-QAM
  Significant gain only for 64-QAM
Throughput vs. Eb/N0 and Throughput vs. SNR:
  Throughput vs. Eb/N0 for fair comparison: Accounts for additional energy on overhead and channel use
  Outer RS coding scheme has lower throughput for all MCS and channels (AWGN, H-LoS, H-NLoS)
 Careful selection of metric to evaluate performance gains of novel schemes

## Slide 14: References
[1] O. Haran, “Backward compatible PHY feasibility,” IEEE 802.11-18/1214r0
[2] I. Sarris, "V2X Reed-Solomon Simulation Model," IEEE 802.11-18/1956r1.