## Slide 1
Channel usage in NGV
Date: 2019-03-12
Authors:

## Slide 2: Introduction
As in PAR document[1], the 11bd operation in V2X communication shares the channel with 11p devices, maintaining interoperability
  This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.
When the number of nodes increases, the channel access mechanism cannot ensure the reliability of the communication because of the channel capacity limitation
In this contribution, the channel access performance for the case of periodic BSM message transmission is investigated, as the number of nodes increases.

## Slide 3: Channel usage in DSRC
According to the FCC regulation[3], in the DSRC communication based on IEEE 802.11p, each channel in 5.9 GHz band assigned for V2X communication utilizes 10 MHz bandwidth
  The BSM message is sent in Ch 172, which is dedicated for safety message
In this contribution, it is assumed that 11bd devices also transmit BSM messages using the same channel as 11p devices.
Ch 172
Ch 174
Ch 176
Ch 178
Ch 180
Ch 182
Ch 184
SCH
safety
SCH
safety
CCH
SCH: may used in 20MHz
SCH: may used in 20MHz

## Slide 4: Channel capacity limitation in dense scenario
In case of the large number of cars, BSMs sent by each node may cause congestion in the single 10 MHz channel
  The dense environment includes traffic jam, intersection and tollgate scenarios

## Slide 5: Contention-based MAC access for highly congested channel
When the channel is congested, the contention-based MAC channel access mechanism causes the large collision probability.
The transmission procedure of BSM messages, which is a broadcast message without retransmission, does not guarantee the reliability of the transmission.

## Slide 6: Brief analysis of collision probability in contention-based channel access
In order to investigate how large number of nodes affects the reliability, brief simulation is performed.
Assumptions
  perfect channel
  channel access with legacy DCF parameters
  only BSM messages with 100ms period
Parameter | Values
BSM size (including Header) | 400 Bytes
Number of nodes | 10~200
AIFSN | 2
minCW | 15
MCS | 0/2

## Slide 7: Collision probability of BSM messages in single 10 MHz channel
For 400 Bytes BSM message with MCS=0
  Collision probability of more than 0.1 occurs in case of more than 70 nodes
For 95% reliability, the number of nodes should be less than 60, for idle channel
For 99% reliability, the number of nodes should be less than 40, for idle channel

## Slide 8: Collision probability of BSM messages in single 10 MHz channel
For 400 Bytes BSM message with MCS=2
  Collision probability of more than 0.1 occurs in case of more than 120 nodes
For 95% reliability, the number of nodes should be less than 100, for idle channel
For 99% reliability, the number of nodes should be less than 40, for idle channel

## Slide 9: Observation
Even with only BSM messages in the channel, the contention-based channel access in single channel does not guarantee the reliability required for safety operation
  Reliability cannot be achieved in dense environments, such as heavy traffic (e.g. traffic jam), platooning scenario, and highly populated places like intersection or tollgate.
For other environments, the number of nodes meeting the reliability requirements will be decreased
  When channel switching is applied, the collision probability will be increased, as described in [4]
  When the other messages sent in the channel(warning signal, etc), the collision probability will be increased

## Slide 10: Discussion
As the reliability issue arises in the dense scenario, the modification of the channel access procedure, as well as channel switching mechanism are needed
  Modification shall not affect backward compatibility and interoperability with legacy devices
  Modification shall work under OCB environment
Higher MCS or wider channel bandwidth may lower the collision probability, but the transmission range requirement may not be satisfied.
Distributed multi-user operation may be required to enhance the channel efficiency.
  Based on distributed 802.11ax OFDMA or Distributed PCF

## Slide 11: Conclusion
In this presentation, we investigated the channel access performance used in 11p, especially for BSM messages in 10 MHz channel
Even though a dedicated 10MHz channel is allocated for BSM messages, the reliability of BSM transmissions cannot be achieved as the number of nodes increases.
The conventional channel access method is not enough to achieve the reliability requirements in dense environment
In 802.11bd, efficient distributed multi-user channel access methods are required to accommodate more vehicles.

## Slide 12: Reference
[1] 18/861r9 IEEE 802.11 NGV SG Proposed PAR
[2] 17/651r2 Indication for WUR Duty Cycle
[3] Electronic Code of Federal Regulations
[4] L. Miao, et. al., Performance Evaluation of IEEE 802.11p MAC Protocol in VANET Safety Applications, 2013 IEEE Wireless Communications and Networking Conference (WCNC), Shanghai, 2013, pp. 1663-1668.
[5] J. B. Kenney Dedicated Short-Range Communication (DSRC) Standards in the United States

## Slide 13: backup

## Slide 14: Collision probability for BSM in single 10 MHz channel
When assuming 300 Bytes of BSM in MCS=0
  Over the 10% collision occurs in case of more than 90 nodes
For 95% reliability, the number of nodes should be less than 70, for idle channel
For 99% reliability, the number of nodes should be less than 40, for idle channel
Notes: 현재 spec 상 WID/Group ID/multiple WID 로는 individually addressed BU를 indicate,
Broadcast WUR로만 group addressed BU를 indication할 수 있음(Group ID/multiple WID로는 group address BU indication 부분이 없음)
Broadcast WUR로 group addressed BU indication->단말에서 Wake-up 이후 implicit sleep(관련 PCR 동작)