## Slide 1: Physical Layer Encoding for Interoperable NGV New Modulations
Date: 2019-03-08
Authors:

## Slide 2: Abstract
This submission provides technical details on a new PPDU and waveform encoding design for IEEE 802.11bd, focusing on the PHY aspects.
This new waveform encoding format brings performance improvements, while maintaining full backward compatibility with legacy IEEE 802.11p stations. It allows it fairness for access to the channel among all stations.
The new PPDU can include two different sections. Each section is fully standalone-decodable, with no need to combine the two sections
Different sections may use different modulation and encoding schemes.

## Slide 3: Introduction
This submission provides technical details on a new PPDU and waveform encoding design for IEEE 802.11bd, focusing on the PHY aspects.
This new waveform encoding format brings performance improvements, while maintaining full backward compatibility.
This new PPDU design is fully compatible with the adaptive retransmission technique that was presented to the NGV SG (see 11-18/1186 and 11-18/1577). The combination of these two techniques (new NGC PPDU format + adaptive retransmission technique) is shown towards the end of this document.

## Slide 4: NGV PPDU format: 2 sections Each section contains a decodable message
Legacy IEEE 802.11p PPDU
NGV New modulation symbols
payload
MAC layer
PHY layer
1 copy is encoded as per legacy IEEE 802.11p standard PPDU
1 copy is encoded as per new IEEE IEEE 802.11bd standard proposal

## Slide 5: NGV PPDU format: 2 sections Details on the New Modulation Symbols NGV section (1)
Legacy IEEE 802.11p PPDU
New modulation symbols
Slide 5
Fischer - Filippi - Martinez, NXP
« New DATA » symbols
« New SIG » symbols
« New LTF »
symbols
L-LTF
SIG
L-STF
time
freq
Payload (802.11p)
Possible configurable gap
payload
PHY layer
MAC layer

## Slide 6: NGV PPDU format: 2 sections Details on the New Modulation Symbols NGV section (2)
Legacy IEEE 802.11p PPDU
New modulation symbols
« New DATA » symbols
« New SIG » symbols
New « SIG-like » symbols
Goal: carries the essential parameters for decoding the new data symbols.
Baseline for discussion: L-SIG, with changes
Main difference vs L-SIG: more rate options, MIMO-precoding options, CRC protection.
« New LTF »
symbols
New « LTF-like » symbols
Goal: perform channel Estimation
Baseline for discussion: suggest starting from VHT-LTF
New « Data » symbols
Goal: carries the encoded payload. Should provide quantitively performance improvement vs IEEE 802.11p
Baseline for discussion: suggest starting from VHT-PPDU format
Main difference vs IEEE 802.11p DATA symbols: more subcarriers, LDPC option, STBC options, various spatial streams, small GI option.
Note: some combinations may be excluded (ex: >2 spatial streams)
L-LTF
SIG
Payload (802.11p)
L-STF
time
freq
Possible configurable gap

## Slide 7: NGV PPDU concept: append new modulated symbols to legacy IEEE 802.11p symbols
 Decode the « legacy » IEEE 802.11p section of the message standalone
 Also able to decode the new symbols standalone (no combining with legacy data needed)
Treated as energy that occupies the channel (channel is busy as viewed by 802.11p stations)
« new modulation » section of the message
Exact content discussed on the next slides
« Legacy » IEEE 802.11p section of the message
L-LTF
SIG
DATA (802.11p)
New modulation symbols
How legacy IEEE 802.11p stations treat the new NGV PPDU: they decode the legacy section & sense the NGV section
How NGV stations treat the new NGV PPDU
New NGV PPDU format
L-LTF
SIG
DATA
(high-power) energy
L-LTF
SIG
DATA
New modulation symbols
L-STF
L-STF
L-STF
 Decode the « legacy » IEEE 802.11p section of the message standalone

## Slide 8: New Modulation NGV PPDU section: Possible encoding techniques and formats
IEEE 802.11 Very High Throughput (VHT) (also referred to as 802.11ac), the successor to IEEE 802.11 High Throughput (HT) (also referred to as 802.11n), offers a solid foundation for IEEE 802.11bd.
Compared to IEEE 802.11p, some advanced features are included in VHT (certain are optional):
FEC coding: convolutional or LPDC with coding rates of 1/2, 2/3, 3/4, or 5/6
More data subcarriers (Data subcarriers / Pilots ratio: 52 / 4)
Modulation up to 256QAM
Spatial streams schemes: MIMO (single-user & multiple-users), STBC, Beamforming
These features have been thoroughly tested and successfully used, providing rock-solid toolkit for IEEE802.11bd. We believe it is essential to capitalize on the VHT work as instead of defining new schemes.
The exact list of VHT features (and combinations) is open for discussion. NXP proposal will be described in a subsequent contribution.

## Slide 9: Indicating NGV Capability
It is necessary for NGV-capable stations to indicate their NGV capability to other NGV stations when transmitting legacy IEEE 802.11p messages.
For more details on such capability indication, refer to submission “MAC Service Updates for NGV” IEEE 802.11-19/0276.

## Slide 10: Dynamic Monitoring of Nearby Station Characteristics
NGV stations monitor received PPDUs to determine NumStationsNGV and NumStationsLegacy which are used to calculate TechPercentage. Based on this percentage, the encoding parameters of each section (the legacy IEEE 802.11p section, and the NGV section) are adapted.
For more details on such monitoring and adaptation, see submission “Adaptation-Mechanisms for Interoperable NGV New Modulations” IEEE 802.11-19/0370-r0

## Slide 11: Append new modulated symbols with configurable gap
« new modulation » section of the message
Exact content discussed on the next slides
« Legacy » section of the message
L-LTF
SIG
Payload
New modulation symbols
L-STF
Configurable gap time
The configurable gap can be set zero (direct concatenation) for best efficiency, to a short interval such as SIFS for instance, or to a longer time interval.
The total duration of the legacy + NGV sections, either with a zero time gap or a deterministic time gap, can be set to a similar total duration as the legacy IEEE 802.11p PPDU encoded with QPSK ½ (rate 6 Mb/s).

## Slide 12: Why it is possible to extend the legacy PPDU?
Not different than the case where a receive station gets overlapping messages, due to different geographical situation.
TXA
TXB
RX
1000 meters
100 meters
time
TX A PPDU
TX B PPDU
From receiver RX perspective, processing over time axis:

## Slide 13: Additional comments on NGV waveform
When defining the new modulation symbols for IEEE 802.11bd based on HT or VHT modulations, the accommodation to narrower channels should be the same as was used when going from 802.11a to 802.11p. For 10 MHz channels the data rate is divided by two and the symbol duration is multiplied by two.

## Slide 14: Compatibility with adaptive retransmission technique (1)
The adaptive retransmission technique described in document 11-18/1577r0 can be used along with the new NGV PPDU format described above. This combination is shown on the next slide.

## Slide 15: Compatibility with adaptive retransmission technique (2)
info* : typically, but not limited to, LLR values
Message #2 “new”
- Combined decoding (with “new” info* saved in accumulator)
- Save “new” info* in accumulator
Message #2 “legacy”
- Combined decoding (with “legacy” info* saved in accumulator)
- Save “legacy” info* in accumulator
Message #1 “new”
- Decode as standalone msg
- Save “new” info* in accumulator
Message #1 “legacy”
- Decode as standalone message
- Save “legacy” info* in accumulator
Treated as energy that occupies the channel
Message #2
Decode as standalone message
Treated as energy that occupies the channel
Message #1
Decode as standalone message
How legacy IEEE 802.11p stations treat the PPDU (RX perspective): 2 independent messages
New NGV PPDU format (TX perspective)
Retransmission (example with 1 retransmission) = exact copies of the initial message
Initial message
How NGV stations treat the PPDU (RX perspective): combine messages (example: combining at LLR level)
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
Configurable gap time
L-LTF
SIG
DATA (IEEE 802.11p)
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
L-LTF
SIG
DATA (IEEE 802.11p)
New modulation symbols
L-STF
(high-power) energy
(high-power) energy

## Slide 16: Benefits
This technique for incorporating new modulation symbols improves performance while maintaining interoperability, coexistence, backward compatibility, and fairness with 802.11p equipment
This technique can be used in conjunction with the adaptive retransmission technique described in 11-18/1577r0
This technique does not require changing higher layers of the ITS protocol stack