## Slide 1: Adaptation Mechanisms for Interoperable NGV New Modulations
Date: 2019-03-08
Authors:

## Slide 2: Abstract
This submission provides technical details on a new PPDU and waveform encoding design for IEEE 802.11bd, focusing on adaptation and modulation and encoding schemes.
This new waveform encoding format brings performance improvements, while maintaining full backward compatibility with legacy IEEE 802.11p stations. It allows it fairness for access to the channel among all stations.
The new PPDU can include two different sections. Each section is fully standalone-decodable, with no need to combine the two sections.
Each section uses a different modulation and encoding scheme, ensuring fairness. This facilitates a smooth transition from an environment dominated by legacy 802.11p equipment to one with increasing amounts of 802.11bd equipment.

## Slide 3: Introduction
This submission provides technical details on a new PPDU and waveform design for NGV, focusing on adaptation and modulation and encoding schemes.
Adaptation mechanisms allow a smooth transition from an environment dominated by legacy 802.11p equipment to one with increasing amounts of 802.11bd equipment.
Dynamic monitoring of nearby station characteristics can be used to adjust durations of the legacy and new modulation sections, based on actual channel usage

## Slide 4: NGV PPDU format: 2 sections Each section contains a decodable message
Legacy IEEE 802.11p PPDU
NGV New modulation symbols
payload
MAC layer
PHY layer
1 copy is encoded as per legacy IEEE 802.11p standard PPDU
1 copy is encoded as per new IEEE IEEE 802.11bd standard proposal

## Slide 5: NGV PPDU format: 2 sections Details on the New Modulation Symbols NGV section
Legacy IEEE 802.11p PPDU
New modulation symbols
« New DATA » symbols
« New SIG » symbols
« New LTF »
symbols
L-LTF
SIG
L-STF
time
freq
Payload (802.11p)
Possible configurable gap
payload
PHY layer
MAC layer

## Slide 6: Details on the NGV encoding
For more details on the new NGV section encoding features and format, see submission “Physical Layer Encoding for Interoperable NGV New Modulations” IEEE 802.11-19/0369

## Slide 7: Indicating NGV Capability
It is necessary for NGV-capable stations to indicate their NGV capability to other NGV stations when transmitting legacy IEEE 802.11p messages.
For more details on such capability indication, refer to submission “MAC Service Updates for NGV” IEEE 802.11-19/0276.

## Slide 8: Dynamic Monitoring of Nearby Station Characteristics
NGV stations monitor received PPDUs to determine NumStationsNGV and NumStationsLegacy which are used to calculate TechPercentage:
TechPercentage = NumStationsNGV / (NumStationsNGV+NumStationsLegacy)
  NumStationsNGV is the number of PPDUs received during the preceding one second originating from 802.11p stations.
  NumStationsLegacy is the number of PPDUs received during the preceding one second originating from NGV-capable stations.
    The TechPercentage measurement duration is preliminary, further discussion is needed.
  Received legacy PPDUs that indicate NGV capability are counted in the NumStationsNGV category, not the NumStationsLegacy category.

## Slide 9: Dynamic balance between legacy and new modulation (1)
 | TechPercentage | Legacy 802.11p PPDU encoding (10 MHz channel) | Legacy 802.11p DATA symbols time duration | New modulation encoding time duration | New modulation encoding, example
state 1 | ≤ 60% | QPSK ½ (6 Mb/s) | 100% | 0% | none
state 2 | [60%-70%[ | QPSK ¾ (9 Mb/s) | 67% | 33% | 16QAM ¾
state 3 | [70%-80%[ | 16QAM ½ (12 Mb/s) | 50% | 50% | 16QAM ½
state 4 | [80%-90%[ | 16QAM ¾ (18 Mb/s) | 33% | 67% | QPSK ¾
state 5 | [90%-100%[ | 64QAM 2/3 (24 Mb/s) | 25% | 75% | QPSK 2/3
state 6 | 100 % | none | 0% | 100% | QPSK ½
Example based on “Table 21-30—VHT-MCSs for mandatory 20 MHz, NSS = 1”
NGV stations use the TechPercentage to select an operating state as shown in the table:
The ranges indicated in the TechPercentage column are an initial proposal, further discussion is needed

## Slide 10: Dynamic balance between legacy and new modulation (2)
Legacy 802.11p PPDU (QPSK ½)
time
Legacy 802.11p PPDU (QPSK ¾)
New modulation
time
State #1
State #2
Legacy 802.11p PPDU (16QAM ½)
New modulation
time
State #3
Legacy (16QAM ¾)
New modulation
time
State #4
Legacy (64QAM 2/3)
New modulation
time
State #5
New modulation
t=0
State #6
STF
New LTF
end of PPDU
time
Adjustable durations of the legacy and new modulation sections are based on actual channel usage – NGV stations form NGV PPDUs according to their measured TechPercentage
Total PPDU duration is similar to 802.11p PPDU with same payload, encoded with QPSK ½ (rate 6 Mb/s)

## Slide 11: Benefits
This technique for incorporating new modulation symbols improves performance while maintaining interoperability, coexistence, backward compatibility, and fairness with 802.11p equipment
Dynamic monitoring of nearby station characteristics allows for smooth transitions between different environments
Adjustable durations of the legacy and new modulation sections are based on actual channel usage