## Slide 1: 802.11bc Air Time Consumption Control
Date: 2019-03-08
Authors:

## Slide 2: Proposal for update to the Functional Requirements Document
A mechanism is needed around the start and stop of 802.11bc broadcasting, to assist with reducing air time consumption of broadcast messages.
There are times and places where broadcasting may not be suitable, either due to low use of the system, or overuse of a broadcasting STA that needs to re-allocate it’s resources.
  Mechanism can be used to control broadcasting.
  Mechanism may be used to inform the broadcast transmitter.
  Mechanism may be used to inform the broadcast receiver(s).

## Slide 3: Broadcasting States
The simplest possible state diagram for a Broadcast Service is shown.
Not Broadcasting
Broadcasting
Start
Broadcasting
Stop
Broadcasting

## Slide 4: Start Broadcasting
Broadcasting STA starts broadcasting with no input from receiving STAs
  A communication procedure is not needed.
  AP may send indicator when it first starts broadcasting
Broadcasting STA starts broadcasting based on input from receiving STAs
  Potential receiving STAs may send a request to start the broadcast. This may be a procedure that follows a discovery procedure.
  In the case where a STA has a multiplicity of Broadcast Streams available, the receiving STA may want to indicate which stream it wants to receive.

## Slide 5: Stop broadcasting
Broadcasting STA stops broadcasting with no input from receiving STAs
  A communication procedure is not needed.
  Broadcasting STA can send an indicator when it stops broadcasting to inform receiving STAs.
    Can include the reason it stops broadcasting, permanent or temporary.
Broadcasting STA stops broadcasting based on input from receiving STAs
  Current receiving STAs may send a notification that they will stop receiving broadcast.
  The broadcasting STA may cease broadcasting based on feedback from receiving STAs.
  Broadcasting STA can send an indicator when it stops broadcasting to inform receiving STAs.

## Slide 6: Proposed Amendment to SFD
Update the indicated section of 802.11bc SFD (802.11-19/0151)
3.7 Air time consumption
TGbc R9: 802.11bc amendment shall have a mechanism to facilitate the sharing of airtime between all broadcast services and all non-broadcast services communications.
TGbc Rx: 802.11bc amendment shall have a mechanism to facilitate starting a broadcast service.
TGbc Rx: 802.11bc amendment shall have a mechanism to facilitate stopping a broadcast service.