## Slide 1: Enhanced Multi-band/Multi-channel Operation
Date: 2019-03-11
Authors:

## Slide 2: EHT Multi-band/Multi-channel Operation
As described in the EHT PAR, one of the needs of the EHT program is to provide the high throughput and meet stringent real-time delay requirements of 4k and 8k video, virtual reality or augmented reality, gaming, remote office and cloud computing applications.
In order to meet those PAR requirements, in this presentation, we have analyzed how the EHT multi-band/multi-channel operation can increase the per-session throughput and reduce the per-session latency.

## Slide 3: EHT Multi-band/Multi-channel Operation goals
To reduce latency during multi-band and multi-channel operation, it is necessary to reduce the session switching overhead (e.g., switching timeout, frame exchanges).
  With legacy FST, when switching sessions, the SME of the STA needs to initiate the FST Setup Request and Response frame exchanges as well as the FST Ack Request and Response frame exchanges. Depending on the session switching frequency, the protocol overhead can be quite high.

## Slide 4: EHT Multi-band/Multi-channel Operation goals
To reduce latency during multi-band and multi-channel operation, it is necessary to reduce the session switching overhead (e.g., switching timeout, frame exchanges).
Data [Seq1, TID1]
5GHz
6GHz
Data [Seq2, TID1]
backoff
Block ACK
AP
STA
AP
STA
Switching procedure should be optimized to reduce the overhead.
Data [Seq1, TID2]
Block ACK

## Slide 5: EHT Multi-band/Multi-channel Operation goals
To improve per-session throughput and per-session latency, MSDUs belonging to single session (e.g., TID) should use multiple bands and/or channels simultaneously.
  In a legacy multi-band and multi-channel operation (e.g., FST), sessions of an individual STA can be transferred from a channel to another channel, in the same or different frequency bands.
  But, a MSDUs belonging to single TID can only use single bands and/or channels at any time. There is no per-session throughput improvement.

## Slide 6: EHT Multi-band/Multi-channel Operation goals
To improve per-session throughput and per-session latency, MSDUs belonging to single session (e.g., TID) should use multiple bands and/or channels simultaneously.
Data [Seq1, TID1]
5GHz
6GHz
Data [Seq2, TID1]
Data [Seq3, TID1]
Data [Seq4, TID1]
Block ACK
Block ACK
Data [Seq5, TID1]
…
AP
STA
AP
STA
backoff

## Slide 7: EHT Multi-band/Multi-channel Operation goals
To reduce overhead, Control information (e.g., Control frames, A-Control information) for a channel can be transmitted in a different channel/band.
  Allowing out-of-band exchange of Control information can result in more efficient allocation of resources.

## Slide 8: Conclusion
In this contribution we discuss the limitations of legacy multi-band/multi-channel operation and how new multi-band/multi-channel mechanisms can help to meet the EHT PAR requirements.