## Slide 1: Coordinated Null Steering for EHT
Date: 2019-03-06
Authors:
Name | Affiliation | Address | Phone | Email
Adrian Garcia-Rodriguez | Nokia |  |  | 
David Lopez-Perez |  |  |  | 
Mika Kasslin |  |  |  | 
Olli Alanen |  |  |  | 
Lorenzo Galati Giordano |  |  |  | 
March 2019

## Slide 2: Introduction
Null steering is a wireless technology through which a device performing data transmission/reception can place spatial radiation nulls towards non-served STAs for interference suppression purposes
Illustration of coordinated null steering in downlink
March 2019
Null steering presents a number of benefits
  Leads to a better spatial reuse
  Mitigates inter-cell interference
It also has challenges
  APs need to acquire channel state information (CSI) from non-served STAs
  APs require coordination procedures for controlling null steering transmissions

## Slide 3: Null steering-related proposals in EHT
In previous EHT TIG/SG meetings, null steering has attracted considerable attention, touching on a number of topics
  Motivation for EHT
  Usage of the right terminology and nomenclature in EHT
11-18-1461: Discussions on the PHY features for EHT | Xiaogang Chen (Intel)
11-18-1533: View on EHT Candidate Features | Yusuke Tanaka (Sony)
11-18-1547: Technology Features for 802.11 EHT | Kome Oteri (InterDigital)
11-18-1161: EHT Technology Candidate Discussions | Hongyuan Zhang (Marvell)
11-19-0105: Functional Requirements for EHT Specification Framework | Yonggang Fang (ZTE)
11-18-1926: Terminology for AP Coordination | Sameer Vermani (Qualcomm)
11-18-1509: Discussions on Multi-AP Coordination | Jianhan Liu (MediaTek)
11-18-1576: Considerations on AP Coordination | Bo (Boyce) Yang (Huawei)
March 2019

## Slide 4: Null steering-related proposals in EHT
  MIMO channel sounding issues and enhancements
  Null steering performance analysis
  None of the above contributions identify the scenarios where coordinated null steering could be the most appealing multi-AP coordination alternative
11-19-0071: Coordinated Multi-AP Transmission for EHT | Kome Oteri (InterDigital)
  In this contribution, we describe the challenges of coordinated null steering, as well as the scenarios where it is particularly effective
March 2019
11-18-1191: MU sounding improvements | Sigurd Schelstraete (Quantenna)
11-18-1982: Consideration on multi-AP coordination for EHT | Kiseon Ryu (LG electronics)

## Slide 5: Multi-AP coordination techniques
Coordinated OFDMA
Null steering offers an appealing complexity and performance trade-off
Coordinated null steering
Joint Distributed MIMO
(D-MIMO)
Coordinates time/freq. resource allocation [3, 4]
Reuses time/freq. resources by placing spatial radiation nulls
Reuses time/freq. resources through joint spatial multiplexing [1, 2]
March 2019
Solutions with simplified requirements
Solution with the most demanding synchronization and backhaul requirements

## Slide 6: When is coordinated OFDMA effective?
Coordinated OFDMA for short packets and highly interfered STAs
March 2019
Medium to large AP densities [4]
  Coordinated transmissions enable a more efficient time/freq. resource utilization
  Resource splitting among APs could suffice to provide a satisfactory performance
Also for STAs experiencing high interference [4]
  Interference mitigation is possible through an intelligent resource unit assignment
Illustration of coordinated OFDMA

## Slide 7: When is coordinated null steering effective?
Coordinated null steering for dense scenarios with multi-antenna APs
March 2019
Medium to large AP densities and APs with multiple antennas [4-6]
  Coordinated transmissions enable a more aggressive time/freq. resource utilization
  Spatial reuse could be necessary to provide a satisfactory performance
Also for STAs experiencing high interference and medium to high SNRs [4]
  APs dedicate spatial resources for interference suppression purposes
Illustration of coordinated null steering

## Slide 8: What does coordinated null steering require?
Null steering requirements are aligned with key EHT potential features
March 2019
APs with multiple antennas
No severe spatial channel correlation among STAs
Efficient CSI acquisition procedures
Methods to acquire CSI from STAs served by other APs
Coordination procedures for null steering transmissions
EHT
EHT
EHT
EHT
 in line with other EHT targets
 more specific work

## Slide 9: Spatial domain-related requirements
Typical APs and indoor channels are ideal for null steering
March 2019
APs with multiple antennas
  In agreement with 16 spatial streams feature considered by EHT
No severe spatial channel correlation among STAs
  Suitable for the typical indoor channels with good condition numbers [7]
  STA separability can always be guaranteed through an appropriate scheduling policy
Illustration of AP1 receiving data from STA1 and placing a radiation null towards the non-served STA2
EHT
EHT

## Slide 10: CSI acquisition-related requirements
Decreasing CSI acquisition overhead for an efficient null steering
March 2019
Efficient CSI acquisition procedures
  Explicit CSI acquisition
    Feedback compression to reduce wireless overhead [4]
  Implicit CSI acquisition [8]
    In agreement with 16 spatial streams feature considered by EHT
    Would greatly limit overhead
EHT
Illustration of multi-user implicit CSI feedback process [8]

## Slide 11: Inter-BSS CSI acquisition requirements
Enabling CSI acquisition from non-associated STAs is crucial
March 2019
Methods to acquire CSI from STAs served by other APs
  Communication between non-served STAs and APs is essential
    Multi-AP association might not be the only alternative
  Agreement among collaborative APs is beneficial
    Collaboration frames exchanged on a sporadic basis (long-term agreement)
Illustration of a long term agreement between AP1 and AP2 for performing subsequent coordinated null steering transmissions

## Slide 12: Multi-AP coordination requirements
Coordinated null steering extends 802.11ax spatial reuse framework
March 2019
Coordination procedures for null steering transmissions
b) Explicit coordination building on coordinated OFDMA framework
a) Implicit coordination building on 802.11ax spatial reuse framework
Handshake among APs prior to
a simultaneous data TX/RX
Distribution of null steering-related information prior to data TX/RX

## Slide 13: Conclusions
March 2019
In this contribution, we identified the suitable scenarios and requirements for the implementation of coordinated null steering:
  Similarly to 802.11ax spatial reuse frameworks, coordinated null steering targets dense deployments with multi-antenna APs
  Many of the specifications required to implement coordinated null steering are essential for an efficient implementation of the 16 spatial streams feature considered within EHT. In addition,
    APs need to acquire CSI from non-served STAs
    Coordination procedures for controlling null steering transmissions should be defined

## Slide 14: References
[1] D. Lopez-Perez (Nokia), “Distributed MU-MIMO architecture design considerations,” IEEE 802.11-18/1190r0, Jan. 2019.
[2] Ron Porat (Broadcom), “Joint Processing MU-MIMO,” IEEE 802.11-19/0094, Jan. 2019.
[3] Bo (Boyce) Yang (Huawei), “Considerations on AP Coordination,”, IEEE 802.11-18/1576, Sep. 2018.
[4] Kome Oteri (InterDigital), “Coordinated Multi-AP Transmission for EHT,” IEEE 802.11-19/0071, Jan. 2019.
[5] G. Geraci, A. Garcia-Rodriguez, D. López-Pérez, L. Galati Giordano, P. Baracca, and H. Claussen, “Indoor massive MIMO deployments for uniformly high wireless capacity,” in Proc. IEEE WCNC, Apr. 2018.
[6] A. Garcia-Rodriguez, G. Geraci, D. López-Pérez, Lorenzo Galati Giordano, Ming Ding, and Holger Claussen, “Massive MIMO Unlicensed for High-Performance Indoor Networks,” in IEEE GLOBECOM, Dec. 2017.
[7] Sameer Vermani (Qualcomm), “16 Spatial Stream Support in Next Generation WLAN”, IEEE 802.11-18/0818, May 2018.
[8] Sigurd Schelstraete (Quantenna), “MU sounding improvements”, IEEE 802.11-18/1191, Jul. 2018.
January 2018

## Slide 15: Appendix
January 2018

## Slide 16: Wired- vs. wireless-based coordination
Coordinated null steering does not require a wired-based coordination
March 2019
Null steering admits both wireless and wired implementations
  Wireless-based coordination
    Overhead can be always limited by simplifying the coordination
    Suitable for implementations with explicit or implicit coordination
  Wired-based coordination
    Solution with the smallest wireless overhead
    Suitable for implementations with explicit coordination