## Slide 1: Motion Booklet for IEEE 802.11 TGbd
Date: 2019-03-14
Authors:

## Slide 2: Abstract
Booklet for the TGbd motions related to FRD and SFD.
Motions are consecutively numbered since the formation of the task group.

## Slide 3: March 2019 FRD & SFD Motions
Motion #1 -- #7
Vancouver, BC, Canada

## Slide 4: FRD&SFD Motion #1
Move to update the 11bd FRD according to the changes captured in document 11-19/0511r1.
Moved: Bahar Sadeghi
Seconded: Joseph Levy
Result: Passed unanimous

## Slide 5: FRD&SFD Motion #2
Move to add the following text to section 3 in 11bd SFD.
  “ 11bd PPDU format includes L-STF, L-LTF, and L-SIG fields as shown in Figure 3.x
    L-STF means short training field of 11p.
    L-LTF means long training field of 11p.
    L-SIG means signal field of 11p.”
Moved: Dongguk Lim
Seconded: Hongyuan Zhang
Result: 33Y/0N/9A, passed
L-LTF
L-STF
L-SIG
11bd PPDU
Figure 3.x 11bd PPDU format

## Slide 6: FRD&SFD Motion #3
Move to add the following text to section 3 in 11bd SFD.
  “11bd supports the 10MHz bandwidth PPDUs.
  11bd supports the 20MHz bandwidth PPDUs. ”
Mover: Dongguk Lim
Second: Hongyuan Zhang
Result: Passed unanimous

## Slide 7: FRD&SFD Motion #4
Move to add the following text to section 3 in 11bd SFD.
  “In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below.”
Mover: Dongguk Lim
Second: Hongyuan Zhang
Result: 25Y/0N/19A, passed
10MHz
10MHz
L-LTF
L-STF
L-SIG
L-LTF
L-STF
L-SIG
11bd PPDU

## Slide 8: FRD&SFD Motion #5
Move to add the following text into Section 3 of SFD
  “11bd amendment shall support LDPC”
Mover: Prashant Sharma
Second: Hongyuan Zhang
Result: Passed unanimous

## Slide 9: FRD&SFD Motion #6
Move to add the following text into Section 3 of SFD
  “An 11bd STA shall be capable of the following operations:
    To decode 11p PPDUs with TBD receive sensitivity threshold (TBD value is -85dBm or lower).
    To transmit PPDU format up on request from upper layer, the PPDU format can be either 11p PPDU or 11bd PPDU.”
Mover: Rui Cao
Second: Hongyuan Zhang
Result: 27Y/0N/14A, passed

## Slide 10: FRD&SFD Motion #7
Move to add the following text into Section 3 of SFD
  “An 11bd STA shall indicate the NGV capability in MAC level, when transmitting an 11p PPDU”
Mover: Rui Cao
Second: Hongyuan Zhang
Result: passed unanimous

## Slide 11: MaY 2019 FRD & SFD Motions
Motion #8 -- #16
Atlanta, GA, USA

## Slide 12: FRD&SFD Motion #8
Move to add the following text to section 3 in 11bd SFD
“11bd shall support the same subcarrier spacing in both 10 MHz PPDU and 20MHz PPDU”
Mover: Dongguk Lim
Second: Hongyuan Zhang
Result: Passed unanimously

## Slide 13: FRD&SFD Motion #9
Move to add the following text to section 3 in 11bd SFD
“11bd PPDU includes a NGV-Signal field to indicate the transmission information”
“ The location of NGV-SIG field is TBD”
Mover: Dongguk Lim
Second: Hongyuan Zhang
Result: Passed unanimously

## Slide 14: FRD&SFD Motion #10
Move to add the following text to section 3 in 11bd SFD
“11bd PPDU design shall support Midamble(s) in Data field.
Midamble is composed by long training field, with design TBD.
Midamble periodicity is TBD. “
Mover: Dongguk Lim
Second: Hongyuan Zhang
Result: 8Y/1N/8A Passed

## Slide 15: FRD&SFD Motion #11
Move to add the following text to section 3.1 of the SFD:
“11bd devices shall support 256 QAM. The 256 QAM constellation mapping is the same as that defined in 21.3.10.9 (Constellation mapping)”
Mover: Hongyuan Zhang
Second: Dongguk Lim
Result: 15Y/2N/10A, PASSED

## Slide 16: FRD&SFD Motion #12
Move to add the following text to Section 3.1 of the SFD:
“11bd devices shall support LDPC codes, with the same code structure and coding methods as defined in 19.3.11.7 (LDPC Codes)”
Mover: Hongyuan Zhang
Second: Dongguk Lim
Result: Passed unanimously

## Slide 17: FRD&SFD Motion #13
Move to add the following text to section 3.1 of the SFD:
“10MHz 11bd Data symbol shall use 11ac 20MHz OFDM numerology. “
Mover: Prashant Sharma
Second: Dongguk Lim
Result: Passed unanimously

## Slide 18: FRD&SFD Motion #14
Move to add the following text to section 3 in 11bd SFD
“Operation of 11bd device with 10MHz bandwidth is allowed in a 20MHz channel.”
Mover: Insun Jang
Second: Dongguk Lim
Result: 15Y/6N/9A, Failed
Move to table the motion
Moved: Hiroshi Mano Second: Michael Fischer
Passed unanimously
Move to remove the table of the motion
Moved: James Lepp Second: Michael Fischer
Passed unanimously

## Slide 19: FRD&SFD Motion #15
Move to include the following text to section 3 in 11bd SFD
“11bd only supports single spatial stream PPDU when operating on OCB broadcast mode .”
Mover: Hongyuan Zhang
Second: Dongguk Lim
Result: Passed unanimously

## Slide 20: FRD&SFD Motion #16
Move to include the following text to section 3 in 11bd SFD
“When an 11bd STA transmits an 11p group-addressed or unicast PPDU, the Duration/ID field of a frame in an 11p PPDU indicates that transmitter of the PPDU is an NGV capable STA.”
Mover: Liwen Chu
Second: Michael Fischer
Result: Passed unanimously