## Slide 1: EUHT standards introduction
Date: 2019-04-20
Authors:

## Slide 2: Abstract
This document is a brief introduction to the EUHT standard and includes new features for URLLC and mMTC scenarios.

## Slide 3: Abbreviation
URLLC（Ultra-Reliable and Low Latency Communications）
mMTC (massive Machine Type Communication)
EUHT（Enhanced Ultra High Throughput）

## Slide 4: Topics
Background
Part I:
  EUHT standard outline
  EUHT MAC Layer Overview
  QoS Guaranteed fast and flexible scheduling
  EUHT PHY transmitter
Part II:
  Features for URLLC
  Features for mMTC

## Slide 5: Background
The attached reference document is the translated version of Chinese industry standard, which is announced in 2012. Complete EUHT technical description is provided in the document, which included features of MAC and PHY layers.
It should be noted that there are many new features added in EUHT system since 2012. For example, More bandwidth/SC interval options, More LDPC code options, Higher and Lower MCS, Finer OFDMA, Seamless Handover, Multiple Connection，etc. We are translating the new features and will update the document ASAP.

## Slide 6: EUHT standard outline
Slide 6
EUHT
Standard
Chapter
（5）
System Reference Model
Overview of MAC services
Chapter
（6）
MAC frame format
Chapter
（7）
Chapter
（8）
MAC layer functions
Chapter
（9）
PHY specifications
Chapter
（1~4）
Scope, Normative Reference , Definitions and Abbreviations

## Slide 7: EUHT MAC Layer Overview
Data and Control Plane
A centralized Scheduling MAC mechanism guaranteed the High MAC efficiency in multiple users scenarios
Adaptation layer for QoS classification and the encryption and decryption of upper layer packets
Extremely low overhead MAC layer (6bytes) in MAC MPDU
G-MPDU aggregation for high throughput
Instant-ACK /feedback for low latency

## Slide 8: QoS guaranteed fast and flexible scheduling
QoS guaranteed for different service requirement.(priority QoS scheduling )
Low complexity and fast scheduling
Fast channel state info feedback for fast link adaptation and scheduling
The flexible resources allocation during the Frame. Support a minimum resource to ONE ofdm symbol.
Scheduler
DL packets queues
Channel Est
Scheduler UL
Channel
Est
Queue Info
UL packets queues
CAP
STA
Base on QoS scheduling
Base on QoS scheduling

## Slide 9: EUHT PHY Transmitter
Bit stream spatial mapping with high spatial diversity gain
Get frequency diversity gain
256QAM->1024QAM
UEQM for different stream
Adaptive pilot mode for different STA channel conditions
Pilot for phase tracking
DL/ UL MU MIMO (SDMA)
TDMA and OFDMA resource allocation
DL: S/L-Preamble, DL-SCH
UL: UL-SCH, UL-SRCH, UL-RACH
BCC
LDPC
  —1344bits
  —2688bits
  —5376bits
Code rate of 5/8, 7/8 for optimized link adaptation in mid-high SNR region

## Slide 10: Features for URLLC
More bandwidth/SC interval options
20/40/80MHz 10/20/40 MHz 8/16/32 MHz
78.125KHz 39.0625KHz 31.25KHz
More CP options
1.6/3.2us
More LDPC code options
new LDPC code for 448 bits
Higher and Lower MCS
1024QAM
Seamless Handover
Multiple Connection
Frequency, Adaptation layer for multiple connections

## Slide 11: Features for mMTC
More bandwidth/SC interval options
Finer OFDMA
minimum frequency resource allocation unit is 16 subcarriers
High sleep ratio and long sleep duration

## Slide 12: Summary
Gives a brief introduction to the existing EUHT standards .
New features for URLLC and mMTC scenarios in EUHT system.

## Slide 13: Reference