## Slide 1: Adjacent Channel Transmission Detector
Date: 2019-05-14
Authors:
Onn Haran, Autotalks

## Slide 2: Recap
Adjacent channel transmitter create harmful interferences to vehicles in its proximity
The ability to utilize all channels is important to enablement of additional V2X use-cases
A simple mitigation scheme was presented in [1] and simulated in [2]: defer transmission while adjacent channel energy is detected
Outcome: Adjacent channel activity doesn’t interfere to nearby vehicles and not impacting latency
May 2019
Onn Haran, Autotalks

## Slide 3: Suggestion: Adjacent Channel Reception Detector allowing Upper Layer Decision
Not changing 802.11 state machines
Upper layer may optionally use PHY indications to defer transmission
  Decision logic is out of 802.11 scope
  Scales to any number of 802.11 channels
May 2019
Onn Haran, Autotalks
Upper layer decision
Channel #1
PHY/MAC
Channel #2
PHY/MAC
Left adjacent ch. detection
Right adjacent ch. detection
Left adjacent ch. detection
Right adjacent ch. detection
CCA
CCA

## Slide 4: Adjacent Channel Detector
The receiver is detecting adjacent channel while tuned to its own channel
  Transmissions in both higher and lower channels have to be detected
The out-of-band emissions of adjacent channel are observed
  It is expected that emissions follow the transmission mask
  Criteria would be “detection of strong signal shaped like OOB mask”
  Target energy could be aligned with ED threshold (-62dBm)
Onn Haran, Autotalks
Main Ch.
Adjacent Ch.
Observable OOB
(0MHz, -26dB)
(0.5MHz, -32dB)
(5MHz, -40dB)
(10MHz, -50dB)

## Slide 5: 20MHz Channel Operation
Onn Haran, Autotalks
Main Ch.
Adjacent Ch.
Main Ch.
Adjacent Ch.
Detection by 20MHz device
Detection of 20MHz channel
Assuming 10MHz channel mask is applied

## Slide 6: Straw Poll
Do you agree that 802.11bd shall include detector of adjacent channel reception?
Y: 7
N: 1
A:20
May 2019
Onn Haran, Autotalks

## Slide 7: References
  [1] Simulation of multi-channel interference (IEEE802.11-19-320/r0)
  [2] Multi-channel interference mitigation (IEEE802.11-19-48/r0)
May 2019
Onn Haran, Autotalks