## Slide 1: Reliable V2X operation
Date: 2019-05-14
Authors:
Onn Haran, Autotalks

## Slide 2: Reliability of Broadcast Based Network
  V2X transmissions, like any other Broadcast messages, are unacknowledged
  Packets can get lost due to failure, hidden node or challenging wireless channel
  Communication network can’t be trusted without message delivery feedback
  Soon, vehicles are expected to use V2X for control, calling for high reliability
  For example: platooning, emergency braking, emergency maneuver, etc…
  Futuristic use-cases, like cooperative maneuvering, can’t be supported without assurance

## Slide 3: Reliable Broadcast Protocols
  VANET broadcast transmission protocols were developed in the academy [1, 2]
  Most protocols define broadcast forwarding (i.e. multi-hop), which isn’t required since single-hop communication range is sufficient
  Some reliable broadcast protocols use selective acknowledgement and retransmission [3]
  3GPP took a similar direction (selective HARQ) in C-V2X Rel. 16

## Slide 4: Reasons for Adding Reliable V2X Operation to 11bd
  1. Single definition in 802.11 instead of multiple regional definitions
  Despite harmonization attempts, upper layers differ per geography. Multiple protocol variations should be avoided
  Not losing to 3GPP in future beauty contest
  Low-hanging fruit
  Simple addition of enabler. The protocol itself is outside 802.11

## Slide 5: Packet Retransmission Considerations
  V2X MAC retransmission is a bad idea
  Packet content is required to be fresh, containing the most updated content
  Instead, packet reception failure should trigger a generation of a new packet
  Packet generation decision is exclusively made by upper layer
  Decision considers multiple factors, like timing of next transmission, congestion control, which vehicles have failed to receive the packet
    For example, no need for retransmission if next transmission is scheduled 100mS ahead

## Slide 6: Minimal Scope of specification
  As opposed to 802.11e/802.11aa BlockAck, the retransmission isn’t performed by the MAC
  No new 802.11 buffers
  No new 802.11 protocol
  No new 802.11 state machine
  Upper layer defines the protocol
  The only 802.11bd change is definition of a new message to indicate received packets
  Minor effort

## Slide 7: Enhanced Reliability Concept
  Vehicles are sending list of received messages
  802.11 defines new packet format “Broadcast ACK”
  Upper layer determines if and when “Broadcast ACK” is transmitted considering channel load
  Vehicles can trigger packet transmission if their previous message wasn’t received
    Upper layer decision
TX
#1
#2
Packet generated ahead of scheduled time
RX
Packet #1 isn’t reported as received

## Slide 8: Scenarios
  Transmitter failure
  Blue car transmits and receives messages, but no other car reports that it received its MAC address
  Hidden node collision
  Purple and green cars transmitted concurrently. Blue car reports the received vehicles, including vehicles further away from green and purple, but not those two. The purple vehicle will trigger a transmission in next 100mS despite not having to
  Wireless link failure
  Green car sometimes fail to receive the blue car. In those cases, the blue car triggers a new packet

## Slide 9: Broadcast Ack can be Encoded as new BlockAck Variant
  Reserved values can be utilized

## Slide 10: Possible Broadcast Ack Format
  Packet contains MAC addresses of successfully received broadcast stations during window
  Typical window is 100mS, so each station is commonly sending a single packet
  Subset of MAC address (e.g. 16bits) can be sent for minimizing channel load
  A station might be mistaken to believe that a message was received. Potential needed transmission wouldn’t be triggered, yet V2X integrity wouldn’t be harmed
  Window start and end times enables detection of lost Broadcast Ack and determining if packet should have been received
  For example, field represented as [0…9999]mS aligned with GNSS timing
RX MAC address #1
2
Octets
RX MAC address #2
2
RX MAC address #N
2
. . . . . . . . . . . . . . .
Window start and end
3 or 4

## Slide 11: Security Impact
  BlockAck message is unsecure
  One can fake a message indicating that packets were received while they weren’t
  The attack will eliminate the reliability enhancement, but will not further harm. Therefore, the threat is low

## Slide 12: Straw Poll #1
Do you agree to add that 802.11bd shall facilitate enhanced reliability?
Y: 13
N: 0
A: 21
May 2019
Onn Haran, Autotalks

## Slide 13: References
  [1] A Survey on Broadcasting Protocols in VANETs, Jothi K R,Ebenezer Jeyakumar A
[2] Evaluation of Selective Broadcast Algorithms for Safety Applications in Vehicular Ad Hoc Networks, Kaan Bür and Maria Kihl
[3] Acknowledgment-Based Broadcast Protocol for Reliable and Efficient Data Dissemination in Vehicular Ad Hoc Networks, Francisco J. Ros, Pedro M. Ruiz and Ivan Stojmenovic
May 2019
Onn Haran, Autotalks