## Slide 1: PPDU Format for 11bd
Date: 2019-05-14
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo choi |  |  |  | js.choi@lge.com
May 2019

## Slide 2: Introduction
We had discussed PPDU format for 11bd in previous meeting and decided the followings [1]
  “11bd PPDU format includes L-STF, L-LTF, and L-SIG fields”
  “In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated”
However, a detail construction of 11bd PPDU has not been yet discussed and decided, so the portion for 11bd in 11bd PPDU is still remained as an undefined.
Therefore, in this contribution, we investigate some technical issues need to be considered when we design the 11bd PPDU format.

## Slide 3: Packet classification (1/2)
As described in [1], 11bd devices can receive either 11p PPDU or 11bd PPDU.
So, to decode the received PPDU successfully, 11bd devices should distinguish whether receiving PPDU is a 11p PPDU or 11bd PPDU.
  Also, it is desirable to distinguish either of it as early as possible.
For differentiating of PPDU, we can consider using one OFDM symbol after L-SIG and this symbol can be used as following.
  Option 1 : for checking constellation mapping
  Option 2 : for checking repetition
In next slides, we discuss the details for each option.

## Slide 4: Packet classification (2/2)
This is not a new method for PPDU classification. Indeed, it already has been used in enhanced WLAN systems.
To leverage the conventional method, we can consider the two options to use the one OFDM symbol after L-SIG.
  Option1 : checking the constellation of symbol
    For that purpose, rate field in L-SIG shall be set to the value of 3 Mb/s.
    And then, Q-BPSK constellation mapping is applied to one OFDM symbol after L-SIG.
    It can be simply implemented and early detection is possible
    This symbol may be used for channel estimation or indication of some information for 11bd transmission.
  Option 2: checking the repetition
    For that purpose, one symbol is being repeated with an L-SIG symbol when 11bd PPDU is transmitted.
      This is already applied to 11ax for classification of 11ax PPDU.
    It can be simply implemented.
    By repeating the L-SIG, we can look forward to the robust transmission of 11bd
L-SIG
Q-BPSK
L-STF
L-LTF
L-SIG
L-SIG
L-STF
L-LTF

## Slide 5: Preamble for 11bd portion
Short Training Field
  In general, STS(i.e., short training symbol) located after the L-SIG is used to improve the automatic gain control for MIMO transmission in 802.11 systems.
  However, MIMO transmission(i.e., beamforming) may not be considered in 11bd in which only one stream transmission may be supported.
  Therefore, we think STF for improving the auto gain control does not need in 11bd
Long Training Field
  The tone allocations for 11bd 10MHz PPDU and 20MHz PPDU have not been defined yet but they can have a different guard tone and available tone in 10/20MHz.
  So, it is hard to estimate the channel accurately because L-LTF can’t support the some of guard or available tones.
  Therefore, in order to estimate the channel without missing, LTF for 11bd is needed that is suitable for tone allocation.

## Slide 6: Candidate for 11bd PPDU
PPDU format for 11bd
  For classification of PPDU, one OFDM symbol after L-SIG is placed in PPDU.
    One OFDM symbol can be either modulated with Q-BPSK or replaced with L-SIG symbol.
    In 20MHz PPDU, L-STF,L-LTF, L-SIG and one OFDM symbol for 10MHz PPDU are duplicated.
  We may not need to insert the additional OFDM symbol if it would be feasible to apply Q-rotated LTF after L-SIG .
L-SIG
One OFDM symbol
L-STF
L-LTF
NGV-LTF
Data
L-SIG
One OFDM symbol
L-STF
L-LTF
L-SIG
One OFDM symbol
L-STF
L-LTF
NGV-LTF
Data
10MHz
20MHz
L-SIG
L-STF
L-LTF
Rotated -LTF
Data
L-SIG
L-STF
L-LTF
L-SIG
L-STF
L-LTF
Rotated-LTF
Data
10MHz
20MHz

## Slide 7: OFDM Numerology : recap
In our previous contribution[1], following OFDM numerologies have been discussed.
  For example, for 20MHz, we can leverage OFDM numerologies of advanced WLAN system such as 11ac and 11ax
  we have shown that op1 and op2 have a similar performance when impairment is not considered.
In this contribution, we perform further investigation of the OFDM numerologies for 11bd by considering the impairment such as CFO.
 | OFDM Numerology | NFFT | NSD | Symbol duration* | Tone spacing | Downclock Ratio
Op.1 | 11ac 40MHz | 128 | 108 | 8us* | 156.25KHz | 2
Op.2 | 11ax 20MHz/ 11ac 80MHz | 256 | 234 | 16us* | 78.125KHz | 4
* : For example, CP = 1.6us for Op.1, CP = 3.2us Op.2

## Slide 8: Simulation assumption
BW : 10MHz
Data : 300Byte
FEC : LDPC
MCS level : 2/4/6
OFDM numerology
  2x : 11ac 20MHz ( 64 FFT)
  4x : 11ac 40MHz ( 128 FFT)
Channel
  Rural LoS, Highway LoS, Highway NLos
Mid-amble period
  4 symbol
  For mid-amble symbol, VHT-LTF is used
CFO
  20PPM in 5.9GHz
Channel estimation : LS

## Slide 9: Performance
Rural LoS
  For all MCS level, it has a similar performance regardless of OFDM numerology.
    But, slightly the 2x numerology has a better performance .

## Slide 10: Performance
Highway LoS
  In High MCS level, i.e., MCS6, 2x OFDM numerology has a 2dB gain compared with 4x numerology

## Slide 11: Performance
Highway NLoS
  In MCS 2 and MCS4, it has a similar performance with both OFDM numerologies.
  But, in MCS6, 4x numerology has a performance degradation

## Slide 12: Conclusion
In this contribution, we examined the followings need to be considered for 11bd PPDU format design.
  For the packet classification, we introduced the two methods that were already adopted in 802.11 systems.
    One is a detection method based Q-BPSK
    Another is a detection method based repetition
  For the design of preamble for an 11bd portion,
    the STF for 11bd may not need to be included.
    the LTF for 11bd should be included to estimate the channel.
Also, we evaluated the performance of OFDM numerologies for 11bd with CFO.
  In all channels, both OFDM numerologies show similar performance when MCS 2 and MCS4 are assumed.
    But, 2x OFDM numerology has a slight better performance in some channel.
  Also, we can confirm that 4x OFDM numerology shows performance degradation when MCS6 is used in highway channel.
    Due to CFO impact, the performance loss is about 2 ~ 6dB.
  Stable performance of 11bd in V2V channel with channel impairment can be achieved using 2x OFDM numerology.

## Slide 13: SP1
Do you agree to add the following to section 3 in 11bd SFD?
  “11bd PPDU includes the NGV-Signal field for indication of transmission information”
  Y/N/A

## Slide 14: SP2
Do you agree to using NGV-SIG field or add repeated L-SIG symbol after L-SIG for packet classification?
  Y/N/A

## Slide 15: SP3
Which option do you support for packet classification ?
  Option 1 : using NGV-SIG field
  Option 2: using repeated L-SIG
  Abs

## Slide 16: SP4
Do you agree that the preamble for 11bd portion consists of following?
  “In a 11bd PPDU, NGV-STF field does not present. And, the preamble for 11bd portion consists only NGV-LTF field.”
  Y/N/A

## Slide 17: SP5
Do you agree to add the following to section 3 in 11bd SFD ?
  11bd PHY shall support the half-clocked operation both using 10 MHz channel spacing and 20MHz channel spacing
    half-clocked from 11ac OFDM numerology.

## Slide 18: Reference
[1] IEEE 802.11-19-0332/r2 , PHY design for 11bd