## Slide 1: 11be Peak Data Rate Analysis
Date: 2019-05-08
Authors:
Name | Affiliations | Address | Phone | Email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 
David Xun Yang |  |  |  | 
Notes: September 2012

## Slide 2: PAR Recap
High throughput and low latency are two key requirements of EHT in the PAR of EHT[1].
The main candidate feature mentioned in the PAR [1] are:
  320MHz bandwidth and more efficient utilization of non-contiguous spectrum,
  Multi-band/multi-channel aggregation and operation,
  16 spatial streams and Multiple Input Multiple Output (MIMO) protocols enhancements,
  Multi-Access Point (AP) Coordination (e.g. coordinated and joint transmission),
  Enhanced link adaptation and retransmission protocol (e.g. Hybrid Automatic Repeat Request (HARQ)),
  If needed, adaptation to regulatory rules specific to 6 GHz spectrum

## Slide 3: Spectrum Recap
For 5 GHz, two 160 MHz contiguous channels can be provided.
For 6 GHz, 3 possible 320 MHz contiguous channels[NOTE], 4 possible 240MHz contiguous channels, 7 possible 160 MHz contiguous channels.
Note: assume a 320 MHz contiguous channel can be formed by crossing two U-NII bands provided that the two U-NII bands are technically identical in terms of unlicensed regulatory requirements.

## Slide 4: Peak data rate analysis
By considering the candidate feature in PAR, assuming 320 MHz, 16SS, 1024-QAM, the peak data rate is 38.4 Gbps. If 4K-QAM is further applied, the peak data rate can be 46.08 Gbps.
Further taking into consideration of multi-band/multi-channel aggregation, the peak data rate can be:
The achievable peak data rate considering 5GHz and 6GHz spectra is about 207Gbps. Further taking the complexity into consideration, a peak data rate of 100Gbps is feasible.
Link # | BW configuration | Peak data rate | 
 |  | w/ 1K QAM | w/ 4K QAM
2 links | 320MHz + 320MHz | 76.8Gbps | 92.16Gbps
3 links | 320MHz + 320MHz + 160MHz | 96Gbps | 115.2Gbps
3 links | 320MHz + 320MHz + 320MHz | 115.2Gbps | 138.24Gbps
9 links | 9*160MHz | 172.8Gbps | 207.36Gbps

## Slide 5: Benefits and Necessity of Achieving 100Gbps
From market point of view, from one generation to another, Wi-Fi should have larger data rate than cellular network of the same generation.
  Theoretically, 5G NR can already support 78.2 Gbps peak data rate.
From application requirement point of view, in [3], for wireless VR applications, the PHY link Tput for raw stream or lightly compressed stream is >30 Gbps. For 3D ultimate immersion and lightly compressed rate, the required rate is 80.62 Gbps.
 |  | Cellular | Wi-Fi
4G LTE-A vs 11ac | Peak data rate | 1Gbps | 6.9 Gbps
5G NR vs 11ax | Peak data rate | 4.89 Gbps per CC 78.2 Gbps over 16CCs (in FR1, sub 6 GHz) [2] | 9.6 Gbps over 160MHz
 | BW | 1.6 GHz for 16CCs 100 MHz per CC | 160 MHz

## Slide 6: Conclusion
Benefits, necessity and feasibility for 11be to achieve a data rate of 100Gbps are discussed.
The proposed method is good for 11be market promotion, can support VR applications for raw stream or lightly compressed stream.

## Slide 7: Reference
[1] 1231r6 EHT draft proposed par
[2] RP-182102 TR37.910 v1.0.0.docx
[3] 11-18-1954-02-0eht-eht-use-case-discussion-vr-requirement-follow-up