## Slide 1: Latency analysis for EHT
Date: 2019-05-13
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Taewon Song |  |  |  | taewon.song@lge.co
Sungjin Park |  |  |  | allean.park@lge.com
Saehee Bang |  |  |  | saehee.bang@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com

## Slide 2: Abstract
This presentation addresses the latency analysis and simulation results for EHT to reduce latency and jitter. This analysis may allow EHT to review technologies to support low latency traffic.

## Slide 3: Low latency support discussion
We have discussed supporting low latency application in EHT
Low latency is mentioned in several sub-clauses in the PAR document
  5.2.b. Scope of the project: “This amendment defines at least one mode of operation capable of improved worst case latency and jitter.”
  5.5 Need for the Project: “New high-throughput, low latency applications will proliferate such as virtual reality or augmented reality, gaming, remote office and cloud computing”. “With the high throughput and stringent real-time delay requirements of these applications, users expect enhanced throughput, enhanced reliability, reduced latency and jitter, and improved power efficiency in supporting their applications over WLAN.”

## Slide 4: Submissions in March meeting
[1] introduces Real Time Application and Time-Sensitive Networking
  RTA TIG provides final report (18/2009r6) which contains description of real-time application usage model, problem statement, technical requirements and potential solutions
  It addresses opportunity for improving reliability for RTA and time-sensitive applications in EHT
[2] proposes multiple primary channels for EHT to mitigate channel access delay
  It also shows simulation results
[3] suggests streaming game as a part of EHT use case

## Slide 5: Latency analysis
The latency will be analyzed by dividing into several portions
To facilitate the better analysis, we will start with the analysis in limited environment
  DL or UL only traffic
  Single BSS
  Fixed number of STA
  Constant Bit Rate (CBR) traffic
  Fixed MCS
And then we will move to next step

## Slide 6: Latency portions – No error case
TW: Contention waiting time
  Time to transmit previously arrived packets
TC: Contention time
  AIFS + backoff + busy time
TTX: Transmission time
  Data TX time + SIFS + ACK TX time

## Slide 7: Latency portions – Error case
TR: Additional time for retransmission
  Time spent for failed transmission
TW: Contention waiting time
TC: Contention time
TTX: Transmission time

## Slide 8: Simulation setting for DL
AP-STA distance: 45 meter
1 AP – 1 STA
Channel model: TGnD
Fixed MCS
Traffic model: CBR, DL only, 1500 bytes MSDU
TX power: 20 dBm(AP), 17 dBm(STA)
40, 80, 160 MHz BW in 5 GHz band

## Slide 9: Simulation cases
We will analyze trend of latency portions in environments where the following variables change.
  Case 1: MCS 1 ~ 5
    50 Mbps traffic load, 80 MHz BW
  Case 2: BW 40 MHz, 80 MHz, 160 MHz
    50 Mbps traffic load, MCS 4
  Case 3: Traffic load 50 Mbps ~ 200 Mbps
    MCS 4, 80 MHz BW
Since there is only one contention device (AP), the impact of ‘Contention time’ can be ignored

## Slide 10: DL Latency analysis: Case 1 (MCS)
 | Tput [Mbps] | PER [%] | Total Latency [usec]
MCS 5 | 47.3 | 46.6 | 15,689
MCS 4 | 50.0 | 6.9 | 694
MCS 3 | 50.0 | 0 | 614
MCS 2 | 50.0 | 0 | 854
MCS 1 | 50.0 | 0 | 2,464

## Slide 11: DL Latency analysis: Case 1 (MCS)
Detail results
 |  |  |  | Each latency portion [usec] |  |  | 
 | Tput [Mbps] | PER [%] | Total Latency* [usec] | TW | TC | TTX | TR
MCS 5 | 47.3 | 46.6 | 15,689 | 12,920 (82.4%) | 114 (0.7%) | 645 (4.1%) | 4,312 (12.8%)
MCS 4 | 50.0 | 6.9 | 694 | 188 (27.1%) | 110 (15.8%) | 266 (38.3%) | 1,899 (18.8%)
MCS 3 | 50.0 | 0 | 614 | 188 (30.7%) | 109 (17.8%) | 316 (51.5%) | -
MCS 2 | 50.0 | 0 | 854 | 291 (34.0%) | 109 (12.8%) | 455 (53.2%) | -
MCS 1 | 50.0 | 0 | 2,464 | 815 (33.1%) | 109 (4.4%) | 1,540 (62.5%) | -
*Total latency = TW + TC + TTX + PER * TR

## Slide 12: DL Latency analysis: Case 2 (BW)
 | Tput [Mbps] | PER [%] | Total Latency [usec]
40 MHz | 50.0 | 2.2 | 3,392
80 MHz | 50.0 | 6.9 | 694
160 MHz | 50.0 | 6.8 | 463

## Slide 13: DL Latency analysis: Case 2 (BW)
Detail results
 |  |  |  | Each latency portion [usec] |  |  | 
 | Tput [Mbps] | PER [%] | Total Latency* [usec] | TW | TC | TTX | TR
40 MHz | 50.0 | 2.2 | 3,392 | 2,436 (71.8%) | 112 (3.3%) | 697 (20.6%) | 6,816 (4.3%)
80 MHz | 50.0 | 6.9 | 694 | 188 (27.1%) | 110 (15.8%) | 266 (38.3%) | 1,899 (18.8%)
160 MHz | 50.0 | 6.8 | 463 | 145 (31.3%) | 111 (24.1%) | 174 (37.7%) | 471 (6.9%)
*Total latency = TW + TC + TTX + PER * TR

## Slide 14: DL Latency analysis: Case 3 (Traffic load)
 | Tput [Mbps] | PER [%] | Total Latency [usec]
50 Mbps | 50.0 | 6.9 | 694
100 Mbps | 100.0 | 5.3 | 4,342
150 Mbps | 147.7 | 4.1 | 9,760
200 Mbps | 159.5 | 4.0 | 73,391

## Slide 15: DL Latency analysis: Case 3 (Traffic load)
Detail results
 |  |  |  | Each latency portion [usec] |  |  | 
 | Tput [Mbps] | PER [%] | Total Latency* [usec] | TW | TC | TTX | TR
50 Mbps | 50.0 | 6.9 | 694 | 188 (27.1%) | 110 (15.8%) | 266 (38.3%) | 1,899 (18.8%)
100 Mbps | 100.0 | 5.3 | 4,342 | 3,265 (75.2%) | 109 (2.5%) | 690 (15.9%) | 5,268 (6.4%)
150 Mbps | 147.7 | 4.1 | 9,760 | 7,292 (74.7%) | 110 (1.1%) | 2,113 (21.6%) | 5,932 (2.5%)
200 Mbps | 159.5 | 4.0 | 73,391 | 68,487 (93.3%) | 109 (0.1%) | 4,513 (6.1%) | 7,031 (0.4%)
*Total latency = TW + TC + TTX + PER * TR

## Slide 16: Observation on DL results
MCS that maximizes Tput and MCS that minimizes latency can be different
  In normal cases, Tput is maximized at the PER 10~20%
  However, the results shows that latency is the minimum when the PER is near 0%
Even though the PER increases, the latency decreases as the BW increases
The latency increases dramatically when traffic is saturated
The variation in TW is greater than the others

## Slide 17: Simulation setting for UL
AP-STAs distance: 45 meter
STAs are co-located (1 ~ 40 STAs)
Channel model: TGnD
Fixed MCS 4
Traffic model: CBR, UL only, 1500 bytes MSDU
TX power: 20 dBm(AP), 17 dBm(STA)
80 MHz BW in 5 GHz band
RTS/CTS on/off

## Slide 18: Simulation cases
We will analyze trend of latency portions in environments where the following variables change.
  Case 1: Number of STA, 1 ~ 10 STAs
    Traffic load = 10 Mbps per STA, RTS/CTS on/off
  Case 2: Number of STA, 10 ~ 40 STAs
    Traffic load = 1 Mbps per STA, RTS/CTS on/off
  Case 3: Access category, 6 STAs
    5 low rate STAs + 1 high rate STA
    High rate STAs: 100 Mbps traffic load, AC_BE/VI/VO
    Low rate STAs: 1 Mbps traffic load per STA, AC_BE only
    RTS/CTS off

## Slide 19: UL Latency analysis: Case 1 (Number of STA)

## Slide 20: UL Latency analysis: Case 1 (Number of STA)
Detail results
*Total latency = TW + TC + TTX + PER * TR
 |  |  |  |  | Each latency portion [usec] |  |  | 
 | RTS/ CTS | Tput [Mbps] | PER [%] | Total Latency* [usec] | TW | TC | TTX | TR
1 STA | Off | 9.88 | 1.9 | 313 | 2 | 110 | 193 | 483
 | On | 9.88 | 1.8 | 441 | 1 | 237 | 193 | 526
2 STA | Off | 19.76 | 3.7 | 324 | 3 | 111 | 193 | 460
 | On | 19.76 | 4.6 | 506 | 3 | 270 | 196 | 833
5 STA | Off | 49.37 | 47.9 | 7,902 | 2,102 | 1,844 | 631 | 6,947
 | On | 49.34 | 19.6 | 11,019 | 1,402 | 5,955 | 1,095 | 13,109
10 STA | Off | 81.67 | 55.3 | 634,556 | 553,085 | 9,826 | 4,053 | 122,299
 | On | 98.27 | 24.3 | 89,986 | 45,902 | 24,775 | 3,232 | 66,044

## Slide 21: UL Latency analysis: Case 2 (Number of STA)

## Slide 22: UL Latency analysis: Case 2 (Number of STA)
Detail results
*Total latency = TW + TC + TTX + PER * TR
 |  |  |  |  | Each latency portion[usec] |  |  | 
 | RTS/ CTS | Tput [Mbps] | PER [%] | Total Latency* [usec] | TW | TC | TTX | TR
10 STA | Off | 9.88 | 53.9 | 1,617 | 21 | 422 | 193 | 1,819
 | On | 9.88 | 30.4 | 3,121 | 4 | 1,972 | 194 | 3,135
20 STA | Off | 19.76 | 65.3 | 3,804 | 105 | 748 | 194 | 4,224
 | On | 19.76 | 32 | 8,784 | 374 | 5,423 | 226 | 8,641
30 STA | Off | 49.37 | 67.4 | 11,215 | 2,115 | 2,363 | 230 | 9,651
 | On | 49.34 | 31.5 | 22,641 | 2,168 | 13,168 | 368 | 22,016
40 STA | Off | 81.67 | 66.6 | 45,097 | 10,828 | 11,248 | 486 | 33,836
 | On | 98.27 | 32.7 | 42,853 | 4,794 | 24,313 | 591 | 40,249

## Slide 23: UL Latency analysis: Case 3 (Access Category)

## Slide 24: UL Latency analysis: Case 3 (Access Category)
Detail results
*Total latency = TW + TC + TTX + PER * TR
 |  |  |  |  | Each latency portion[usec] |  |  | 
 | AC | Tput [Mbps] | PER [%] | Total Latency* [usec] | TW | TC | TTX | TR
Case 3-1 | BE | 85.48 | 43.1 | 100,014 | 91,656 | 397 | 4,360 | 8,346
 | BE | 4.90 | 50.7 | 65,308 | 18,623 | 19,019 | 575 | 53,471
Case 3-2 | VI | 94.32 | 36.5 | 45,278 | 38,604 | 377 | 3,656 | 7,224
 | BE | 4.74 | 67.5 | 297,566 | 97,028 | 58,690 | 1,982 | 207,227
Case 3-3 | VO | 98.61 | 23.5 | 7,038 | 4,178 | 297 | 1,692 | 3,710
 | BE | 4.17 | 82.1 | 289,752 | 97,017 | 48,329 | 1,997 | 173,362

## Slide 25: Observation on UL results
RTS/CTS shows performance gains not only in Tput but also in latency when the number of STAs is above a certain level
  On the contrary, RTS/CTS degrades latency performance if the number of STAs is below the certain level
  The level depends on number of STA and traffic load
Unlike in DL case, the portion of TC,TR by collision increases significantly if the number of STAs increases
We can enhance latency performance of certain traffic dramatically by allocating AC_VI,VO instead of AC_BE
  However AC_BE STAs should be prepared for performance degradation on Tput and latency

## Slide 26: How to reduce latency
We could see from the simulation results that the followings can reduce latency
  Use appropriate MCS for latency and wider BW
  Use RTS/CTS only when the number of STAs is high
  Use AC_VI/VO instead of AC_BE
And it can be inferred that the followings can also reduce latency indirectly
  Enhance PHY data rate
  Use HARQ
  Multi-user transmission

## Slide 27: Further step
Applying TST (time sensitive traffic) model
  We will apply TST which is defined in 11ax Evaluation Methodology document and RTA TIG report
Latency performance on OFDMA
  We will address performance gain on latency when we adopt OFDMA
    Preliminary results were submitted in TGax [4][5]
    We will conduct in-depth review in terms of latency on OFDMA
OBSS performance
  We will extend current simulation to OBSS environment
We will evaluate latency performance of EHT features
  Multi-band, 16 streams, 320 MHz, etc.

## Slide 28: Summary
We conducted in-depth latency analysis on non-MU system
  The latency is divided into several portions and analyzed with simulation
  We could identify some variables that affect latency
  We also were able to check some things to reduce latency by simulation results

## Slide 29: References
[1] 11-19-0373-00-0eht-time-sensitive-applications-support-in-eht.pptx
[2] 11-19-0402-01-0eht-reducing-channel-access-delay.pptx
[3] 11-19-0430-00-0eht-low-latency-streaming-capability-for-game-applications.pptx
[4] 11-16-1363-01-00ax-11ax-par-verification-through-ofdma.ppt
[5] 11-15-1095-10-00ax-ofdma-performance-in-11ax.ppt

## Slide 30: Appendix
Latency portion in RTS/CTS case