## Slide 1: Enhanced Multi-band/Multi-channel Operation
Date: 2019-05-14
Authors:

## Slide 2: Outline
As described in the EHT PAR, one of the needs of the EHT program is to provide the high throughput and meet stringent real-time delay requirements of 4k and 8k video, virtual reality or augmented reality, gaming, remote office and cloud computing applications.
In this presentation, we have analyzed how the EHT multi-band/multi-channel operation can be helpful to meet those PAR requirements.

## Slide 3: EHT Multi-band/Multi-channel Functional Requirement
In a legacy multi-band and multi-channel operation (e.g., FST), sessions of an individual STA can be transferred from a channel to another channel, in the same or different frequency bands.
But, a limitation is that MSDUs belonging to single TID can only use single bands and/or channels.

## Slide 4: EHT Multi-band/Multi-channel Functional Requirement
As discussed in [1], if a STA can simultaneously use the multiple bands and/or channels, per-session throughput and per-session latency can be significantly improved.
  Because MSDUs belonging to single session (e.g., TID) can be sent on multiple bands and/or channels simultaneously.

## Slide 5: EHT Multi-band/Multi-channel Functional Requirement
A STA may perform a channel access on multiple bands and/or channels independently.
When the STA obtains TXOPs on multiple bands and/or channels, it can send frames belonging to same TID over multiple links simultaneously.
Data [Seq1, TID1]
5GHz
6GHz
Data [Seq2, TID1]
Data [Seq3, TID1]
Data [Seq4, TID1]
Block ACK
Block ACK
Data [Seq5, TID1]
…
AP
STA
AP
STA
backoff

## Slide 6: EHT Multi-band/Multi-channel Functional Requirement
But, if the STA has an in-device coexistence interference on multiple bands and/or channels, it may not transmit and receive frames simultaneously.
In such a case, the STA needs to coordinate and synchronize the transmission and reception timing over bands and/or channels.
Data [Seq1, TID1]
5GHz
6GHz
Data [Seq2, TID1]
Data [Seq3, TID1]
Data [Seq4, TID1]
Block ACK
Block ACK
Data [Seq5, TID1]
…
AP
STA
AP
STA
backoff
Data [Seq6, TID1]
…
backoff

## Slide 7: EHT Multi-band/Multi-channel Functional Requirement
In this operation, the STA should access multiple bands and/or channels without additional protocol overhead.
  With legacy FST, when switching sessions, the SME of the STA needs to initiate the FST Setup Request and Response frame exchanges as well as the FST Ack Request and Response frame exchanges.
Also, control information (e.g., control frames, A-Control fields) for a channel can be transmitted in a different channel/band.
  Allowing out-of-band exchange of control information can result in more efficient allocation of resources.

## Slide 8: Performance Evaluation via Simulation
Throughput comparison between single band operation (legacy) and multi-band operation
AP
STA
Link 1/5GHz
Link 2/6GHz
AP
STA
Link 1/5GHz
Single-band
(Legacy)
Multi-band

## Slide 9: Performance Evaluation via Simulation
Busy
Busy
Link 1/5GHz
Link 2/6GHz
Async Operation
Dual primary channels (on Link 1 and Link 2) Sync Operation
Busy
Single primary channel (on Link 1) Sync Operation
Busy
Busy
Busy
Link 1/5GHz
Link 2/6GHz
Link 1/5GHz
Link 2/6GHz

## Slide 10: Simulation Setup
Simulation Parameters:
  Bandwidth: 80 MHz
  MCS: 9 (453.7 Mbps)
  Full buffer DL UDP traffic.
  Busy percentage: Percentage of Link 2/6GHz air time occupied by OBSS activities on Link 1/5GHz.

## Slide 11: Performance Evaluation via Simulation

## Slide 12: Conclusion
In this contribution we discuss the limitations of legacy multi-band/multi-channel operation and the desired EHT multi-band/multi-channel function requirements.
  Key improvement should be that a STA can transmit frames of same TID or different TIDs over multiple bands and/or channels concurrently or non-concurrently.
Via Simulation, showed that it is possible for multi-band/multi-channel operation (synchronous and asynchronous) to achieve significant performance enhancements under heavy interference.

## Slide 13: Reference
[1] https://mentor.ieee.org/802.11/dcn/18/11-18-1155-01-0eht-multi-ap-enhancement-and-multi-band-operations.pptx