## Slide 1: Enabling Persistent Allocation for EHT
Date: 2019-05-12
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yanyi Ding |  |  |  | 

## Slide 2
Background
Many candidate features for 11be has been discussed in EHT SG [1], e.g.
  320MHz bandwidth and more efficient utilization of non-contiguous spectrum
  Multi-band/multi-channel aggregation and operation
  16 spatial streams and MIMO protocols enhancements
A large amount of users can be supported in a single PPDU. For example,
  If all 26-tone RUs in 320 MHz are allocated to different STAs, about 150 users can be supported in a single PPDU.
It is expected that control signaling overhead required for EHT MU transmission will be increased significantly.
This contribution addresses one possibility of reducing control signaling overhead for EHT MU transmission.

## Slide 3
  Only dynamic allocation per PPDU is allowed for HE MU transmission.
    For DL MU, resource allocation information for all RU allocations is included in the HE-SIG-B of a HE MU PPDU.
    For UL MU, resource allocation information for all RU allocations is included in the Trigger frame for soliciting HE TB PPDU transmission.
  For reducing control signaling overhead, persistent allocation (PA) across PPDUs can be considered for EHT MU transmission.
    For a PA, user-specific allocation information (e.g. RU allocation, MCS, SS allocation, etc.) is unchanged for a time period.
    Transmissions of a PA can be done with reduced control signaling overhead before the PA expires.
Enabling Persistent Allocation for EHT

## Slide 4
Thought on Persistent Allocation for Uplink MU Transmission
A PA identifier (PAID) which uniquely identifies an uplink PA can be included in a Trigger frame to solicit the transmissions of the uplink PA.

## Slide 5: Example Use Case
In an IoT usage scenario with a lot of client devices (STAs),
  The STAs may be grouped into a number of groups.
    Most of STAs are fixed and thus the grouping may be stable for a long time.
  AP may poll each group of STAs periodically to report device information.
    The STAs in a group may share the same PAID.
      Hundreds of STAs can be scheduled with a limited number of PAID.
AP
A lot of STAs
(e.g. sensors)
Time
Poll G1 using PAID1
Poll G2 using PAID2
G1 Uplink
G2 Uplink
G1 Uplink
G2 Uplink
Poll G1 using PAID1
Poll G2 using PAID2

## Slide 6: Summary
It is proposed to enable persistent allocation for EHT to reduce control signalling overhead for MU transmission, especially for uplink MU transmission.

## Slide 7: Reference
11-18-1231-06-0eht-eht-draft-proposed-par, March 2019