## Slide 1
Further Discussion on legacy indication in NGV
Date: 2019-05-14
Authors:

## Slide 2: Introduction
In 11bd SFD[1],
  The PPDU format can be requested by upper layer
  11bd devices indicate NGV capabilities in MAC frame format, when it transmits 11p PPDU
Since the transmission of 11p PPDU by 11bd device indicates that the 11p device is located around the 11bd device, the receiver of 11p PPDU with NGV capabilities may:
  Decide the PPDU format considering the efficiency, interoperability, and environmental issue
  May need to collect more information to decide the PPDU format
In this contribution, the various cases of coexistence with legacy devices are investigated

## Slide 3: Recap: Indication of 11bd Capability
To provide interoperability in coexistence case, 11bd devices indicate the NGV capability when it transmits 11p PPDU[2]

## Slide 4: 11p PPDU transmission case for interoperability
When a 11bd device receives 11p PPDU with NGV capability, it may transmit 11bd PPDU or 11p PPDU
  Decision may be performed by the upper layer
To ensure the interoperability and fairness[3] in 11p devices, it may use 11p PPDU format

## Slide 5: Need for addition indication for robustness
However, if 11bd devices use 11p for robustness in coexistence environment, unnecessary 11p PPDU transmission may occur
  11bd devices may transmit 11p PPDU even though there is no 11p device around it
  Without other information, the decision of PPDU format may be inaccurate

## Slide 6: Insertion of additional information
To help the decision of PPDU type, 11bd device transmitting 11p PPDU may insert additional information in addition to the 11bd capability
  The received RSSI value
    The receiver may decide to transmit 11p PPDU when the RSSI is more than certain value

## Slide 7: Insertion of hop information
To help the decision of PPDU, 11bd device transmitting 11p PPDU may insert additional information in addition to the 11bd capability
  The hop count may prevent unnecessary propagation of 11p PPDU transmission

## Slide 8: Conclusion
In this presentation, the transmission cases of 11p PPDU sent by 11bd devices are discussed
When it detects 11p PPDU sent by 11bd device, it may use 11p PPDU format for robustness
  The request of PPDU format may be performed by upper layer
To prevent the unnecessary propagation of 11p PPDU transmission, more information on 11p device may be helpful for upper layer to decide the proper PPDU format
  The information may include hop count, Rx RSSI, etc.

## Slide 9: Reference
[1] 19/0497r1 specification framework document
[2] 19/0018r0 NGV backward interoperability discussions
[3] 18/0861r9 IEEE 802.11 NGV SG Proposed PAR

## Slide 10: Straw poll 1
Do you agree that the additional information (e.g. hop count, received power) in addition to the 11bd capability is needed?
Y/N/A

## Slide 11: Straw poll 2
Do you agree to indicate the hop count of received 11p PPDU from legacy device when the 11bd devices transmit 11p PPDU?
Y/N/A

## Slide 12: Straw poll 3
Do you agree to indicate the received RSSI of the received 11p PPDU when the 11bd devices transmit 11p PPDU?
Y/N/A