## Slide 1
11p PPDU transmission with legacy device information
Date: 2019-07-15
Authors:

## Slide 2: Introduction
In 11bd SFD[1],
  “To transmit PPDU format up on request from upper layer, the PPDU format can be either 11p PPDU or 11bd PPDU.”
  “An 11bd STA shall indicate the NGV capability in MAC level, when transmitting an 11p PPDU.”
  “When an 11bd STA transmits an 11p group-addressed or unicast PPDU, the Duration/ID field of a frame in an 11p PPDU indicates that transmitter of the PPDU is an NGV capable STA.”
Since the decision of PPDU format is made by upper layer, more information is preferable in order to make more correct decision
  Conservative vs Efficient
In this contribution, various cases of coexistence with legacy devices are investigated

## Slide 3: Recap: Indication of 11bd Capability
To provide interoperability in coexistence case, 11bd devices indicate the NGV capability when it transmits 11p PPDU[2]

## Slide 4: Unnecessary 11p PPDU TX propagation
To ensure the interoperability and fairness[3] in 11p devices, it may use 11p PPDU format
  Conservative approach: use 11p PPDU format

## Slide 5: Additional Information to Help PPDU Format Decision
Hop # and/or RSSI can help 11bd devices to figure out how far the legacy device is.

## Slide 6: Conclusion
In this presentation, the transmission cases of 11p PPDU sent by 11bd devices are discussed
When 11bd detects 11p PPDU sent by 11bd device, it may use 11p PPDU format for robustness
  The PPDU format decision is made by upper layer
To prevent the unnecessary propagation of 11p PPDU transmission, more information on 11p device may be helpful for upper layer to make decision on the proper PPDU format
  The information may include hop count, Rx RSSI, etc.

## Slide 7: Reference
[1] 19/0497r1 specification framework document
[2] 19/0018r0 NGV backward interoperability discussions
[3] 18/0861r9 IEEE 802.11 NGV SG Proposed PAR

## Slide 8: Straw poll 1
Do you agree that the additional information (e.g. hop count, received signal strength) is needed in 11p PPDU transmitted by 11bd devices?
Y/N/A

## Slide 9: Straw poll 2
Do you agree to add the following text into 11bd SFD?
  An 11bd STA shall indicate the hop number between the 11bd STA and the legacy device, when transmitting an 11p PPDU with NGV capability.
Y/N/A

## Slide 10: Straw poll 3
Do you agree to add the following text into 11bd SFD?
  An 11bd STA shall indicate the RSSI of the received 11p PPDU, when transmitting an 11p PPDU with NGV capability.
Y/N/A