## Slide 1: Discussion on 6 GHz Band Support
Date: 2019-7-15
Authors:
Name | Company | Address | Phone | Email
Yusuke Tanaka | Sony Corporation |  |  | Yusuke.YT.Tanaka@sony.com
Sho Furuichi |  |  |  | Sho.Furuichi@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com
Ryuichi Hirata |  |  |  | Ryuichi.Hirata@sony.com
Naotaka Sato |  |  |  | naotaka.sato@ieee.org
Chen Sun |  |  |  | Chen.Sun@sony.com
William Carney |  |  |  | William.Carney@sony.com

## Slide 2: Introduction
Frequency range described in IEEE P802.11be PAR includes 6 GHz band [1].
6 GHz band (5,925 – 7,125 MHz (US) / 5,925 – 6,425 MHz (EU)) is now under regulatory discussion to opening up for Wireless Access System including Radio LAN (WAS/RLAN).
This contribution proposes way forward on IEEE P802.11be specification development for 6 GHz band support, assuming regulatory rules proposed as of today is the premise.
  Note that, in the world as of today, FCC is the only national regulatory authority (NRA) which has issued proposed “rule” for shared use of 6 GHz band.
  If the other NRAs propose different rules, we need to consider them also.

## Slide 3: Motivations
Of great benefit to IEEE P802.11be:
  Great contributions to prospective new features such as contiguous 320 MHz bandwidth and Multi-Band Operation and Aggregation using 6 GHz.
  Good path forward to achieve “a maximum throughput of at least 30 Gbps” that is a main scope of TGbe [1].
Reality of 6 GHz availability
  Availability is up to the incumbent system protection requirements
    Primary allocation to other radio systems such as Fixed Systems (FS), Fixed Satellite Systems (FSS) (earth-to-space), i.e. they are incumbent systems.
    Wireless LAN to operate on a secondary basis, i.e. incumbent protection requirements will likely be imposed by national regulatory authorities (not only FCC but also the others).
  Entire 6 GHz band will not necessarily be available to wireless LAN.

## Slide 4: Examples of Proposed Rules to Ensure Incumbent Protection
Notice of Proposed Rulemaking (NPRM) issued by FCC [2]:
  15.403 (b): Automated Frequency Coordination (AFC) is a system that automatically determines and provides lists of which frequencies are available for use by access points operating in the 5.925-6.425 GHz and 6.525-6.875 GHz bands.
  15.407 (d)(3): Operation in the 6.425-6.525 GHz and 6.875-7.125 GHz bands is limited to indoor locations.
  15.407 (k)(1): Access points operating in the 5.925-6.425 GHz and 6.525-6.875 GHz bands shall access an AFC system to determine the available frequencies at their geographic coordinates prior to transmitting. Access points may transmit only on frequencies indicated as being available by an AFC system.
U-NII-5
U-NII
-6
U-NII-7
U-NII-8
5,925
6,425
6,525
6,875
7,125
Freq [MHz]
500 MHz
100 MHz
350 MHz
250 MHz
Database required
Low power and indoor devices only

## Slide 5: Observations on 6 GHz Availability under the Proposed Rules
Only 29% of 6 GHz band is available without database access.
Contiguous 320 MHz is unavailable without database access.
Utilization of Non-contiguous 320 MHz operation is limited.
  A combination of 5 GHz band + U-NII-8 only (e.g. 160 MHz + 160 MHz).
  This will cause congestion in U-NII-8 band, that leads inefficient utilization of U-NII-8 band and non-contiguous 320 MHz operation.

## Slide 6: Consequences for the TGbe Spec Development
TGbe needs to consider and develop a specification to utilize the entirety of the 6 GHz band.
  This is a key requirement to achieve “a maximum throughput of at least 30 Gbps” that is a main scope of TGbe, and also realize “320MHz bandwidth and more efficient utilization of non-contiguous spectrum” that is a candidate technology of TGbe.
If not considered or defined in 11be:
  71% of 6 GHz band cannot be utilized.
  Contiguous 320 MHz operation cannot be supported in 11be.
  Non-contiguous 320 MHz operation will be inefficient.

## Slide 7: TGbe Potential Focus Areas for Complete 6 GHz Band Support
Develop database access (AFC) capability as one of 11be key functionalities.
Development or enhancement of Interface (SAP), Primitive and Entity necessary for database access.
Frame exchange to indicate available channels, maximum allowable transmission power, etc. which are authorized by database.
  Up to the final rules.

## Slide 8: Proposed Way Forward
Reuse of defined functionalities in IEEE 802.11af (WLAN for TVWS, a part of IEEE 802.11-2016 [3]).
  11af = 11n/ac PHY/MAC + Operation under GDB
  11be = new PHY/MAC + Amendment of Operation under GDB
Merits of this approach
  TGbe can develop both 1) the new PHY/MAC and 2) operation under 6 GHz database access in parallel.
  Parallel development of PHY/MAC specification and database amendment accommodates the current regulatory uncertainties and may be faster than creating new database specification from scratch.
  TGbe can continue developing PHY/MAC even if some regulatory authorities do not adopt database access for 6 GHz use.
Note that “new PHY/MAC” here covers any PHY/MAC development to be done by TGbe.

## Slide 9: 802.11af High Level Architecture [3]
Geolocation Database (GDB): A database whose operation is mandated or authorized by a regulatory authority and that organizes storage of information by geographic location.
GDB dependent (GDD) enabling STA: A STA that has the authority to control the operation of GDD dependent STAs after obtaining available spectrum for use at its own location.
.
GDB dependent (GDD) dependent STA: A STA that is under the control of a GDD enabling STA.
For 6GHz support:
§ 15.403 (g) defines that Client Device is generally under the control of an access point.
For 6GHz support:
§ 15.407 (k)(1) requires access points operating in U-NII-5 and 7 to access an AFC system

## Slide 10: 802.11af High Level Architecture [3]
registered location secure server (RLSS): An entity that accesses and manages a database that organizes storage of information by geographic location and securely holds the location and some operating parameters of one or more basic service sets (BSSs)
RLSS can manage one or more GDD enabling STAs.
RLSS can access to GDB on behalf of one or more GDD enabling STAs.

## Slide 11: Observations from the Architecture
AFC can be considered as another form of “GDB”
  employing capability to manage use of 6 GHz band
A definition of “GDD enabling STA” can be re-used for 11be access points to meet FCC’s proposed requirement.
  obtaining available spectrum for use at its own location
A definition of “GDD dependent STA” well matches with the definition of client device.
  generally under the control of GDD enabling STA
“RLSS” can be re-used as network proxy to access AFC on behalf of one or more “GDD enabling STAs”.
  It would be beneficial for professional use such as enterprise network administrators, etc.

## Slide 12: Registered Location Query Protocol (RLQP) [3]
The query protocol for registered location information that is received and transported by generic advertisement service (GAS) Public Action frames.
  Registered location is defined as “the geolocation of a station (STA) registered in accordance with the requirements for the regulatory domain.”
The specific mechanisms are as follows:
  Channel availability query, used to obtain one or more WSMs of available channels for an area or a geolocation
  Channel schedule management, used to obtain start and ending times for each available white space channel
  Contact verification signal, used by a GDD dependent STA to verify it is still receiving frames from its GDD enabling STA
  GDD enablement, the procedure where a GDD enabling STA forms a network and maintains the network under the control of a GDB
  Network channel control, used to inform a local channel controller that has a view of nearby transmitters and their emissions footprints
  WSM (white space map), used to retrieve the available white space channels and their transmit power restrictions
RLQP could also be re-used but how to utilize/modify RLQP for 6 GHz support is for further study.

## Slide 13: Conclusion
To develop functionalities for 6 GHz band support will be a key requirement to achieve “maximum throughput of at least 30 Gbps” that is a main scope of TGbe [1].
TGbe should consider database access as one of these 11be functionalities so that it can globally achieve 30 Gbps where permitted.
TGbe should consider:
  Interface (SAP), Primitive, Entity
  Frame exchange to available channels, maximum allowable transmission power, etc.
  Reuse and enhancement of “Operation under GDB” defined for 11af

## Slide 14: Reference
[1] 11-18-1231-01-0eht-eht-draft-proposed-par
[2] FCC 18-147, “Notice of Proposed Rulemaking”, ET Docket No. 18-295 Unlicensed Use of the 6 GHz Band, October 24, 2018
[3] IEEE Std 802.11™-2016

## Slide 15: Straw Poll 1
Do you think that TGbe may need to consider the NRA proposed rules such as database access requirements and so on to support the entirety of the 6 GHz bands?
  Yes
  No
  Need more information

## Slide 16: Straw Poll 2
Do you think that so-called IEEE 802.11af could be a potential baseline reference for TGbe to develop a database access specification to use 6 GHz band?
  Yes
  No
  Need more information