## Slide 1: Multi-Link Operation: Design Discussion
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-09-17

## Slide 2: Overview
Multi-Link framework to consider the following aspects:
  Aggregation of packets sent on multiple bands/channels concurrently
    Addresses the use-case for improving peak-throughput and reduce latency
  Fast Link Switching
    Seamless transition between different channels/bands to address the use-case for efficient load balancing, coexistence constraints, etc.
  Control/Data separation
    Addresses the use cases for efficient utilization of channel and power-save
EHT should consider a unified framework & signaling to support the above aspects

## Slide 3: Example configurations for MLO
Config 1: Packet-level Agg
Config 2: Flow-level Agg

## Slide 4: Terminology
STA (MAC-PHY instance): There is one STA (MAC/PHY instance) per link
  Each STA has its own per-link MAC/PHY attributes/capabilities
  The MAC address of each STA may be same or different
Multi-Link Logical Entity (MLLE): An MLLE is affiliated with one or more STAs
  An MLLE has an externally addressable unique MAC address which is the MAC-SAP endpoint
  Common BA session, security and SN across all STAs affiliated with an MLLE
MLO-Device: An MLO-Device is a collection of MLLEs
  An MLO-Device may have multiple MAC-SAP endpoints
  Enables common mgmt. signaling across all MLLEs for power-save reasons

## Slide 5: Definition
Propose adding new definitions as follows:
  multi-link operation (MLO) entity: A logical entity that has one or more affiliated STAs and has a singly addressable MAC-SAP endpoint.
  multi-link operation (MLO) device: A logical entity that enables common management signaling between a collection of one or more multi-link logical entities

## Slide 6: Packet-level agg. hi-level architecture
Common upper MAC
  Single-link interface to higher layer
  Common sequence # space and BA scoreboard
    Retransmissions need not be on the same link
  Increase BA Bitmap length to account for increase in peak throughput
  Management
    Single association (on ‘home’ channel)
      A STA that is idle monitors only the home channel
    Dynamically signal expansion to additional links
Independent lower MAC/PHY instances
  Each link has a MAC instance that performs link specific functionality independently
    e.g., EDCA, CCA, sounding, etc
Common Rx Q
Lower Tx MAC 1
1
…
9
Link 1
Link 2
Lower Tx MAC 2
MSDU/AMSDU from a TID
1
9
Common Tx Q
+ Common Seq #
…
Lower Rx MAC 1
Lower Rx MAC 2
Attach common SN
SN + (A)MSDU
SN + (A)MSDU
MPDU
generation
MPDU
generation

## Slide 7: Multi-link aggregation schemes
Option 1: Independent MLA
  Independent channel access and PPDU transmit parameters on each link
  Independent PPDU
    Independent Tx parameters for PPDUs on each link
    PPDU size, start and end times need not be the same
Option 2: Simultaneous MLA
  Channel access through primary channel
    Dynamic non-contiguous BW
  PPDU Tx on other link(s) based on secondary channel rules
    ED @ -72dBm
  Simultaneous PPDU
    Independent Tx parameters for PPDUs on each link
    PPDU size, start and end times are the same
Both schemes are being considered for EHT
* Doc 11-19/0764 looks at the gain with the two schemes

## Slide 8: Summary
The contribution
  Provides definitions to various elements for multi-link operation
  Introduces an architecture which provides a unified solution for addressing aggregation, link availability and power management
    Common MAC-SAP to higher layers
    Common seq# space and BA scoreboard
    Single association

## Slide 9: Straw Poll 1
Do you support that the 802.11be amendment shall add a new definitions as follows:
  multi-link operation (MLO) device: A logical entity that enables common management signaling between a collection of one or more Multi-Link Logical Entities (MLLEs)
    Note – the exact name can be changed later
  Y: 36
  N: 21
  A: 57

## Slide 10: Appendix

## Slide 11: Definitions in current spec
station (STA): A logical entity that is a singly addressable instance of a medium access control (MAC) and physical layer (PHY) interface to the wireless medium (WM).
link: In the context of an IEEE 802.11 medium access control (MAC) entity, a physical path consisting of exactly one traversal of the wireless medium (WM) that is usable to transfer MAC service data units (MSDUs) between two stations (STAs).