## Slide 1: TGba Possible Architecture and Specification Issues
Date: 2019-05-12
Authors:

## Slide 2: Abstract
This presentation attempts to provide a discussion on some possible specification technical issues in 802.11ba D2.0 that are the result of changes made to the draft when the concept of WURx and PCR were removed and WUR functionality was defined as a mode of an AP and non-AP STA.

## Slide 3: There are 3 basic concepts that need review/draft edits
Multi-Channel operation of WUR AP and non-AP STA is not defined
  STA/AP pairs operate on a Single Channel
  DFS in the 5 GHz - precludes WUR PPDUs transmission
Now that WUR functionality is a mode of the STA, it must be defined:
  The allowed states of the STA needs to be clearly specified
  How a STA goes into and out of its allowed states must be specified
  The properties of the STA in each defined state must be specified
Now that the transmission of WUR PPDUs is a capability of an AP
  The type of WUR PPDUs that can be transmitted need to be clearly specified
  When a WUR PPDU shall/may be transmitted must be specified

## Slide 4: (1) A STA/AP operate on a Single Channel
The change in .11ba architecture from multiple devices (AP, PCR, WURx) to simply an AP and non-AP STA with a WUR mode restricts multi-band operation specification. Therefore:
A non-AP STA associated with a AP have a single defined channel of operation. Throughout the 802.11 spec all transmission are assumed to be on the channel used when the non-AP STA associates with the AP. (WUR PPDUs can only be transmitted on this channel.)
The only allowed multi-band operation is described in 11.32 [1], which allows for multi-band operation when a device contains multiple STAs.
A device can have multiple STAs, but how these STAs behave need to be defined, I cannot find discussion/requirements for the behavior in the draft (P802.11ba D2.0).
If .11ba intends to allow for multiband operation – changes/additions should be made. (To 11.32 or the multiband operation should be described in 30.)

## Slide 5: Potential Issues of WUR in DFS 5GHz Band
Transmission of WUR PPDUs will confuse DFS receivers.
The current 802.11ba draft does not allow for WUR operation in the DFS bands.
Since multiband operation is not defined in the specification, WUR operation can only be on a few 5GHz channels (non-DFS).
And since a non-AP STA associated with a AP have a single defined channel of operation
WUR usefulness in the 5GHz band is very limited.

## Slide 6: (2) The STA and its State
A STA is a logical entity that has a state.
  “station (STA): A logical entity that is a singly addressable instance of a medium access control (MAC) and physical layer (PHY) interface to the wireless medium (WM).”[1]
  “state: condition or mode of existence that a system, component, or simulation can be in” [2]
Hence a STA is only in one state at any given time
  There are not two parts to a STA, hence a WUR non-AP STA is a single entity and has a single State.
e.g. when a non-AP WUR STA is in WUR awake state it:
  can only receive WUR PPDUs on the WUR channel configured by the frame exchange that defined the WUR mode for the STA.
  is not also in any other state, e.g. doze (a well defined PS state with different properties)

## Slide 7: (2) State Changes
It is critical that the P802.11 and its amendments clearly define:
  The properties of the various states that 802.11 entities (AP or STA) can be in.
  The methods used to change the state of an 802.11 entity:
    Providing the sequence of events (frame exchanges, timers, measurements, etc.)
    When the changes in state occur or may occur
Possible issues with the current 802.11ba draft:
  There seems to be a mixing or nesting of PS and WUR states: e.g. “wake-up radio (WUR) mode: A negotiation status between a WUR AP and a WUR non-AP STA such that the WUR non-AP STA alternates between the WUR awake state and the WUR doze state when the WUR non-AP STA is in the doze state.” – this nesting is also present in other areas of the specification.
  The procedure for triggering the start of a WUR awake/doze schedule, does not seem to be defined.
    I have been told that the STA is assumed to start its WUR awake/doze schedule upon the competition of a WUR setup frame exchange defining the WUR mode (This seems to be buried in Table 30-1, assuming the phrase “enters WUR mode” means the STA is assumed to follow its WUR awake/doze schedule.)
    I have also been told that the STA with a defined WUR mode (one that has completed the WUR setup frame exchange) triggers the start of the WUR awake/doze schedule by sending a frame with the PS bit set to 1. (I can’t find this in the current draft, except for the use of “doze state” above.)

## Slide 8: (2) State Changes (cont.)
If the STA is assumed to start its WUR awake/doze schedule upon the completion of a WUR setup frame exchange defining the WUR mode:
  The need for WUR mode suspend capability is probably no longer necessary. As procedure for triggering WUR mode would provide all the require configuration information to be exchanged by the WUR non-AP STA and WUR AP to trigger the mode. Therefore there is no need to remember the WUR parameters with WUR mode suspend.
  Note that if WUR mode is triggered by the setup frame exchange then it is independent of PS mode.
If the STA with a defined WUR mode is assumed to be trigger to start its WUR awake/doze schedule by sending a frame with the PS bit set to 1:
  This needs to be clearly specified
  I have a hard time understanding why WUR isn’t simply a new Power Save mode. As, any mode that uses the PS bit to trigger its behavior and saves power should be considered a Power Save mode.
  If WUR mode is activated by setting the PS bit, then the WUR mode suspend has purpose.
  If WUR is a Power Save mode, why does it need a MAC clause?

## Slide 9
Figure 11-12
State Transition diagram of non-AP and non-PCP STAT in active and PS modes
From [1]

## Slide 10: WUR STA State Diagram Assuming WUR frame Exchange Trigger
Scheduled PS mode
Active mode
Unscheduled PS mode
Scheduled / Unscheduled PS mode
WUR mode
WUR Mode can be triggered from any PS state, WUR wakeup would return to that PS state.

## Slide 11: WUR STA State Diagram Assuming PS Bit Trigger
Scheduled PS mode
Active mode
Unscheduled PS mode
Scheduled / Unscheduled PS mode
WUR mode
WUR Mode is triggered by the PS bit – as PS modes are. WUR wakeup to Active mode.

## Slide 12: References
Draft P802.11REVmd_D2.0
24765-2017 - ISO/IEC/IEEE International Standard - Systems and software engineering—Vocabulary