## Slide 1: TGbb MAC Channel Access features proposal
Date: April 24, 2019
Authors:

## Slide 2
The presentation also provides the review of Multi-User (MU) operations in 802.11ax and suggestion on the modifications of channel access for TGbb.
Abstract

## Slide 3: Background on Channel Access in 802.11ax

## Slide 4: HCF in 802.11ax
HCF consists of HCCA(with centralised controller) and EDCA(ad-hoc).
HCCA is not used in 802.11ax STAs.
Contention exists in:
  UL MU operation, UORA, DL MU operation, and non-UORA STAs
  Inside UORA

## Slide 5: Top level contention
DL MU operation, UL MU operation, UORA, and non-UORA STAs all compete on the WM based on EDCA.
A STA that does not support UORA can contend for the WM using EDCA for sending UL frames to the AP with which it intends to communicate.
DL MU operation
UL MU operation
UORA
Non-UORA STA
Backoff
Backoff
Backoff
Non-UORA STA

## Slide 6: Illustrations for MU operations in IEEE P802.11ax

## Slide 7: DL MU operation (1)
One to many transmission
HE MU PPDU to STA 1
HE MU PPDU to STA 2
HE MU PPDU to STA n
HE TB PPDU to ACK AP by STA 1
HE TB PPDU to ACK AP by STA 2
HE TB PPDU to ACK AP by STA n
Backoff
SIFS
…
…
…
Padding

## Slide 8: RU allocation
The HE-SIG-B field provides the OFDMA and DL MU-MIMO resource allocation information to allow the STAs to look up the corresponding resources to be used in the data portion of the frame.
User Field 1
User Field 2
STA ID
NSTS
Tx beamforming
MCS
DCM
coding
Bit-loading can be supported with minor changes.
One STA is not allowed to be allocated with multiple RUs in User Specific field. Up to one User field per STA.
Notes: The User Specific field of an HE-SIG-B content channel consists of zero or more User Block fields followed by padding (if present). Each User Block field is made up of two User fields that contain information for two STAs to decode their payloads. The last User Block field may contain information for one or two STAs depending on the number of users indicated by the RU Allocation field and the Center 26-tone RU field.

## Slide 9: DL MU operation (2) – with MU-RTS/CTS
Early detection of failure

## Slide 10: PROPOSAL: Modified DL MU operation
HE MU PPDU to STA 1
HE MU PPDU to STA 2
HE MU PPDU to STA n
HE TB PPDU to ACK AP by STA 1
HE TB PPDU to ACK AP by STA 2
HE TB PPDU to ACK AP by STA n
Backoff
SIFS
…
…
…
Padding
HE MU PPDU to STA 2
HE TB PPDU to ACK AP by STA 2
Allow STA to be allocated with multiple RUs in each cycle of the DL MU operation.

## Slide 11: PROPOSAL: DL MU operation
To enable bit-loading on DL in TGbb using 11ax as a basis:
  The modification needs to allow multiple User Specific fields to be added for the same STA in HE-SIG-B.
  Revise the following text in IEEE P802.11axD3.0 to support bit-loading:
    L13-17pp488, 28.3.10.8.5, ‘The RU Allocation field in the Common filed and the position of the User field in the User Specific field together identify the RU used to transmit a STA’s date. Multiple RUs addressed to a single STA shall not be allowed in the User Specific field. Therefore, the signaling that enables STAs to decode their data is carried in only one User field. ’
The sentence has been removed in IEEE 802.11ax D8.0.

## Slide 12: UL MU operation (1)
Dedicated allocation for all selected STAs
Multi‐STA BlockAck

## Slide 13: UL MU operation (2)
Trigger frame
One selected STA, one RU allocated, one MCS selected.
Bit-loading can be supported with minor changes.

## Slide 14: PROPOSAL: UL MU operation (3)
To enable bit-loading in TGbb using 11ax as a basis:
  Set the bit for ‘CS Required’ subfield in the ‘Common Info’ field of Trigger Frame as ‘0’, in order to disable the requirement of channel sensing before sending TB PPDU response.
  Revise the following text in IEEE P802.11axD8.0 to support bit-loading:
    L51-52pp286, 27.5.3.3, ‘The received PPDU contains either a Trigger frame (that is not an MU-RTS variant) with a User Info field addressed to the STA, ’
    L28-29 pp376, 26.5.2.3.1, ‘A non-AP STA addressed by a User Info field in a Trigger frame (i.e., the AID12 subfield is equal to the 12 LSBs of the AID of the non-AP STA) may ignore the remainder of User Info fields in the Trigger frame.’
    L65 pp383, 26.5.2.5, ‘The CS Required subfield in the MU-RTS Trigger frame shall be set to 1. ’
    L55-56 pp373, 26.5.2.2.4, ‘An AP shall not transmit a Trigger frame that contains more than one User Info field with the same value in the AID12 subfield unless the value in the AID12 subfield is 0 or greater than 2007.’
    See the rest changes in doc.11-21/0545r2.
With the Relayed CCA mechanism added to the TGbb, the modification is no longer needed.

## Slide 15: UL MU operation (4) – with MU-RTS/CTS
Dedicated allocation for all selected STAs; early detection of failure

## Slide 16: UORA (UL OFDMA-based Random Access)
No dedicated resource allocation for all STAs
Eligible STAs with OBO counter number (<= Available RUs for AID0/2045) compete for RA-RUs
Random selection of AID0/2045 RUs causes collisions
No knowledge after/if others selected any AID0/2045 RUs

## Slide 17: PROPOSAL: Summary of changes for RA
Do not use UORA (UL OFDMA-based Random Access) in TGbb
  In the use cases of TGbb, no such frequent change in terms of existence is expected as in IEEE P802.11ax.
  The UORA is designed to serve large amount of users, which is also not the case in TGbb.
Reserve a RU (Resource Unit) for random access in UL MU operation
  STAs know where to do RA.
  Benefits will also include fewer wasted resources, fewer collisions, fewer retransmissions.

## Slide 18: PROPOSAL: Modified UL MU operation
Multi-STA BlockAck
Backoff
AID 3,
RU 5
AID 9,
RU 4
AID 4,
RU 2
AID 4,
RU 3
AID 0,
RU 1
AID 3,
RU 6
Trigger frame
SIFS
HE TB PPDU from STA of AID 3
HE TB PPDU from STA of AID 9
HE TB PPDU from STA of AID 4
HE TB PPDU from STA of AID 4
RU 1 is reserved for Random Access
HE TB PPDU from STA of AID 3
SIFS
Frequency
Time

## Slide 19: PROPOSAL: Technical details
UORA (26.5.4 in IEEE P802.11axD8.0) may be disabled due to the low efficiency of resource allocation
Random access is introduced in UL MU operation (26.5.2 in IEEE P802.11axD8.0)
  In each Trigger frame sent by the AP in UL MU operation, the RU1 is reserved for random access.
  Different APs may reserve different RUs for random access in order to avoid collisions from OBSS. This could be considered in the future implementation.

## Slide 20: List of related clauses/sub-clauses
IEEE P802.11axD8.0
  DL MU operation (26.5.1)
  UL MU operation (26.5.2)
  MU-RTS/CTS procedure (26.2.6)
  UORA (26.5.4)
  Trigger frame (9.3.1.22)