## Slide 1: NGV PPDU with Hierarchical MCS
Date: 2019-05-13
Authors:

## Slide 2: Abstract
This contribution proposes a new NGV PPDU, compatible with WAVE PPDU, enabling spectral efficient way to communicate with WAVE and NGV capable devices simultaneously using hierarchical MCS.
Other kind of NGV PPDU, where WAVE and NGV payloads are concatenated in time, is discussed in [1]

## Slide 3: Multiplexing with Hierarchical MCS
Hierarchical MCS is a technology used for example in various DVB standards [2]
The basic idea is to have two independent streams, called basic and additional layer, transmitted at the same time, each coded with different modulations
In DVB, it can mean that the transmission includes SD level video encoded with 16QAM modulation and HD video using 256QAM.

## Slide 4: WAVE and NGV layers
WAVE receiver can decode only the basic (WAVE-) layer, NGV receiver can decode the both layers, basic (WAVE-) layer and additional (NGV-) layer, depending on the SINR
We preferably need a mechanism to indicate NGV layer existence to NGV devices e.g. by reusing some WAVE header bit
MCS used in NGV layer can be derived from WAVE MCS (e.g. if WAVE layer is modulated with QPSK then NGV is with 64QAM) if there is no reusable bits to spare for this purpose
WAVE stream bits
NGV stream bits
802.11bd
MAC
802.11bd
PHY
802.11bd
MAC
802.11bd
PHY
802.11p
MAC
802.11p
PHY
BSM-1 MCS-x
BSM-2 MCS-y
BSM-1
BSM-2
BSM-1
Hierarchical multiplexing
BSM-1 on WAVE layer
BSM-2 on NGV layer
Both layers
received
Only WAVE
Layer received
BSM: Basic Safety Message

## Slide 5: Proposal
We propose a new type of NGV PPDU that is compatible with WAVE PPDU
Comparing NGV PPDU that multiplexes WAVE+NGV payloads concatenated in time versus with use of hierarchical MCS, the main advantage is simultaneous transmission of the payloads and the main disadvantage is inter-layer interference requiring better SINR
We believe that both multiplexing methods (concatenated in time and hierarchical MCS) would be beneficial to be specified in TGbd allowing upper layers to do the trade-off between spectral efficiency and reliability

## Slide 6: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-0082-02-00bd-interoperable-approach-for-ngv-new-modulations.pptx
[2] https://www.etsi.org/deliver/etsi_tr/102300_102399/102377/01.04.01_60/tr_102377v010401p.pdf