## Slide 1: Multi-band comments resolution
Date: 2019-01-15
Name | Affiliation | Address | Phone | Email
Mohamed Abouelseoud | Sony | 1730 N. First Street, San Jose CA 95112 |  | Mohamed.Abouelseoud(at)sony.com
Kazuyuki Sakoda |  |  |  | kazuyuki.sakoda(at)sony.com

## Slide 2
CID | PP.LL | Comment | Proposed Change
4233 | 11.31.6 | As pointed out by CID3518, the current draft standard lacks a tool for the distribution network bootstrapping, particularly when applications are expecting low latency communication. DMG discovery assistance should enable neighbor DMG/EDMG STA discovery beyond an AP to ease implementation of the distribution network leveraging 802.11ay. In particular, the standard should provide a tool for the AP that serves discovery assistance to propagate discovery assistance request to neighbor STAs. | Add a container that allows AP to transmit discovery assistance request to STAs in the BSS. Also, allow AP to propagate the discovery assistance request.
4306 | 11.32.6 | Multi-band discovery assistance allows discovery of an AP or PCP that this STA is connected to however this is not enough. For some use cases, the STA might need to talk to a non-AP/PCP STAs in the same BSS or even in other BSSs . A STA should find other non-AP in that BSS and other BSS | The standard should define a mechanism to allow new STA to find neighbor STAs in an on-demand fashion. Commenter is willing to provide resolution text.

## Slide 3: Discovery assistance request propagation
New STA establish a link to AP on lower band
New STA sends discovery assistance request to AP on lower band
Multi-band Discovery Assistance Procedure
FST Setup Request frame with DMG Discovery Assistance & DMG Capabilities elements
Established sub-6GHz link
(1) Discovery Asst. Req
Established mmW link
STA1
PCP 1
Multi-band capable AP
AP
New STA
Multi-band capable STA
Lower band signal
mmW band signal

## Slide 4: Discovery assistance request propagation
AP propagates the DMG discovery assistance request to STA 1 on mmW band
STA 1 responds to AP with DMG discovery assistance response if it supports discovery assistance on mmW band
Response include:
  Discovery assistance response (accept/reject)
  PCP1 start time of discovery assistance
  Discovery assistance window length
  MAC address of PCP 1
Information Request frame with DMG Discovery Assistance & DMG Capabilities elements
Information Response frame with DMG Discovery Assistance element
Established sub-6GHz link
(1) Discovery Asst. Req
Established mmW link
(2) Discovery Asst. Req.
(3) Discovery Asst. Resp.
STA1
PCP 1
Multi-band capable AP
AP
New STA
Multi-band capable STA
Lower band signal
mmW band signal

## Slide 5: Discovery assistance request propagation
AP responds to new STA with DMG discovery assistance response on lower band
Response includes:
  Discovery assistance response (accept/reject)
  MAC address of AP and PCP 1
  Start time of the discovery assistance (including AP and PCP1)
  Discovery assistance window length (including AP and PCP1)
Multi-band Discovery Assistance Procedure
FST Setup Response frame with DMG Discovery Assistance element
(4) Discovery Asst. Resp
Established sub-6GHz link
(1) Discovery Asst. Req
Established mmW link
(2) Discovery Asst. Req.
(3) Discovery Asst. Resp.
STA1
PCP 1
Multi-band capable AP
AP
New STA
Multi-band capable STA
Lower band signal
mmW band signal

## Slide 6: Discovery assistance request propagation
Potential mmW link
Potential mmW link
mmW SSW
mmW SSW
Established mmW link
STA1
PCP 1
Multi-band capable AP
AP
New STA
Multi-band capable STA
AP and PCP 1 start SSW on mmW band at the advertised time
New STA can form mmW link with the STA in range
Lower band signal
mmW band signal

## Slide 7: How to propagate discovery assistance request
Use the Information Request and Response frame to propagate the DMG Discovery Assistance element from the STA requesting discovery assistance to other STAs
AP processes the responses and sends one response to the STA requesting discovery assistance ( FST Setup Response frame)

## Slide 8: DMG discovery assistance request
New STA DMG Capabilities element
DMG Discovery Assistance element
Information Request frame
Element ID
Length
Discovery Assistance Control
Element ID Extension
Discovery Assistance Window Length
Sector Sweep Start Time (optional)
Discovery Assistance Request Status Code
Number of STAs Providing Discovery Assistance

## Slide 9: DMG Discovery assistance response
DMG Discovery Assistance element
Information Response frame
Element ID
Length
Discovery Assistance Control
Element ID Extension
Discovery Assistance Window Length
Sector Sweep Start Time
Discovery Assistance Request Status Code
Number of STAs Providing Discovery Assistance
MAC Address of STA 1

## Slide 10: Discovery assistance response to new STA
AP sets the discovery assistance response to the new STA as follows:
  Add the MAC Addresses of STAs providing discovery assistance
  Send the discovery assistance campaign allocation as one of these options:
    Send the earliest SSW start time of all STAs in the discovery campaign and the period of time where the discovery campaign is active; or
    Send the Extended Schedule element
* Details in document 0879r0

## Slide 11: Multi-band Discovery assistance response
DMG Discovery Assistance element
FST Setup Response frame
Element ID
Length
Discovery Assistance Control
Element ID Extension
Discovery Assistance Window Length
Sector Sweep Start Time (optional)
Discovery Assistance Request Status Code
Temporary AID (optional)
Dwelling Time (optional)
Number of STAs Providing Discovery Assistance
MAC Address of STA 1
…
MAC Address of STA N
Other optional elements

## Slide 12: Straw Poll
Do you support the proposed resolution of CIDs 4233,4306?
  Yes
  No
  Abstain