## Slide 1: HARQ Framing
Date: 2019-05-13
Authors:
Name | Affiliation | Address | Email
Imran Latif | Quantenna Communications | 1704 Automation Parkway, 95131, San Jose, CA, USA | ilatif@quantenna.com
Sigurd Schelstraete |  |  | sschelstraete@quantenna.com
Debashis Dash |  |  | ddash@quantenna.com
Huizhao Wang |  |  | hwang@quantenna.com
Ambroise Popper |  |  | apopper@quantenna.com

## Slide 2: Background
Hybrid-ARQ is one of the candidate topics for TGbe
HARQ presentations in previous meetings show clear interest [1] – [9]
HARQ has been proposed for previous 802.11 standards
However, it has never been successful in securing its place in 802.11 standard despite its promised gains
We believe it can have its chances with TGbe
Therefore, we would like to go beyond showing results and discuss how HARQ can be enabled through framing support

## Slide 3: HARQ Framing
In this presentation we stress on the fact that we need to present HARQ framing
To enable HARQ, MPDU and/or codeword related information is required at PHY level on both Tx and Rx side
At Tx Side:
  Tx needs to send the information about HARQ related parameters for each MPDU/codeword at the PHY level by encoding the PHY level HARQ control signal.
  It is essential to decode HARQ-SIG in order to be able to decode the DATA portion of the received packet.
  At a minimum HARQ SIG needs a unique identifier for the MPDUs/Codeword contained in the DATA(retransmission or not)
L-STF
L-LTF
L-SIG
…
HARQ-SIG
DATA
Legacy Preamble
HARQ Control Information

## Slide 4: HARQ Framing
At Rx Side:
  Rx obtains the information about HARQ related parameters at the PHY level by decoding the PHY level HARQ control signal which is essential for HARQ operation in the following DATA portion of the received packet.
  There is no CRC at the PHY level.
  So how do we get the decoding status of each codeword?
  One way is to check the status of decoded codeword with LDPC parity check matrix at PHY level.
  PHY can provide error information on per codeword basis
  MAC can provide CRC information on MPDU level
  Finally Rx needs to send the feedback to Tx about the wrongly decoded codewords/MPDUs.

## Slide 5: Dual Feedback
For the feedback there can be two options, codeword level and/or MPDU level
It should be able to send the feedback not only based on MPDU level bitmap but also with the codeword level information either appended to the existing BA or creating a new additional acknowledgement packet for codeword information.
This information can be kept at PHY for indexing and keeping codewords/MPDUs in its memory for recombination on receiving re-transmissions.
BA bit mask
Codeword level Feedback

## Slide 6: Summary
We have discussed the Framing for HARQ
We presented a new PHY level signaling enabling HARQ at both Tx and Rx
We have also discussed the feedback options for HARQ
We proposed the dual granularity of doing feedback based on either the MPDU or both MDPU and Codeword.
Notes: MAC level protp

## Slide 7: Reference
[1] Shimi Shilo – HARQ for EHT (DCN:1587) – 13 Sep 2018
[2] Ron Porat – Multi-AP-HARQ-for-EHT (DCN: 1116) – 6 July 2018
[3] Bo Sun - Discussion on HARQ for EHT (DCN: 1963) – 11 Nov 2018
[4] Tianyu Wu – HARQ performance analysis (DCN: 1979) – 11 Nov 2018
[5] Hongyuan Zhang – HARQ Feasibility (DCN: 1992) – 11 Nov 2018
[6] Sindhu Verma – HARQ gain studies (DCN: 2031) – 13 Nov 2018
[7] Bo Sun - Discussion on HARQ for EHT (DCN: 1963) – 28 Nov 2018
[8] Jinmin Kim – Consideration on HARQ (DCN: 354) – 07 Mar 2019
[9] Kome Oteri - Effect of Preamble Decoding on HARQ in 802.11be (DCN: 390) – 09 March 2019