## Slide 1: Channelization for 6 GHz (CID 21378)
Date: 2019-05-13
Authors:
Name | Affiliation | Address | Email
Imran Latif | Quantenna Communications | 1704 Automation Parkway, 95131, San Jose, CA, USA | ilatif@quantenna.com
Sigurd Schelstraete |  |  | sschelstraete@quantenna.com
Debashis Dash |  |  | ddash@quantenna.com
Huizhao Wang |  |  | hwang@quantenna.com

## Slide 2: CID 21378

## Slide 3: Background
FCC has issued first Notice for Proposed Rulemaking (NPRM) for opening the 6 GHz band for unlicensed use.
In proposed NPRM, FCC has announced to open band from 5925 MHz to 7125 MHz – 1200 MHz
IEEE has divided this 1200 MHz band into 4 sub-bands,
  U-NII-5 (500 MHz under AFC)
  U-NII-6 (100 MHz – Low Power Unlicensed Devices)
  U-NII-7 (350 MHz under AFC)
  U-NII-8 (250 MHz – Low Power Unlicensed Devices)
11ax supports operation in the 6 GHz band

## Slide 4: Channel Allocation in the 6 GHz in 11ax
11ax D4.0 Section 27.3.22.2 defines the channel allocation in the 6 GHz band as,
This channelization does not take OOB emissions in to account;
  The channel starting frequency, 5940 MHz, leaves only 10 MHz of guard band between U-NII-4 and U-NII-5 band

## Slide 5: Channel Allocation in the 6 GHz in 11ax1
Starting frequency of 5940 MHz
  Only 10 MHz of Guard band for U-NII-5
  Challenging filter design
Channels can cross U-NII boundaries
In case U-NII-5 and 6 work under different regulatory rules
  No 80 MHz channel in U-NII-6
  Only one 40 MHz channel in U-NII-6
1 – Channel numbers in this Figure are shown as a continuation of 5GHz channel numbers.
U-NII-5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-6 |  |  |  |  |  |  |  |  |  | U-NII-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 5945 |  | 5965 |  | 5985 |  | 6005 |  | 6025 |  | 6045 |  | 6065 |  | 6085 |  | 6105 |  | 6125 |  | 6145 |  | 6165 |  | 6185 |  | 6205 |  | 6225 |  | 6245 |  | 6065 |  | 6285 |  | 6305 |  | 6325 |  | 6345 |  | 6365 |  | 6385 |  | 6405 |  | 6425 |  | 6445 |  | 6465 |  | 6485 |  | 6505 |  | 6525 |  | 6545 |  | 6565 |  | 6585 |  | 6605 |  | 6625 |  | 6645 |  | 6665 |  | 6685 |  | 6705 |  | 6725 |  | 6745 |  | 6765 |  | 6785 |  | 6805 |  | 6825 |  | 6845 |  | 6865 |  | 6885 |  | 6905 |  | 6925 |  | 6945 |  | 6965 |  | 6985 |  | 7005 |  | 7025 |  | 7045 |  | 7065 |  | 7085 |  | 7105 |  | 7125 | 
 | 189 |  | 193 |  | 197 |  | 201 |  | 205 |  | 209 |  | 213 |  | 217 |  | 221 |  | 225 |  | 229 |  | 233 |  | 237 |  | 241 |  | 245 |  | 249 |  | 213 |  | 257 |  | 261 |  | 265 |  | 269 |  | 273 |  | 277 |  | 281 |  | 285 |  | 289 |  | 293 |  | 297 |  | 301 |  | 305 |  | 309 |  | 313 |  | 317 |  | 321 |  | 325 |  | 329 |  | 333 |  | 337 |  | 341 |  | 345 |  | 349 |  | 353 |  | 357 |  | 361 |  | 365 |  | 369 |  | 373 |  | 377 |  | 381 |  | 385 |  | 389 |  | 393 |  | 397 |  | 401 |  | 405 |  | 409 |  | 413 |  | 417 |  | 421 |  |  | 
 | 191 |  |  |  | 199 |  |  |  | 207 |  |  |  | 215 |  |  |  | 223 |  |  |  | 231 |  |  |  | 239 |  |  |  | 247 |  |  |  | 215 |  |  |  | 263 |  |  |  | 271 |  |  |  | 279 |  |  |  | 287 |  |  |  | 295 |  |  |  | 303 |  |  |  | 311 |  |  |  | 319 |  |  |  | 327 |  |  |  | 335 |  |  |  | 343 |  |  |  | 351 |  |  |  | 359 |  |  |  | 367 |  |  |  | 375 |  |  |  | 383 |  |  |  | 391 |  |  |  | 399 |  |  |  | 407 |  |  |  | 415 |  |  |  |  |  |  | 
 | 195 |  |  |  |  |  |  |  | 211 |  |  |  |  |  |  |  | 227 |  |  |  |  |  |  |  | 243 |  |  |  |  |  |  |  | 259 |  |  |  |  |  |  |  | 275 |  |  |  |  |  |  |  | 291 |  |  |  |  |  |  |  | 307 |  |  |  |  |  |  |  | 323 |  |  |  |  |  |  |  | 339 |  |  |  |  |  |  |  | 355 |  |  |  |  |  |  |  | 371 |  |  |  |  |  |  |  | 387 |  |  |  |  |  |  |  | 403 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 203 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 235 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 267 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 299 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 331 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 363 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 395 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Center Frequency [MHz]
20 MHz Channels
40 MHz Channels
80 MHz Channels
160 MHz Channels

## Slide 6: OOBE limits and 10 MHz Guard Band
Based on FCC’s proposed rules in NPRM1, OOBE limits mask is shown here
It can be seen that U-NII-5 OOBE limit is quite strict and to meet it around the edges of U-NII-5 band we would have to either,
  Increase the guard band, i.e., sacrifice few MHz (more than 10 MHz endangers 160 MHz channel)
  Or reduce the transmit power by at least 10dB to meet this requirement
  Or have a relaxed OOBE limits on the U-NII-5 which are similar to the U-NII-3 - FCC
1 all emissions below 5.925 GHz and above 7.125 GHz shall not exceed an EIRP of -27 dBm/MHz
Chart: NPRM based FCC U-NII 3, 5 bands OOBE Masks
| 5600 | 5650 | 5700 | 5720 | 5725 | 5725.01 | 5849.99 | 5850 | 5855 | 5875 | 5925 | 5975
 | -27 | -27 | 10 | 15.6 | 27 | 57 | 57 | 27 | 15.6 | 10 | -27 | -27
 | -27 | -27 | 17 | 17

## Slide 7: Channel Allocation in 5 GHz - FCC
U-NII-1 |  |  |  |  |  |  |  |  | U-NII-2A |  |  |  |  |  |  |  |  |  | U-NII-2C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 5180 |  | 5200 |  | 5220 |  | 5240 |  | 5260 |  | 5280 |  | 5300 |  | 5320 |  |  |  |  | 5500 |  | 5520 |  | 5540 |  |  | 5560 |  | 5580 |  | 5600 |  | 5620 |  | 5640 |  | 5660 |  | 5680 |  | 5700 |  | 5720 | 
 | 36 |  | 40 |  | 44 |  | 48 |  | 52 |  | 56 |  | 60 |  | 64 |  |  |  |  | 100 |  | 104 |  | 108 |  |  | 112 |  | 116 |  | 120 |  | 124 |  | 128 |  | 132 |  | 136 |  | 140 |  | 144 | 
 | 38 |  |  |  | 46 |  |  |  | 54 |  |  |  | 62 |  |  |  |  |  |  | 102 |  |  |  | 110 |  |  |  |  | 118 |  |  |  | 126 |  |  |  | 134 |  |  |  | 142 |  |  | 
 | 42 |  |  |  |  |  |  |  | 58 |  |  |  |  |  |  |  |  |  |  | 106 |  |  |  |  |  |  |  |  | 122 |  |  |  |  |  |  |  | 138 |  |  |  |  |  |  | 
 | 50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 114 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
U-NII-3 |  |  |  |  |  |  |  |  |  |  | 
 | 5745 |  | 5765 |  | 5785 |  | 5805 |  | 5825 |  | 
 | 149 |  | 153 |  | 157 |  | 161 |  | 165 |  | 
 | 151 |  |  |  | 159 |  |  |  |  |  | 
 | 155 |  |  |  |  |  |  |  |  |  | 
20 MHz Gap
Guard band allocation is not universal among all U-NII bands
20 MHz guard exists for U-NII-1
Does strict OOBE require larger guard band?
Only U-NII-3 has a different OOBE requirement
5 MHz Gap
20 MHz Gap
15 MHz Gap

## Slide 8: Proposed Channel Allocation in the 6 GHz in 11ax
Shifting the starting frequency from 5940 to 5950 MHz provides 20 MHz of Guard band and,
  More relaxed filter design
  Similar to the U-NII-1 band
  One complete 80 MHz channel in the U-NII-6 band
  Two 40 MHz channels in the U-NII-6 band
  The U-NII-5 band still has three 160 MHz channels
Note: In Europe 6 GHz band ends at 6425 MHz and shifting the channel by 10 MHz can impact the filter design on the higher end of the 6 GHz band in order to meet the European OOBE limits.
U-NII-5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-6 |  |  |  |  |  |  |  |  |  | U-NII-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5935 |  | 5955 |  | 5975 |  | 5995 |  | 6015 |  | 6035 |  | 6055 |  | 6075 |  | 6095 |  | 6115 |  | 6135 |  | 6155 |  | 6175 |  | 6195 |  | 6215 |  | 6235 |  | 6255 |  | 6075 |  | 6295 |  | 6315 |  | 6335 |  | 6355 |  | 6375 |  | 6395 |  | 6415 |  | 6435 |  | 6455 |  | 6475 |  | 6495 |  | 6515 |  | 6535 |  | 6555 |  | 6575 |  | 6595 |  | 6615 |  | 6635 |  | 6655 |  | 6675 |  | 6695 |  | 6715 |  | 6735 |  | 6755 |  | 6775 |  | 6795 |  | 6815 |  | 6835 |  | 6855 |  | 6875 |  | 6895 |  | 6915 |  | 6935 |  | 6955 |  | 6975 |  | 6995 |  | 7015 |  | 7035 |  | 7055 |  | 7075 |  | 7095 |  | 7115 |  | 
 |  | 191 |  | 195 |  | 199 |  | 203 |  | 207 |  | 211 |  | 215 |  | 219 |  | 223 |  | 227 |  | 231 |  | 235 |  | 239 |  | 243 |  | 247 |  | 251 |  | 215 |  | 259 |  | 263 |  | 267 |  | 271 |  | 275 |  | 279 |  | 283 |  | 287 |  | 291 |  | 295 |  | 299 |  | 303 |  | 307 |  | 311 |  | 315 |  | 319 |  | 323 |  | 327 |  | 331 |  | 335 |  | 339 |  | 343 |  | 347 |  | 351 |  | 355 |  | 359 |  | 363 |  | 367 |  | 371 |  | 375 |  | 379 |  | 383 |  | 387 |  | 391 |  | 395 |  | 399 |  | 403 |  | 407 |  | 411 |  | 415 |  | 419 |  | 423 |  | 
 |  | 193 |  |  |  | 201 |  |  |  | 209 |  |  |  | 217 |  |  |  | 225 |  |  |  | 233 |  |  |  | 241 |  |  |  | 249 |  |  |  | 217 |  |  |  | 265 |  |  |  | 273 |  |  |  | 281 |  |  |  | 289 |  |  |  | 297 |  |  |  | 305 |  |  |  | 313 |  |  |  | 321 |  |  |  | 329 |  |  |  | 337 |  |  |  | 345 |  |  |  | 353 |  |  |  | 361 |  |  |  | 369 |  |  |  | 377 |  |  |  | 385 |  |  |  | 393 |  |  |  | 401 |  |  |  | 409 |  |  |  | 417 |  |  |  |  |  | 
 |  | 197 |  |  |  |  |  |  |  | 213 |  |  |  |  |  |  |  | 229 |  |  |  |  |  |  |  | 245 |  |  |  |  |  |  |  | 261 |  |  |  |  |  |  |  | 277 |  |  |  |  |  |  |  | 293 |  |  |  |  |  |  |  | 309 |  |  |  |  |  |  |  | 325 |  |  |  |  |  |  |  | 341 |  |  |  |  |  |  |  | 357 |  |  |  |  |  |  |  | 373 |  |  |  |  |  |  |  | 389 |  |  |  |  |  |  |  | 405 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 205 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 237 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 269 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 301 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 333 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 365 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 397 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: Comparison of number of channels
Channel BW/ U-NII Band | U-NII-5 | U-NII-6 | U-NII-7 | U-NII-8
20 MHz | 24 | 4 | 17 | 12
40 MHz | 12 | 1 | 8 | 5
80 MHz | 6 | 0 | 3 | 2
160 MHz | 3 | 0 | 1 | 1
Channel BW/ U-NII Band | U-NII-5 | U-NII-6 | U-NII-7 | U-NII-8
20 MHz | 24 | 5 | 17 | 12
40 MHz | 12 | 2 | 8 | 5
80 MHz | 6 | 1 | 3 | 2
160 MHz | 3 | 0 | 1 | 1
Current
Proposed

## Slide 10: Summary and Discussion
We raise an important point about channelization in the 6 GHz band
Current channelization leaves only 10 MHz guard band at the lower end of U-NII-5 making filter design challenging
We propose to increase the guard-band on lower U-NII-5 from 10 to 20 MHz, shifting starting frequency from 5940 to 5950 MHz
However, there is lot of uncertainty from the Regulations point of view and we should be prepared for handling this kind of issues before hand
There might be some concerns about U-NII-5 filter design towards U-NII-6 in Europe and rest of the world, which should be addressed as well