## Slide 1: IEEE 802.11-IETF Liaison Report
Date: 2019-05-15
Authors:

## Slide 2: Abstract
This presentation contains the IEEE 802.11 – IETF liaison report for May 2019.

## Slide 3: IETF Meetings
Upcoming Meetings:
  July 20-26, 2019 – Montreal
  November 16-22, 2019 – Singapore
  March 21-27, 2019 – Vancouver
http://www.ietf.org
  Newcomer training: https://www.ietf.org/edu/process-oriented-tutorials.html#newcomers
  April 2016: Wireless Tutorial (Donald Eastlake), 802.11 & 802.15 tutorials (Dorothy Stanley, Charlie Perkins), see 11-16/500, July 2016: Pat Thaler & Juan Carlos – 802.1E (Privacy Considerations) and 802.c (Local MAC address usage) https://www.ietf.org/edu/tutorials.html
  http://tools.ietf.org/dailydose/

## Slide 4: IETF- IEEE 802 Liaison Activity
Joint meetings, agenda and presentations
  http://www.iab.org/activities/joint-activities/iab-ieee-coordination/
  Coordination topics include: Data Center Bridging, use of Local Address in virtualization and IoT, MAC randomization trial results, DETNET/TSN, YANG models, pervasive monitoring
  IETF-IEEE 802 coordination teleconference: February 20, 2019
802.11 related items
  Tracked: Intelligent Transportation Systems (ITS)- IETF IP Wireless Access in Vehicular Environments ipwave

## Slide 5: IETF protocol use with 802.11 technology
RFC 8576 (Informational): Internet of Things (IoT) Security: State of the Art and Challenges – mentions IEEE 802.11 APs in general and notes IEEE 802.11ah as a new, long-range means of connecting IoT devices to the Internet.
RFC 8578 (Informational): Deterministic Networking Use Cases – mentions use of IEEE 802.11 by the mining industry. May be of general interest to IEEE 802.11be.

## Slide 6: BOFs at IETF 105 July 20-26, 2019
See https://datatracker.ietf.org/wg/bofs/
TBD | BOF proposals due in ~two weeks
Notes: ila – splitting IPv6 node identity from location for improved mobility. Done efficiently without tunneling.
mls – generalized capability for message confidentiality, authentication, and integrity. Also membership verification, asynchronous key distribution, forward secrecy, post-compromise secrecy, and scalability.
Not clear that coms, ila, and mls will meet at IETF 102.

## Slide 7: IETF new groups being (re-)chartered
See https://datatracker.ietf.org/group/chartering/
anima | Autonomic Network Integrated Model and Approach (internal IESG/IAB review)
qirg | Quantum Internet Proposed Research Group (IRTF) (internal IESG/IAB review)
lamps | Limited Additional Mechanisms for PKIX and SMIME (external review)
raw | Reliable and Available Wireless (charter to be discussed in July). Formerly PAW (Predictable and Available Wireless)

## Slide 8: YANG Model Catalog
YANG catalog development
  A YANG model catalog and registry that allows users to find models relevant to their use cases from the large and growing number of YANG modules being published.
  YANG Catalog was developed through a collaboration between the IETF and the Broadband Forum, and contains many data models, including from other Standards Development Organizations (SDOs) such as the IEEE, as well as some vendor-specific data models. Interest and participation from other SDOs, equipment vendors, open source projects and network operators is encouraged.
See https://www.ietf.org/blog/yang-catalog-latest-developments-ietf-100-hackathon/
See https://yangcatalog.org/ and https://1.ieee802.org/yangsters/

## Slide 9: IoT related work
6LO
  Working Group website: http://datatracker.ietf.org/wg/6lo/charter/
  Focus: IPv6 over Networks of Resource-constrained Nodes
  Publication requested: Address Protected Neighbor Discovery for Low-power and Lossy Networks, see: https://datatracker.ietf.org/doc/draft-ietf-6lo-ap-nd/ (Updated: April 2019)
  In Progress (updated WGLC): IPv6 Backbone Router, see: https://datatracker.ietf.org/doc/draft-ietf-6lo-backbone-router/. Feedback solicited from IEEE 802.11, otherwise it will be published in current state. (Updated: February 2019)
  In Progress (updated since WGLC): IPv6 over Constrained Node Networks (6lo) Applicability & Use cases, see: https://datatracker.ietf.org/doc/draft-ietf-6lo-use-cases/. (Updated: March 2019)
  Related: Source Address Validation for WLAN: https://tools.ietf.org/html/draft-bi-savi-wlan-17. Comments solicited to ietf@ietf.org. (Updated [trivially]: May 2019)

## Slide 10: IoT related work (cont.)
6TiSCH: IPv6 over IEEE 802.15.4 Time-slotted Channel Hopping
  Working group slowly winding down, but may be re-chartered to cover other underlying layer 2 protocols. This could have a bearing on IEEE 802.11be activities.
ROLL: Working Group website: http://datatracker.ietf.org/wg/roll/
  Focus: Routing over Low Power and Lossy Networks
CORE: (Constrained RESTful Environments) Working Group website: http://datatracker.ietf.org/wg/core/
  Focus: framework for resource-oriented applications intended to run on constrained IP networks.
IoT Directorate:
  Reviews IETF drafts that are IoT related
  See: https://datatracker.ietf.org/group/iotdir/about/

## Slide 11: CAPPORT WG
CAPtive PORTal: https://datatracker.ietf.org/wg/capport/charter/
The CAPPORT Working Group will define secure mechanisms and protocols to
  allow endpoints to discover that they are in this sort of limited environment,
  provide a URL to interact with the Captive Portal, - allow endpoints to learn about the parameters of their confinement,
  interact with the Captive Portal to obtain information such as status and remaining access time, and
  optionally, advertise a service whereby devices can enable or disable access to the Internet without human interaction. (RFC 7710 may be a full or partial solution to the first two bullets)
Updates [May 2019]
  N/A

## Slide 12: RADEXT WG
See http://datatracker.ietf.org/wg/radext/
RADIUS Extensions
  The RADIUS Extensions Working Group will focus on extensions to the RADIUS protocol required to define extensions to the standard attribute space as well as to address cryptographic algorithm agility and use over new transports.
  In addition, RADEXT will work on RADIUS Design Guidelines and define new attributes for particular applications of authentication, authorization and accounting such as NAS management and local area network (LAN) usage.
  WG appears to have no remaining drafts other than one personal draft noted below. It also has not convened during the last 4 IETF meetings.
Updates [April 2019]
  Published: RFC 8559: Dynamic Authorization Proxy: https://www.rfc-editor.org/info/rfc8559
  Updated: RADIUS Extensions for 0-RTT TCP Converters: https://datatracker.ietf.org/doc/draft-boucadair-radext-tcpm-converter/

## Slide 13: EMU WG
See http://datatracker.ietf.org/wg/emu/
EAP Method Updates
  This working group has been chartered to provide updates to some commonly used Extensible Authentication Protocol methods including of EAP-TLS, EAP-AKA, EAP-AKA’ (for 5G), EAP-SIM, etc.
  The group should document any recently gained new knowledge on vulnerabilities or the possible implications of pervasive surveillance or other new concerns.
Updates [March 2019]
  Updated: Using EAP-TLS with TLS 1.3: https://datatracker.ietf.org/doc/draft-ietf-emu-eap-tls13/
  Updated: Improved Extensible Authentication Protocol Method for 3rd Generation Authentication and Key Agreement (EAP-AKA’): https://datatracker.ietf.org/doc/draft-ietf-emu-rfc5448bis/
  Related: Perfect-Forward Secrecy for the Extensible Authentication Protocol Method for Authentication and Key Agreement (EAP-AKA' PFS): https://datatracker.ietf.org/doc/draft-arkko-eap-aka-pfs/
  New: Credentials Provisioning and Management via EAP (EAP-CREDS): https://datatracker.ietf.org/doc/draft-pala-eap-creds/ (Wi-Fi noted)

## Slide 14: Operations Area Working Group
http://datatracker.ietf.org/wg/opsawg/
Updates [March 2019] Operations Area Working Group work group items
  Of interest: RFC 6632, An Overview of the IETF Network Management Protocols, see https://tools.ietf.org/html/rfc6632
  Automated network management, including YANG data models, see https://www.ietf.org/topics/netmgmt/
  Of interest: Manufacturer Usage Description Specification, see https://datatracker.ietf.org/doc/draft-ietf-opsawg-mud/
  New and related: Network Telemetry Framework, see https://datatracker.ietf.org/doc/draft-ietf-opsawg-ntf

## Slide 15: Transport Layer Security (TLS)
Transport Layer Security Working Group website: http://datatracker.ietf.org/wg/tls/charter/
Updates [May 2019]
  Updated: The Datagram Transport Layer Security (DTLS) Protocol Version 1.3: https://datatracker.ietf.org/doc/draft-ietf-tls-dtls13/ (Waiting for implementation)
  Updated: Deprecating TLSv1.0 and TLSv1.1: draft-ietf-tls-oldversions-deprecate
  Updated: TLS 1.3 Extension for Certificate-based Authentication with an External Pre-Shared Key: https://datatracker.ietf.org/doc/draft-ietf-tls-tls13-cert-with-extern-psk/

## Slide 16: Deterministic Networking (DETNET)
DETNET: https://datatracker.ietf.org/wg/detnet/charter/
  The Deterministic Networking (DetNet) Working Group focuses on deterministic data paths that operate over Layer 2 bridged and Layer 3 routed segments, where such paths can provide bounds on latency, loss, and packet delay variation (jitter), and high reliability.
  The IEEE 802.11be activities seem like they may fit in with DetNet and there was a joint IEEE-IETF DetNet discussion in Bangkok.
  Addresses Layer 3 aspects in support of applications requiring deterministic networking.
  The Working Group collaborates with IEEE 802.1 Time Sensitive Networking (TSN), which is responsible for Layer 2 operations, to define a common architecture for both Layer 2 and Layer 3.
  Example applications for deterministic networks include professional and home audio/video, multimedia in transportation, engine control systems, and other general industrial and vehicular applications being considered by the IEEE 802.1 TSN Task Group.
Of interest:
  Updated (May 2019): Deterministic Networking Architecture, see https://datatracker.ietf.org/doc/draft-ietf-detnet-architecture/
  Published: RFC 8578: Deterministic Networking Use Cases, see https://www.rfc-editor.org/info/rfc8578
  In RFC Editor’s queue: Deterministic Networking Problem Statement, see https://datatracker.ietf.org/doc/draft-ietf-detnet-problem-statement/
  New (May 2019): DetNet Data Plane: IP over IEEE 802.1 Time Sensitive Networking (TSN), see https://datatracker.ietf.org/doc/draft-ietf-detnet-ip-over-tsn/

## Slide 17: IP Wireless Access in Vehicular Environments (IPWAVE)
IPWAVE: https://datatracker.ietf.org/group/ipwave/about/
Deliverable is: document that will specify the mechanisms for transmission of IPv6 datagrams over IEEE 802.11-OCB mode
For further information:
  Updated (March 2019): Use cases and problem statement document: https://datatracker.ietf.org/doc/draft-ietf-ipwave-vehicular-networking/
  Updated (April 2019): Draft deliverable:Transmission of IPv6 Packets over IEEE 802.11 Networks operating in mode Outside the Context of a Basic Service Set (IPv6-over-80211-OCB) https://datatracker.ietf.org/doc/draft-ietf-ipwave-ipv6-over-80211ocb/ [submitted to IESG for publication]

## Slide 18: Autonomic Networking Integrated Model and Approach (ANIMA)
ANIMA: https://datatracker.ietf.org/group/anima/about/
ANIMA designs protocols to allow network operations to be carried out without requiring low-level management of individual devices
For further information:
  Updated (April 2019): BRSKI over IEEE 802.11 : https://datatracker.ietf.org/doc/draft-friel-anima-brski-over-802dot11/
  Updated (May 2019): BRSKI is Bootstrapping Remote Secure Key Infrastructures: https://datatracker.ietf.org/doc/draft-ietf-anima-bootstrapping-keyinfra/

## Slide 19: References
RFC 7241, “The IEEE 802/IETF Relationship” (RFC 4441 update)
  https://datatracker.ietf.org/doc/rfc7241/
IEEE 802 Liaisons list is available
  http://ieee-sa.centraldesktop.com/802liaisondb/FrontPage