## Slide 1: Request for Legacy IE ID for RSN Extension
Date: 2019-05-16
Authors:

## Slide 2: Abstract
Need ANA assignment for new IE created for RSN Extension element (RSNXE)

## Slide 3: Background of the IE
RSNXE and behavior approved by TGmd (Motion 116) as in comment resolution for LB236
  Approved text, as in doc. 11-19-114r5, is to be incorporated into the next draft of REVmd.
RSNXE contains an Extended RSN Capabilities field for carrying additional RSNA related capability bits
  Protected TWT Operations Support bit being the first bit added by TGmd
  Expecting other TGs to consider this element for advertising and verifying new security related capabilities, for example, Protected WUR Frame Support bit in 11ba.

## Slide 4: Where is the RSNXE?
Sent by AP in Beacons, Probe Response frames, 4-way handshake message 3, FILS (Re)association Response, and FT authentication sequence messages 3 and 4
Sent by non-AP STA in (Re)association Request frames and 4-way handshake message 2
Verified during 4-way handshake, FT reassociation, and FILS (re)association.

## Slide 5: Legacy vs Extended ID
Element ID values
  About 10 remaining
Extended Element ID values
Presence of RSNXE in all Beacons sent by AP suggests shorter duration of IE
  To minimize Beacon overhead
  Hence, legacy IE ID preferred

## Slide 6: Motion
Move to instruct ANA to assign a legacy element ID for an RSN Extension element