## Slide 1: EHT Multi-Link Operation Follow-up
Date: 2019-07-16
Authors:

## Slide 2: Abstract
In this contribution, we further evaluate performance of multi-link operation (MLO) under various BSS and OBSS traffic load, and propose the inclusion of the TID-to-link mapping concept in the TGbe SFD.

## Slide 3: Recap: Multi-link Operation
A multi-link device may perform a channel access (e.g., EDCA or Triggered Uplink Access) on multiple links independently [1,2].
When such a multi-link device obtains TXOPs on multiple links, it can send frames belonging to the same TID over multiple links simultaneously.
Data [Seq1, TID1]
5GHz
6GHz
Data [Seq2, TID1]
Data [Seq3, TID1]
Data [Seq4, TID1]
Block ACK
Block ACK
Multi-link AP
Multi-link STA
Multi-link AP
Multi-link STA
Back-off
5
4
3
2
1
0
Back-off
9
8
7
6
5
4
3
2
1
0
<Asynchronous MLO>

## Slide 4: Recap: Multi-link Operation
But, if a multi-link device is adversely affected by in-device coexistence interference across multiple links, it may not reliably transmit and receive frames over those links simultaneously.
In such a case, the multi-link device may coordinate and synchronize its transmission and reception timing over those multiple links.
Data [Seq1, TID1]
5GHz
6GHz
Data [Seq2, TID1]
Data [Seq3, TID1]
Data [Seq4, TID1]
Block ACK
Block ACK
Back-off
5
4
3
2
1
0
Back-off
9
8
7
6
5
4
Multi-link AP
Multi-link STA
Multi-link AP
Multi-link STA
PIFS
<Synchronous MLO>

## Slide 5: Performance Evaluation via Simulation
In previous performance evaluation [1], we compared throughput between single-link operation (legacy) and multi-link operation under one STA per BSS scenario.
  It shows an upper bound of the throughput gain through the multi-link operation.
In this contribution, we evaluate multi-link performance in the presence of BSS and OBSS background traffic generated by multiple STAs per BSS.

## Slide 6: Performance Evaluation via Simulation
Topology
  My BSS
    1 EHT AP and 1 EHT STA
    3 VHT STAs
  OBSS
    1 VHT AP and 3 VHT STAs
Parameters:
  MCS 9 at 80 MHz bandwidth (390 Mbps)
  Background traffic load: 2%, 20%, 55%, 85% airtime link
    Bi-directional UDP application

## Slide 7: Performance Evaluation via Simulation
An EHT AP accesses links through the asynchronous MLO.
An EHT STA accesses links through one of the following three MLO types.

## Slide 8: Performance Evaluation via Simulation
Throughput Comparisons
Chart: EHT STA Throughput (Mbps)
| 0.02 | 0.2 | 0.55000000000000004 | 0.85
Legacy | 266.75 | 171.68 | 75 | 78.74
Async | 596.77 | 439.53 | 283.78 | 175.06
Sync-DPC | 572.21 | 393.27 | 249.8 | 140.78
Sync-SPC | 533.73 | 364.51 | 183.31 | 109.89

## Slide 9: Performance Evaluation via Simulation
Latency Comparisons
Chart: EHT STA Latency (sec)
| 0.02 | 0.2 | 0.55000000000000004 | 0.85
Legacy | 0.17582 | 0.27382 | 0.6147 | 0.581
Async | 0.076709 | 0.10448 | 0.16217 | 0.26477
Sync-DPC | 0.080851 | 0.11668 | 0.18351 | 0.32557
Sync-SPC | 0.085627 | 0.12563 | 0.25679 | 0.37539

## Slide 10: Proposal
Many TGbe MLO submissions are going in a direction that allows a STA to send frames belonging to single TID over multiple links.
  But, the details about channel access protocol of the multi-link operation [2] are TBD.
In a way forward, we propose to define the TID-to-link mapping in the TGbe SFD as a top level concept of EHT MLO.
  TID-to-link mapping : A single TID is mapped to one or more links. The frames belonging to the single TID are sent on the mapped link(s).

## Slide 11: Conclusion
In this contribution, we evaluate performance (throughput and latency) of the multi-link operation under more realistic environments.
  Even though the performance gain of the MLO operation varies depending on the BSS and OBSS background traffic load, we can see throughput and latency improvement in all scenarios.
To achieve those gains, the multi-link operation should allow frames of the same TID (or different TIDs as well) to be transmitted over multiple links concurrently or non-concurrently.

## Slide 12: Reference
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-0766-01-00be-enhanced-multi-band-multi-channel-operation.pptx
[2] https://mentor.ieee.org/802.11/dcn/19/11-19-0731-00-00be-multi-link-operation.pptx
[3] https://mentor.ieee.org/802.11/dcn/19/11-19-0822-00-00be-extremely-efficient-multi-band-operation.pptx

## Slide 13: Straw Poll 1
Do you support defining a mechanism to negotiate TID-to-link mapping among the enabled links of a multi-link device (or logical entity).
  Note: TID-to-link mapping can be 1-to-1 or 1-to-many.