## Slide 1
SIG-A Changes for Ranging NDP
Date: 2019-06-12
Authors:

## Slide 2
Problem in SIG-A with Ranging NDP
Repetition of HE-LTFs
  Pre-11az STAs will decode LSIG length
  Compare with NSTS in SIG-A
  Will determine Data field length >0
    Not an NDP!
    Will try to decode “fake” Data field
  Will also affect 11ax based sniffers
Desirable to have 11az Wave 1 devices with minimal PHY changes
  Will potentially ignore NDPs with repeated HE-LTFs
  Parameters received in NDP-A need to be available at preamble time of NDP when LSIG is decoded

## Slide 3
Solution Option 1
Modify SIG-A NSTS
  Include repetitions of non-secure HE-LTFs in SIG-A NSTS
  Non-secure HE-LTFs can be limited to 8 to fit SIG-A NSTS subfield
    Typically used for 1x1 and 2x2 STAs to improve SNR
    Encoding allows for 1/2/4/6/8 LTFs
  Any decoding STA will correctly identify as NDP
    Based on LSIG length and NSTS, data field has length 0
    When NDP processing starts, can figure out true NSTS and N_REP
    Could encode N_REP in HE-MCS subfield of HE SIG-A (not used for NDP)

## Slide 4: Solution Option 2
Modify SIG-A MCS
  Set SIG-A MCS value to 0xf (values > 0xb are not used)
  Legacy STA will still think it has a data field > 0 (not an NDP)
    Can’t decode with invalid MCS
  11az STAs can know it is a Ranging NDP
    Can figure out repetitions based on LSIG length / Data field length

## Slide 5: Allowed Combinations of N_STS and LTF_REP
Possible cases:
  N_STS=1, Base P-matrix=1
    LTF_REP=1/2/4/6/8
  N_STS=2, base P-matrix=2,
    LTF_REP=1/2/3/4
  N_STS=3/4, base P-matrix=4
    LTF_REP=1/2
P-matrix sizes 2/4/6/8
  N_STS=5/6, base P-matrix=6
    LTF_REP=1
  N_STS=7/8, base P-matrix=8,
    LTF_REP=1

## Slide 6: Strawpoll I
Do you prefer modifying HE-SIGA NSTS+MCS subfields as described on slide 3 “Option 1” or only modifying MCS subfield as described on slide 4 “Option 2”?
Option 1:
Option 2:
No change: