## Slide 1: The MAC Services Mismatch Between 802.11 and 1609.4
Date: 2019-06-24
Authors:

## Slide 2: Abstract
IEEE 1609.4 provides MAC services for the upper layers of the WAVE protocol, operating just above (and partially overlapping with) the IEEE 802.11 MAC operating with dot11OCBActivated = TRUE. Some of the functions that 1609.4 needs to perform require access to facilities that are not exposed at either the 802.11 MAC_SAP or MLME_SAP. The work of TGbd will increase the number of such facilities. Therefore, it is important for TGbd to include extensions to 802.11 MAC services (when dot11OCBActivated = TRUE) that expose the functions needed by 1609 (and the analogous layers of the ITS protocol stacks used in other regulatory domains).

## Slide 3: Overview
Unexposed MAC facilities needed by 1609.4 today include:
  Direct selection of many items in the TXVECTOR, including channel, data rate/MCS, and transmit power level, on a per-MSDU basis
  The ability to specify an “expiry time” which is the value of the TSF timer at which the MSDU is no longer valid and may be purged by the 802.11 MAC before transmission
  The ability to change the station’s MAC address without resetting the entire MAC
  Measurement of Channel Busy Percentage, or access to PHY channel status
Additional MAC facilities likely to be needed with 802.11bd:
  Control of the capabilities indicated by the NGV capability indication mechanism
  Measurement of capabilities indicated by other stations whose transmission are received
  Access to far more TXVECTOR parameters as well as reporting of RXVECTOR parameters from receptions that are reported upward

## Slide 4: Comparison of the MAC_SAP as of 2016
IEEE 802.11-2016
  MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class)
  MA-UNITDATA.indication (source address, destination address, routing information, data, reception status, priority, service class)
  MA-UNITDATA-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class)
IEEE 1609.4-2016
  MA-UNITDATAX.request (source address, destination address, routing information, data, priority, service class, Channel Identifier, Time Slot, Data Rate, TxPwr_Level, ExpiryTime)
  MA-UNITDATA.indication not specified, presumably the 802.11 primitive is used
  MA-UNITDATAX-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class)

## Slide 5: Functions Added by TGbd Needing SAP Exposure
The enhanced MAC and PHY functionality being added by TGbd are going to require further extension
Selection of MAC enhancements provided by TGbd on a per-MSDU basis
Selection of PHY enhancements provided by TGbd on a per-MSDU basis
Reporting of optional facilities used to convey received MSDUs
Reporting of station capabilities, both for received MSDUs and for stations within RF range whose transmissions are detected but not addressed for reception at this station

## Slide 6: Comparison of the MLME_SAP as of 2016
IEEE 802.11-2016
The subset of 802.11 MLME primitives explicitly listed in 1609.4 are:
MLME-GET
MLME-SET
MLME-TIMING_ADVERTISEMENT
MLME-GETTSFTIME
IEEE 1609.4-2016
MLME extension primitives specified in 1609.4:
MLMEX-TA / MLMEX-TAEND
MLMEX-CHSTART / MLMEX-CHEND
MLMEX-REGISTERTXPROFILE / MLMEX-DELETETXPROFILE
MLMEX-CANCELTX
MLMEX-GETUTCTIME
MLMEX-AddressChange
MLMEX-SendPrimitive
The primitives in bold appear to require support within the MAC

## Slide 7: Extending the MAC Data Service Primitives (after 11-19/0276r4)
The best way to extend MAC Data Service is to define a new, NGV-specific parameter to each of the MAC Data Service primitives:
  MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class, radio environment request vector)
  MA-UNITDATA.indication (source address, destination address, routing information, data, reception status, priority, service class, radio environment status vector)
  MA-UNITDATA-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class, radio environment status vector)
A radio environment {request/status} vector parameter shall be present when dot11OCBActivated is TRUE and absent otherwise.
  By defining the new parameter as a vector, and describing the elements of these vectors in separate sub-clauses, the editorial impact on existing clause 5 text is minimized.

## Slide 8: Radio Environment Request Vector Contents (after 11-19/0276r4)
The Radio Environment Request Vector allows the higher layers to control the format, encoding, and MPDU handling for the 802.11bd transmission
The elements of the Radio Environment Request Vector include:
  Transmission format (legacy/NGV, data rate/MCS, repetitions, etc.)
  Coding alternatives (BCC, LDPC, etc.)
  Spatial stream alternatives (MIMO, STBC, etc.)
  Aggregation alternatives
  PHY alternatives (band, channel, transmit power level, etc.)
  Expiry time (time after which this MSDU is discarded if not transmitted)
  … whatever else needs to be controlled within the NGV MAC and PHY functionality)
A value that permits selection within the MAC should exist for each element

## Slide 9: Radio Environment Status Vector Contents (after 11-19/0276r4)
The Radio Environment Status Vector provides to the higher layers status about the current radio environment and the most recent 802.11bd reception
The elements of the Radio Environment Status Vector include:
  Transmission format used (legacy/NGV, data rate/MCS)
  Coding alternatives used (BCC, LDPC, etc.)
  Spatial stream alternatives used (MIMO, STBC, etc.)
  PHY alternatives used (band, channel, etc.)

## Slide 10: Reporting of Radio Environment Characteristics
The characteristics of the radio environment are reported on a periodic basis, independent of receptions of MSDUs, so ought to be reported separately
MA-RADIOENVIRONMENT.indication (Channel Busy Percentage, Capability Percentage, Station Count)
  Channel Busy Percentage – as already defined in IEEE 1609
  Capability Percentage – proposed (as “TechPercentage”) in 11-19/0783
  Station Count – number of stations detected during most recent measurement period of Channel Busy Percentage and Capability Percentage

## Slide 11: MLME SAP Extension
IEEE 1609.4 includes a set of primitives extending the MLME_SAP. These appear as MLMEX-primitives in Clause 7 of IEEE 1609.4-2016
  As a minimum, the MLME_SAP in 802.11bd should include a request/confirm primitive pair that corresponds to MLMEX-AddressChange
  It is recommended strongly that the MLME_SAP in 802.11bd include a generic means for the MAC at an NGV station to accept additional, ITS-related management primitives
  It is unclear whether 802.11bd should include the full set of MLMEX primitives
    The exact set of extensions required vary with regional ITS standards
    The functions of the various regional MLME extensions should probably remain in the higher-layer standards documents, rather than having redundant definitions in documents that are maintained by different organizations, and are updated according to different schedules
    Defining the full set of MLMEX primitives will also necessitate adding quite a bit of normative text elsewhere in the MAC that may complicate and/or delay the work of TGbd

## Slide 12: Additional Attributes in 802.11bd MIB
Some of the NGV-specific parameter values are static, and can be managed as MIB attributes rather than service primitive parameters at the MAC or MLME SAPs. These include:
  NGV activation (the NGV equivalent of dot11OCBactivated)
  NGV capabilities (to be indicated in transmissions from this station)
  NGV bands supported
  Measurement interval for ChannelBusyPercentage (default value 100ms)
  ChannelBusyPercentage smoothing parameters (to accommodate CBR/CBP differences)
  Measurement interval for TechPercentage (default value 1000ms)