## Slide 1: Coexistence in 6 GHz License-exempt Spectrum
Date: 2019-07-17
Authors:

## Slide 2: Unlicensed Spectrum - Principles
Same carrier can be accessed by multiple networks or operators
Networks and carriers can use different technologies
  Not limited only to IEEE and 3GPP technologies
No restrictions on the operation mode of networks and devices
  Networks can be managed or ad-hoc
    IEEE networks are optimized for ad-hoc operation
    3GPP networks are optimized for managed operation

## Slide 3: Unlicensed spectrum in 6 GHz – Key features
No RLAN technologies already deployed
  Opportunity for enhancing spectrum efficiency by using modern technology neutral coexistence
Coexistence with incumbent services is critical
  Needs some form of AFC (automatic frequency coordination)
  Discussions are ongoing in regulatory bodies on how this is to be achieved
The range of spectrum made available for unlicensed operation is still under discussion
  6.425 GHz to 7.125 GHz could be assigned as licensed spectrum in some regions
  5.925 GHz to 6.425 GHz expected to be assigned as unlicensed spectrum in both US and Europe

## Slide 4: 3GPP Technologies – Channel Access in 5 GHz
Coexistence with a large number of devices already deployed in 5 GHz was a key design constraint for LTE-LAA
  The design criterion adopted was to not harm a Wi-Fi network more than another Wi-Fi network
  The design criterion was biased towards already deployed networks to ensure they were not affected was adopted
    e.g., an LTE-LAA network with zero throughput would meet the criterion
Channel access procedures aligned with IEEE 802.11 on most aspects
  Such alignment was prioritized over optimizing the performance of 3GPP networks in many cases

## Slide 5: 3GPP Technologies – Channel Access in 5 GHz
Started from a clean slate with several fundamental aspects discussed
  LBT Protocol
    Load based vs. Frame based
      Frame based was an attractive choice due to frame structure of LTE
    LBT types: Random back-off with a contention window of fixed size (cat. 3 LBT) vs. variable size with exponential backoff (cat. 4 LBT)
      Cat. 3 LBT was better suited to the frame structure of LTE
    Slot size: 9 µs vs. 20 µs
      20 µs better suited for LTE with 1 ms subframes
    Contention window sizes: EDCA vs. other options
      Shorter contention window size very attractive for LTE UL and control
  Maximum Channel Occupancy Time (MCOT)
    Channel occupancy times aligned with ETSI BRAN harmonized standard
  Energy detection thresholds
    An absolute and calibrated ED threshold that is 10 dB lower than Wi-Fi
  Multi-carrier operation
    Wi-Fi channel bonding sets adopted for LTE UL

## Slide 6: 3GPP Technologies – Channel Access in 5 GHz
Remaining differences in channel access design are mainly due to one or more of the following
  Fundamental differences between a managed and an ad-hoc network
    LTE and NR UEs do not transmit any data on their own unless explicitly granted by a supervising node
  Performance considerations
  Complexity considerations
Coexistence depends on sensing threshold, LBT protocol and transmit duration
The most significant remaining difference between IEEE 802.11 and 3GPP technologies is the differing sensing thresholds used by 802.11 nodes to 802.11 and non-802.11 nodes
  IEEE 802.11 devices defer to 802.11 devices at a lower sensing threshold and all other devices at a higher sensing threshold
  LTE (and NR-U) devices defer to all devices at the same threshold

## Slide 7: A Single Common Maximum Threshold
A single common maximum energy detection threshold for all technologies
  Fundamentally fair coexistence: It enables all nodes to be respected at the same energy level regardless of which technology they use
  Superior performance: Allows fully flexible adaptation of the threshold used for each deployment
  Simple and robust compliance verification
  Flexible technology innovation
    Coexistence is decoupled from the use of technology specific signals: Each technology can independently develop preambles or other signals/protocols that provide benefits such as power saving, system performance improvements etc. without concerns on coexistence
Additional sensing mechanisms for sharing within a network can be independently used as long as these mechanisms comply with the single common maximum energy detection threshold across all technologies. Examples:
  A network operating without scheduling can use preambles for sharing (e.g., IEEE 802.11a/n/ac/ax)
  A managed network can use scheduled operation for sharing (e.g., LTE, NR, IEEE 802.11ax)

## Slide 8: 3GPP Technologies – Channel Access in 5 GHz
For 3GPP technologies, a single ED threshold of −72 dBm/20 MHz was chosen to be in between the ED and PD thresholds for IEEE 802.11 devices to enable a long term convergence for all technologies, including 802.11ax, to this single harmonized threshold
  IEEE 802.11ac was an already deployed technology at the time LTE-LAA was developed but harmonization with 802.11ax was considered a possibility
  Adoption of ED at −72 dBm/MHz for all technologies in 5 GHz, including IEEE 802.11ax, was part of an ETSI TC BRAN agreement. This agreement and associated discussions are documented in [2–6].
3GPP RAN1 requested IEEE 802.11 to adopt an aligned ED threshold of −72 dBm. IEEE 802.11 declined this request and explained it as follows [1]:
  “IEEE 802 declined 3GPP RAN1’s request because it would put 802.11ax systems at a disadvantage compared to billions of existing and future 802.11a/n/ac systems using an ED threshold of −62 dBm and at a disadvantage to any LAA systems not detecting 802.11 preambles at −82 dBm.”

## Slide 9: Coexistence in 6 GHz
Unlicensed spectrum in 6 GHz does not have any already deployed RLAN devices preventing the adoption of a single threshold
  No issue with existing IEEE 802.11n/ac devices that use a higher ED threshold => ED threshold can be reduced to −72 dBm (or some other value common to all nodes, networks and technologies)
  Preamble detection threshold can optionally be raised to −72 dBm at least for other IEEE 802.11ax networks (no legacy 80211n/ac devices)
The 6 GHz band provides an excellent opportunity to converge to a single common maximum harmonized energy detect (ED) threshold for all devices
  Ensures truly fair coexistence for all current and future technologies operating in this spectrum

## Slide 10: Regulations for unlicensed spectrum
Regulations should be simple
  The ETSI BRAN Harmonized Standard for 5 GHz includes technology specific exemptions and is too complex to build conformance tests
  Better to focus on key aspects and avoid unnecessary complexity
Regulations should be testable
  Simple regulations allow the key aspects to be tested and enforced
  Reliance only on declaration of compliance to regulations undermines the effectiveness of regulatory requirements
Regulations should be identical for all devices, networks and technologies
  No exceptions should be provided to any technology or device

## Slide 11: Regulations for unlicensed spectrum
The sensing threshold options in the latest BRAN draft for 5 GHz are a good example of unnecessary complexity
  There are two options, ED = −72 dBm and ED/PD = −62 dBm/−82 dBm if an IEEE 802.11a preamble is used
The use of the 802.11a preamble by other technologies may prevent implementations from using additional information to improve robustness
  Because the 802.11a preamble “is weakly protected” some implementations may perform sanity checks based on Wi-Fi signals following the preamble [9]
It is not clear if all 802.11 devices are calibrated to accurately satisfy the −82 dBm PD threshold
  Thresholds applied in some products may depend on background noise and measurements [7, 8]
Strict requirements on the PD threshold should not limit flexibility to optimize performance
  Some 802.11 products have features that allow raising the PD threshold up to −65 dBm to optimize performance in certain scenarios [10-12]

## Slide 12: Summary
Regulatory framework should be simple, testable, technology neutral and be future proof to allow any new technologies to use the spectrum without the constraints of older technologies
Coexistence with existing (e.g. fixed) services in the band is important to consider
Greenfield spectrum provides an excellent opportunity for truly fair coexistence between RLANs operating in the band
A single common maximum energy detection threshold for all devices and technologies is crucial to ensure fairness and performance benefits for all users of unlicensed spectrum in 6 GHz

## Slide 13: References
IEEE EC-17-0064-00-00EC, Liaison Statement to 3GPP RAN/RAN1/RAN4 related to PD & ED issues, 22 March 2017
Cisco, “Compromise summary for EN 301 893,” BRAN(15)194r1
RCWG Chair, “Agreed Compromise on Adaptivity,” BRAN(15)200r4
J. Prats, “Meeting minutes of the RCWG sessions during BRAN 85,” BRAN(15)190
J. Prats and D. Boldy, “Meeting minutes of the RCWG sessions during BRAN 86,” BRAN(16)10
D. Boldy, “Meeting minutes of the RCWG sessions during BRAN#88,” BRAN(16)116r1
D. Coleman, “What is a Clear Channel Assessment (CCA)?,” Aerohive Networks Blog, Jul. 2018, available: https://blog.aerohive.com/what-is-clear-channel-assessment-cca/
K. Jamieson, B. Hull, A. Miu, and H. Balakrishnan, “Understanding the Real-World Performance of Carrier Sense,” ACM SIGCOMM Workshop on Experimental Approaches to Wireless Network Design and Analysis (E-WIND), Aug. 2005, available: http://nms.csail.mit.edu/papers/index.php?detail=133
E. Perahia and R. Stacey, “Next Generation Wireless LANs: Throughput, Robustness, and Reliability in 802.11n,” Cambridge University Press, ISBN 978-0521885843, Aug. 2008
Cisco, “Meraki Documentation – Receive Start of Packet (RX-SOP),” available: https://documentation.meraki.com/MR/Radio_Settings/Receive_Start_of_Packet_(RX-SOP)
Cisco Meraki, “Documentation—RF Profiles,” available: https://documentation.meraki.com/MR/Radio_Settings/RF_Profiles#RX-SOP
Cisco, “Cisco RX-SOP Deep Dive,” YouTube video, August 2014, available: https://www.youtube.com/watch?v=p5nx4L3RIVk