## Slide 1: Per-Packet Multiple Link Selection
Name | Affiliations | Address | Phone | email
Alan Jauh | Unisoc |  | +86-131-6727-1685 | alan.jauh@unisoc.com
Yanchao Hsu |  |  |  | 
Henry Yu |  |  |  | 
Long Wang |  |  |  | 
Xin Zuo | Tencent |  |  | 
Kate Meng |  |  |  | 
Date: 2019-07-12
Authors:

## Slide 2: Introduction
We have proposed a Joint MAC + multiple concurrent PHY architecture for multi-band operation to support the concept of per-packet multi-link assignment[1]
We got some feedbacks on “Why we need to do that?”. Here we further clarify this concept and provide some examples

## Slide 3: Recap (1) Multiple Links System
Ch1 and Ch2 are different channels that can be in the same or different bands, e.g. one is in 2.4GHz and the other is in 5GHz
The traffic is put into the queue and use all or part of the available channels to send
Each packet can assign available channel(s) independently
AP
STA
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
Joint MAC or Unified MAC

## Slide 4: Recap (2) Queuing Arrangement Example
A
B
C
D
E
Channel 1 queuing list
A
B
E
Channel 2 queuing list
Packets A, B, E are allowed to be transmitted via both channels
Packet C and D are allowed to be transmitted via channel 1 only
...
...
Dispatch
...
Descriptors
A(1,2)
B(1,2)
C(1)
D(1)
E(1,2)
Centralized queuing list
Removal module to remove the redundant queuing list after transmission

## Slide 5: Recap (3) Per Packet Selection Example
One device support two links (Link_1, Link_2). Each sending packet can has the following option
  Link_1 only
  Link_2 only
  Link_1 or Link_2 (depends on which link send first)
  Link_1 and Link_2 (allowed to send via both link concurrently)
Further constraint may apply, for example
  The packet send to Link_1 only device will only use Link_1
  If one application group has special requirement to use Link_2 only, the packets belong to this application group will only use Link_2
Packets for the same TID can have different assignments for some special purposes

## Slide 6: Multiple Links System Example
AP
STA2
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
LMAC3
PHY3
Ch 3
STA3
MAC
LMAC1
LMAC2
PHY1
PHY2
STA1
MAC
LMAC1
PHY1
RM:
Removal module to remove the redundant queuing list after transmission
RM
RM
RM

## Slide 7: Example 1: Legacy Support
AP
STA C
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
5GHz
Ch 2
2.4GHz
PHY1
PHY2
PHY1
PHY2
STA A
STA B
MAC
LMAC1
PHY1
MAC
LMAC1
PHY1
RM
RM
Single link device
Single link device

## Slide 8: Per Packet Multiple Link Selection Example 1
In [1] shows per packet multi-link assignment can support legacy devices (single link devices)
  In a multi-link system with link 1 in 5GHz and link 2 in 2.4GHz. STA A is a 2.4GHz legacy device. STA B is a 5GHz device. STA C is a multi-link device support both band.
  In AP side, the data sent to STA A will be assigned to link 2 only, the data sent to STA B will be assigned to link 1 only, the data send to STA C can be assigned to link 1 only, link 2 only or both link 1 and link 2
  Per packet multi-link assignment can support legacy single link devices

## Slide 9: Example 2: Multi-Channel FDD Support
AP
STA C
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
5GHz
BW80
Ch 2
2.4GHz
BW20
PHY1
PHY2
PHY1
PHY2
RM
RM
TCP data TX
TCP data TX
TCP ACK TX
TCP ACK TX

## Slide 10: Per Packet Multiple Link Selection Example 2
In [2] shows separate TCP data and TCP ACK in different channel can improve the TCP throughput in Multi-Channel FDD concept
  If we can know the incoming data is TCP data or TCP ACK, we can assign TCP data to one channel(e.g., an 80MHz channel) and assign TCP ACK to another channel(e.g. a 20MHz channel)
    Otherwise, since TCP data is relatively long packet and TCP ACK is short packet, we can assign long packet(TCP data) to one channel(e.g., an 80MHz channel) and assign short packet(TCP ACK) to another channel(e.g. a 20MHz channel)
  Per packet multi-link assignment has flexibility to gain this benefit

## Slide 11: Example 3: Control Channel Support
LMAC3
PHY3
AP
STA2
MAC
LMAC1
LMAC2
MAC
LMAC1
LMAC2
Ch 1
Ch 2
PHY1
PHY2
PHY1
PHY2
LMAC3
PHY3
Control Ch
STA3
MAC
LMAC1
LMAC2
PHY1
PHY2
STA1
RM
MAC
LMAC1
LMAC2
PHY1
PHY2
RM
RM
RM

## Slide 12: Per Packet Multiple Link Selection Example 3
Dedicated control channel(s)
  This feature can be supported by assigning the related control frames to use the link(s) of control channel(s)

## Slide 13: Conclusion
We have listed some examples that per packet multiple link selection can support or has benefit
With per packet multiple link selection capability, the system can be more flexible.
It is possible to enable other applications based on this feature.
  Additional information may be required for the per packet assignment depend on application

## Slide 14: References
[1] 802.11-19/760r1 Multi-band Opinion
[2] 802.11-18/1518r0 EHT Multi-Channel Operation