## Slide 1: Conditional Packet Duplication in Multiple Link System
Date: 2019-07-12
Authors:
Name | Affiliations | Address | Phone | email
Alan Jauh | Unisoc |  | +86-131-6727-1685 | alan.jauh@unisoc.com
Yanchao Hsu |  |  |  | 
Henry Yu |  |  |  | 
Long Wang |  |  |  | 
Xin Zuo | Tencent |  |  | 
Kate Meng |  |  |  | 

## Slide 2: Introduction
“Improve the worst case latency and jitter” is described in EHT PAR [1]
In RTA report, Duplicate Mode and Joint Mode for multiple link are mentioned [2]
We propose a conditional packet duplication mode in multiple link system

## Slide 3: Duplicate Mode/Joint Mode
AP
STA
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
Duplicate Mode
AP
STA
1
2
3
4
8
9
5
6
7
Joint Mode

## Slide 4: Duplicate Condition
Timer for each RTA TX frame is required
  Timer start when the RTA TX frame is received from upper layer
  Each RTA TX frame has its latency requirement, depends on the application
When the timer of a RTA frame has expired its threshold, the event of duplicate condition is triggered
E.G., a RTA frame has latency requirement 10ms and the duplicate condition threshold is set to 60% of latency requirement, i.e. 6ms. When its timer expire 6ms, the duplicate condition is triggered

## Slide 5: Conditional Packet Duplication
When duplicate condition is triggered
  The RTA frame will be duplicated from current link to other supported links
    The original and duplicated frames have high priority. E.G., it can be in the first queuing list location if there is no other ongoing or pending high priority frame
    The transmission of the duplicated frames in different links can be concurrently
  When any duplicated frame is successfully transmitted, the other pending or ongoing duplicated frame transmission can be stopped

## Slide 6: Conditional Duplication Mode Example
AP
STA
1
3
5
7
9
2
4
8
AP
STA
1
3
5
7
9
2
4
6
8
6
6
6
6
6
Channel blocked
Other frames
insert duplicated frame
Packet Failed.
Assume retry only in the same link
Case 1
Case 2
duplicate condition is triggered
duplicate condition is triggered
insert duplicated frame

## Slide 7: RTA Traffic Insertion
When duplicated condition is triggered
  If the RTA traffic sender is the TXOP holder, it can override the queuing list and send out the RTA traffic ASAP
  The original TXOP may be set up for AC that is different to the RTA traffic. We can allow insertion RTA traffic in a TXOP that is for different AC to speed up the RTA traffic transmission

## Slide 8: TXOP Transfer
When duplicated condition is triggered
  AP may take over the TXOP ownership from STA A temporarily for the transmission of RTA traffic.
    If AP is the RTA traffic sender, AP can send the RTA traffic after AP takes over the TXOP ownership
    If the other STA B is the RTA traffic sender, AP will transfer the TXOP ownership to STA B
  After the completion of RTA traffic transmission, AP returns the TXOP back to the original TXOP holder STA A

## Slide 9: Conclusion
We propose a conditional duplicate mode in multiple link system
  When the transmission of RTA traffic is not completed successfully within a specified time interval, the duplication condition is triggered
  The conditional duplication mode is enabled to speed up the transmission of duplicated RTA traffic in high priority

## Slide 10: References
[1] 802.11-18/1231r6 EHT draft proposed PAR
[2] 802.11-18/2009r6 RTA report draft