## Slide 1: A unified transmission procedure for multi-AP coordination
Date: 2019-07-02
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Guogang Huang |  |  |  | 
Bo (Boyce) Yang |  |  |  | 

## Slide 2: Introduction
In the PAR of EHT SG, Multi-Access Point (AP) Coordination has been considered as a main candidate feature [1].
  Item 5.2b:
  The main candidate features that have been discussed are:
  320MHz bandwidth and more efficient utilization of non-contiguous spectrum,
  Multi-band/multi-channel aggregation and operation,
  16 spatial streams and Multiple Input Multiple Output (MIMO) protocols enhancements,
  Multi-Access Point (AP) Coordination (e.g. coordinated and joint transmission),
  Enhanced link adaptation and retransmission protocol (e.g. Hybrid Automatic Repeat Request (HARQ)),
  If needed, adaptation to regulatory rules specific to 6 GHz spectrum
There are many modes of Multi-AP Coordination, such as
  Coordinated BF [2][3][6]
  Coordinated OFDMA [3]
  Coordinated SR [4]
  Joint transmission [5]
Many contributions have shown performance gain in various scenarios[2-5]
In this contribution, we propose a unified transmission procedure to support the above multi-AP coordination modes

## Slide 3: Requirements of multi-AP transmission
Two key aspects that are needed in the unified procedure are synchronization and resource allocation.
Synchronization
  In joint transmission, very tight synchronization is needed to ensure a reasonable performance [5].
  In co-BF and co-OFDMA, symbol level synchronization is needed to avoid mutual interference between OBSS [6].
  In co-SR, PPDU level synchronization is preferred to make the mutual interference controllable.
Resource allocation
  In all the modes, slave APs need to know how long the transmission could be
  In joint transmission, slave APs need to know which data frames to send, what transmission parameters to use
  In co-OFDMA, slave APs need to know which channels/RUs to use
  In co-BF and co-SR, slave APs need to know the receiving STAs to decide the beamforming vector and transmit power
Hence, a specific frame is needed to provide the synchronization and resource allocation functions. We propose to use a slave trigger frame to perform the above functions.

## Slide 4: Unified transmission procedure
The master AP shall transmit a slave Trigger frame (TF) to initiate the multi-AP transmission
  How to determine the master AP is TBD
    The master AP can be a selected AP which is pre-defined
    The master AP can be any AP that successfully accesses the channel
The function of the slave TF includes
  Synchronization for all the APs
    Make sure the transmissions from all APs start and end at the same time
      Time/frequency/phase synchronization for joint transmission
      Symbol level synchronization for co-BF and co-OFDMA
      PPDU level synchronization for co-SR
  Resource allocation for the slave APs
    Notifying the slave APs which mode to use
    Allocating the time/frequency/spatial/power domain resources that can be used by each slave AP

## Slide 5: Examples of frame exchange sequence
DL procedure
  slave TF + simultaneous DL data + UL BA
Slave TF
Data 1
Data 2
Data 3
BA
BA
BA
AP 1
(master)
AP 2
AP 3
Slave TF
Data 1
Data 2
Data 3
BA
BA
BA
AP 1
(master)
AP 2
AP 3
Basic TF
Basic TF
Basic TF
UL procedure
  slave TF + simultaneous basic TF + simultaneous UL data + DL BA

## Slide 6: Slave Trigger Frame format
Regarding the slave trigger frame format, one option is to reuse the Trigger frame format defined in TGax, which contains a Common info field and one or more User Info fields
  The common info field carries the information for all slave APs
  The user info field carries the information for a specific slave AP
Use a reserved value of the Trigger Type field to represent slave TF
Another option is to define a new subtype of control frame
Both options are considerable
Frame Control
Duration
RA
TA
Common Info
Per AP Info
Padding
FCS
……
Per AP Info

## Slide 7: Conclusion
  We propose a unified transmission procedure for multi-AP coordination which supports various types of coordination modes, including
    Coordinated BF
    Coordinated OFDMA
    Coordinated SR
    Joint Transmission
  Two possible options of slave trigger frame format are discussed

## Slide 8: Reference
[1] 11-18-1231-06-0eht-eht-draft-proposed-par
[2] 11-18-1510-01-0eht-ap-coordinated-beamforming-for-eht
[3] 11-18-1509-00-0eht-features-for-multi-ap-coordination
[4] 11-19-801-00-0eht-ap-coordination-in-eht
[5] 11-19-0384-00-0eht-joint-processing-mu-mimo-update
[6] 11-19-0638-00-00be-nulling-and-coordinated-beamforming