## Slide 1: Channel Access in Multi-band operation
Date: 2019-09-05
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yifan Zhou |  |  |  | 
Ming Gan |  |  |  | 
Dandan Liang |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Multi-band/multi-channel operation is defined in EHT PAR [1] to
  Increase throughput
  Enhance reliability
  Reduce latency
Since the terminology “Link” is preferred based on discussion in [2,3], it is used throughout this contribution;
Current channel access is designed for single link, how to access in multi-link need to be discussed, especially when the links are dependent.

## Slide 3: Synchronized/Asynchronized ML
Based on the simultaneous TX&RX capability, there are two types of multi-link (ML);
  Asynchronized ML
  Synchronized ML
Both of them are needed depending on scenarios.
  Asynchronized ML: The two links are far enough to ignore the power leakage from each other link. The channel access of multi links could be independent, which makes the protocol design simple.
  Synchronized ML: When multiple links are close to each other, the power leakage from the other link cannot be ignored, so multi-link TX/RX always need to be aligned when designing the protocol. The benefit is it can aggregate several close links to get high peak throughput, which is very important for the areas with less unlicensed spectrum.

## Slide 4: PPDU Parameters in ML
PPDU length in each link is dependent in synchronized ML, which is used to align the start or end time in different links;
Other parameters besides the PPDU length in each link could be independent, e.g. BW, MCS, NSTS,…
Dynamic bandwidth negotiation could be supported in each link independently, based on the channel status on its own channel;
Similar as single link, the bandwidth of a PPDU within a TXOP should always be smaller or equal to the bandwidth of previous PPDU in the same TXOP.

## Slide 5: Asynchronized ML
Each link could has its own EDCA parameters, e.g. CW_min, CW_max, AIFS, …;
Channel access is independent in each link;
Pros:
  Minor or no change is needed for channel access in standard
Cons:
  Need large guard bands between each links, or need self interference cancellation between multi-links;

## Slide 6: Synchronized ML
Always need to consider the constraint that one ML entity cannot simultaneously support TX and RX in different links during the communication;
The channel access is dependent for multi-links;
May have many different ways to do channel access, here we classify them into two kinds of architectures in following slides;
Pros:
  Could support more links in the limited spectrum, or reduce the complexity of self interference between adjacent links.
Cons:
  Complex channel access rules and transmission procedures

## Slide 7: Synchronized ML
Architecture 1:
  there is one primary link and one or more secondary link, backoff performs on primary link;
  when the backoff counter is reduced to 0, the ML entity could send PPDUs on the primary link and the secondary links which the CCA results are idle in PIFS time preceding the transmission;
  for each transmission, the primary link should always be included;
  Single link STAs and legacy STAs associate on the primary link.

## Slide 8: Synchronized ML
Architecture 2:
  There is no primary link, backoff performs simultaneously on multiple links;
Two potential issues need to considered
  Issue 1: backoff in multiple links is usually finished at different times, but the transmission in ML need to be synchronized
    When the backoff in one link first is reduced to 0, and aggregate other secondary links, it will cause fairness issue in secondary links.
    When the backoffs in all links are reduced to 0, and then transmit PPDUs, EHT STA will have less chance to access the channel than the legacy STA;
  Issue 2: how to support legacy STAs and single link EHT STAs?
    Legacy STAs and single link EHT STAs cannot respect the constraint that ML AP entity cannot TX & RX simultaneously at different links.

## Slide 9: Transmissions in synchronized ML
Two UL PPDUs, or two DL PPDUs are supported in synchronized ML;
  Two PPDUs can be sent by single ML entity, or different ML entities
  The start time of two PPDUs may not be aligned
  The end time of two PPDUs should be aligned
One UL PPDU and one DL PPDU in different links is not supported if they have any overlapping in time domain;
UL PPDU 1
UL PPDU 2
DL PPDU 1
DL PPDU 2
UL PPDU 1
DL PPDU 2
X
Case 1
Case 2
Case 3

## Slide 10: Conclusion
There are two types of multi-links based on the capability of simultaneous TX&RX on different links, namely, asynchronized ML and synchronized ML;
Both types have their own use scenarios and benefits;
The issues that need to be considered in the channel access of both types of ML are summarized.

## Slide 11: Straw Poll 1
Do you agree the PPDU bandwidths on multiple links between two multi-link devices below rules?
  The PPDU bandwidth on each link could be different;
  The PPDU bandwidth on each link is independent of the CCA of other link(s);
  The PPDU bandwidth selection rules in each link are the same as in single link.
  SP deferred

## Slide 12: Straw Poll 2
Do you agree that the channel access mechanism in each link of multiple asynchronous links can be independent from the channel access mechanism of the other links?
Y:20
N:4
A:20

## Slide 13: Straw Poll 3-a
Do you agree that synchronous multiple links need a different channel access mechanism from asynchronous multiple links?
  Exact designs are TBD
SP deferred

## Slide 14: Straw Poll 3-b
Do you agree that a multi-link capable device that doesn’t support simultaneous transmit and receive needs a different channel access mechanism from a multi-link capable device that support simultaneous transmit and receive on different links?
  Exact designs are TBD
SP deferred

## Slide 15: Straw Poll 4-a
Do you agree that below rule is needed on two synchronous links?
  two UL PPDUs, or two DL PPDUs could be transmitted concurrently, and the end times of the two PPDUs shall be aligned if responses are needed for frames carried in both PPDUs;

## Slide 16: Straw Poll 4-b
Do you agree that below rule is needed for a multi-link capable device that doesn’t support simultaneous transmit and receive on different links?
  two UL PPDUs, or two DL PPDUs could be transmitted concurrently, and the end times of the two PPDUs shall be aligned if responses are needed for frames carried in both PPDUs;

## Slide 17: Reference
[1] EHT PAR document, 11-19-0244-00-0eht-eht-par-document
[2] 11-19-0823-00-00be-multi-link-aggregation
[3] 11-19-0822-00-00be-extremely-efficient-multi-band-operation