## Slide 1: Mechanisms for Reliable V2X operation
Date: 2019-09-16
Authors:
Onn Haran, Autotalks

## Slide 2: Future V2X Communication Requirement
  Increased need for reliability while more challenged to achieve it
  Higher reliability needs
  V2X provides more data which isn’t available by any other sensor, such as pedestrian observed by other vehicle
  V2X data will be used for vehicle control
  Functional safety requires certainty that V2X is operating properly
  Greater reliability challenges
  Higher hidden node probability due to increased channel load, following the longer messages
  Higher activity in adjacent channels

## Slide 3: Reliable Broadcast Communication
  MAC acknowledgement can add Broadcast delivery guarantee to 802.11
  MAC acknowledgement is baseline for media-agnostic upper layers
  Upper layers are defined for DSRC and C-V2X. DSRC would be disadvantageous if only C-V2X (as added in Rel. 16) would support delivery guarantee
  MAC acknowledgement assures bounded latency
  In Europe, messages may be sent up to 1 second apart. Lost message doubles that
  MAC acknowledgement is simpler than upper layer acknowledgement
  Using RSSI as simple predictor if message should be retransmitted (simplification from last meeting)

## Slide 4: Broadcast Acknowledgement Transmission Operation
  Broadcast Ack message reports the successfully received MAC addresses

## Slide 5: Reaction to Broadcast Acknowledgement
  Principle of operation: if RSSI of BroadcastAck is high, then prior self-transmission should have been received by the device transmitting the BroadcastAck. Absence of self MAC address in BroadcastAck report content indicates a failure
  No need to know vehicles’ location
  RSSI threshold should be set well above sensitivity level (for example, -77dBm) to ignore imbalance between different vehicles, and to handle only major failures
  Retransmission is avoided for data freshness requirements. Instead, new message should be triggered

## Slide 6: Channel Load Consideration
  Broadcast Ack transmission should have low impact on channel load
  It is unnecessary that all vehicles in a dense environment would share their feedback
  Three options are presented to reducing number of transmission
  A. Some vehicles are transmitting all the time: Each vehicle selects if it transmits
  B. All vehicles are transmitting 100mS log some time: Each vehicle selects period between TX
  C. Limiting packet length to N reported stations (strongest received) [can be applied to A&B]
Channel load | Option A: Probability of transmission | Option B: Period between transmission
<10% | 100% | 100mS
<25% | 50% | 400mS
Otherwise | 10% | 1sec

## Slide 7: Broadcast Acknowledge Operation Sparse environment
2. Broadcast Ack:
Green car not listed
All vehicles transmit Broadcast Ack every 100mS
1. Safety message transmission
3. Safety message transmission Triggered since message wasn’t received by purple vehicle
2. Broadcast Ack:
Green car listed

## Slide 8: Broadcast Acknowledge Operation Dense environment
Some of the vehicles transmitted Broadcast Ack in last cycle
2. Broadcast Ack: Green car not listed
1. Safety message transmission
2. Broadcast Ack: Green car listed
3. Safety message transmission Triggered since message wasn’t received by purple vehicle

## Slide 9: Upper Layer New Packet Generation Decision
Functionality is shown for the sake of complexity estimation. Performed in upper layer
Did self vehicle transmit in last 100mS?
Is self MAC address not in BroadcastACK with high RSSI?
Trigger new packet generation (it might be planned anyhow)
Yes
No
Yes
No need to check
No
Transmission was successful

## Slide 10: Broadcast Ack can be Encoded as new BlockAck variant
  Reserved values can be utilized

## Slide 11: Possible Broadcast Ack Format
  Timing information: Log UTC start and stop times
    Used to determine relevancy of Ack to last transmitted message
  UTC can be represented as [0…9999]mS aligned with GNSS timing
  Information per successfully received message:
    MAC addresses: Compressed (e.g. 16bits) for minimizing channel load
    RSSI of received message
    Detecting self failures: If RSSI reported in BroadcastAck is much lower than measured for BroadcastAck, then TX fails. If much higher, then RX fails
Compressed RX MAC address #1
2
Octets
Compressed RX MAC address #2
2
Compressed RX MAC address #N
2
. . . . . .
Log UTC start
2
Log UTC stop
2
RSSI of message #1
1
RSSI of message #2
1
RSSI of message #N
1

## Slide 12: Straw Poll #1
Should 802.11bd define feedback of received MAC addresses decoded in a BlockAck variant?
Y: 6
N: 2
A: 23
July 2019
Onn Haran, Autotalks

## Slide 13: Straw Poll #2
Assuming 802.11bd includes Broadcast Ack, what should be specification scope?
Option A: Broadcast ACK format definition: 1
Option B: Broadcast ACK format and transmit and receive operation: 9
None of the above:
Abstain: Many
July 2019
Onn Haran, Autotalks

## Slide 14: References
  [1] Reliable V2X operation, Onn Haran 802.11-19-0717/r1
July 2019
Onn Haran, Autotalks

## Slide 15: Backup

## Slide 16: Broadcast Ack Transmission
Broadcast Ack transmission
Logging received MAC addresses with valid CRC
Periodic transmission of the log
Start log
Stop log
Packet for transmission
UTC
Functionality is shown for the sake of complexity estimation
Operation may be performed either in MAC layer or in upper layer
MAC address of RX packet with valid CRC

## Slide 17: Broadcast Ack Reception
Broadcast Ack reception
Checking
  Is RSSI > Threshold?
  Is self MAC address listed inside Broadcast Ack?
  Is time of last transmitted packet within log period?
Received Broadcast Ack
Received MAC address
Self MAC address found / not found
Last TX packet is within reported period
Functionality is shown for the sake of complexity estimation
Operation may be performed either in MAC layer or in upper layer
Received Broadcast Ack RSSI
UTC of last transmitted packet
Received RSSI > Threshold