## Slide 1: Discussion on HARQ
Date: 2019-09-09
Authors:

## Slide 2: Introduction
Hybrid ARQ (HARQ) exploits a retransmission and combining mechanism
  Receiver stores erroneously received packets
  Receiver combines the retransmitted signal with the stored signal
The following topics are considered
  Retransmission scheduling
  Control information for HARQ procedures
  HARQ unit
  ACK/NACK

## Slide 3: Retransmission
We consider the following two retransmission strategies
  Contention based retransmission
  Back to back retransmission
    New transmission and retransmission in same TXOP

## Slide 4: Contention Based Retransmission
Perform contention before retransmission
  No changes to current IEEE 802.11 retransmission except combining transmissions
  Issues:
    Large number of HARQ processes are needed, e.g. HARQ process/memory per TID and per STA
    Possible solution: limit HARQ process to certain TID

## Slide 5: Scheduled Retransmission
Reserve TXOP including HARQ retransmission
  Smaller amount of memory is required.
  Fast retransmission is possible
  Issues:
    Number of HARQ retransmissions is limited to TXOP limit
    Can be inefficient when number of retransmissions is less than expected.

## Slide 6: Control Information
Two potential ways to carry HARQ control information
  PLCP header
  New MAC control frame
    BSS color may be not precise enough, and larger size of ID clarification may be needed
    With higher MCSs, the mac control frame contain more control information compared with PLCP header with lower MCSs
HARQ control information
  Transmitter and receiver ID
  HARQ parameters
  Feedback related information (if needed)
  HARQ process ID (if needed)

## Slide 7: HARQ Unit
HARQ Unit: unit for retransmission
Option 1: MPDU
  HARQ unit is encoded based on each MPDU size
    Size of codeword can be varying for each MPDU
  Need to inform MPDU size in HARQ control information
    Large HARQ control information size
  Can reuse Block Ack

## Slide 8: HARQ Unit (Cont.)
Option 1-1: Fixed size with one or more MPDU(s)
  HARQ unit size is chosen based on MPDU sizes
    Each HARQ unit may contains multiple MPDUs
  Need to inform HARQ unit size in HARQ control information
  Can reuse Block Ack
  Compared to option 2,
    May have larger padding overhead
    Less HARQ control information

## Slide 9: HARQ Unit (Cont.)
Option 2: Codeword
  ACK/NACK for each codeword
    Feedback overhead could be high
  Need CRC per codeword
  Need to store even successful codewords at PHY layer

## Slide 10: HARQ Unit (Cont.)
Option 2-1: Multiple codewords with fragmentation
  ACK/NACK for each of HARQ unit
  Or reuse Block Ack using dynamic fragmentation
  Compared to option 2
    Fragmentation overhead
    Lower feedback overhead
    No CRC per codeword
    No need to store successful HARQ unit

## Slide 11: ACK/NACK Channel
Two potential ways to carry HARQ ACK/NACK information
Block Ack: minimal design effort
New PHY feedback: optimize overhead, e.g. omitting transmitter and receiver ID

## Slide 12: Summary
Discussed about
  Retransmission scheduling
  HARQ control information and its exchange
  HARQ Unit for retransmission
  ACK/NACK channel

## Slide 13: Reference
[1] IEEE 802.11-19/1098r0 Acknowledgement for HARQ Transmission