## Slide 1: Considerations of New Queue Mechanism for Real-Time Application
Date: 2019-07-10
Authors:

## Slide 2: Abstract
A few frames having worst-case latency are critical for some RTAs.
There is lack of means to improve the worst-case latency/jitter for RTA, in current .11 design.
Careful design is required to achieve the tradeoff
Latency-critical traffic that is medium/low in transmitting frequency and small in frame size, may have the design freedom to fulfil the requirement by RTA.

## Slide 3: Background
Goal/Requirement
  PAR: “This amendment defines at least one mode of operation capable of improved worst case latency and jitter.”[1]
  A few frames experiencing worst-case latency may not degrade the average latency, but are critical to some RTAs.
    i.e. no responds in online mobile games, damaging the user experiences.
    accidents in remote control in manufacturing,
    etc.

## Slide 4: Background
Current EDCA may be unable to help improve worst-case latency.
  Discriminating AC queues is mainly in the probability to access to the wireless medium, w.r.t. large number of frames.
    Good at average  potential worst-case latency.
  Once backoff counter is determined from [0,CW], the latency is almost determined.
    Some high-AC frames get unlucky  potential worst-case latency
  ACs differentiate traffic, only according to QoS fields (DSCP, UP, etc.).
    Latency-critical traffic may be treated equally as throughput-critical traffic.  potential worst-case latency
  AC could be stacked with frames.  Potential worst-case latency

## Slide 5: Background
A new design of queue may
  improve by
    linking access delay directly to the latency required by the latency-critical traffic;
    categorizing traffic, taking into consideration more parameters;
    being grant with higher priority in channel access; etc.
  Need to consider the tradeoff, such as that between latency and throughput; that between prioritization and fairness; etc.
Latency-critical traffic could be characterized into 4 types:
  Frequent and large in size  too difficult to satisfy both.
  Frequent and small  may damage the fairness, throughput, etc..
  Less frequent and large  possible to satisfy, but maybe challenging.
  Less frequent and small  possible to satisfy, without much damaging.
    Also matches with the realistic RTA traffic, including online mobile gaming, remote control in manufacturing, specific IoT application, etc.

## Slide 6: Sketch of New Queue
filter
The new design of queue respects EDCA.
“Speeding up” the channel access procedure, when the frame waiting time is close to the required latency advertised.
  i.e., reducing backoff counter.
  other ways to “speed up”.
Filtering frames according to not just QoS fields, but the size and frequency.
  Maintaining the throughput, fairness, etc.
The new queue could be dynamically opened/terminated.
  Adapting to the change in network/channel.
  Avoiding stacking/abusing.
frame
New Queue
frame
frame
frame
frame
frame
Indicates latency required
Reduce backoff counter

## Slide 7: Simulations
Detail design and simulations…

## Slide 8: Conclusions
We emphasized the challenges the current EDCA trying to improve worst-case latency.
  Latency requirement of RTA can not be directly reflected.
  Current EDCA is good at average, but may need pay more attention on individual frames.
  QoS fields are not sufficient to discriminate among traffic.
A new queue design could help improve the worst-case latency.
  We have sketch out the new design.

## Slide 9: References
[1] 802.11-18/1231r6 EHT draft proposed PAR