## Slide 1: Updated Channelization for 6 GHz
Date: 2019-07-14
Authors:
Name | Affiliation | Address | Email
Imran Latif | Quantenna Communications | 1704 Automation Parkway, 95131, San Jose, CA, USA | ilatif@quantenna.com
Sigurd Schelstraete |  |  | sschelstraete@quantenna.com
Debashis Dash |  |  | ddash@quantenna.com
Huizhao Wang |  |  | hwang@quantenna.com

## Slide 2: Background
In 11-19/876 and CID 21378 the channelization for 6 GHz was presented
Since 11ax supports operation in the 6 GHz band so channelization definition is of imperial importance
In 11-19/876 it was shown that current 6GHz proposed channelization is not efficient
Hence, we propose an update to the previously presented 6 GHz channelization

## Slide 3: Recap: Channel Allocation in the 6 GHz in 11ax
11ax D4.0 Section 27.3.22.2 defines the channel allocation in the 6 GHz band as,
The resulting channelization, by applying this rule, is extremely challenging for both
  the TX filter design
  and RX filter design

## Slide 4: 6 GHz Uncertainties
Following uncertainties exist in the 6 GHz rule making today
  USA
    FCC is planning to open 1200 MHz of total band, dividing it in to 4 U-NII bands
    Though FCC has not finalized the rule making, however, certain bands will most probably be under AFC control
    Limitations due to this AFC are still unknown
    AFC itself can take long time in finalization and by the time it will be fixed, 11ax standardization might have been finalized
  Europe
    EC is planning to open 500 MHz in 600 band but that will also take at least 2 – 3 years from now onwards.
  Rest of the world
    Far behind on 6 GHz for unlicensed as compared to USA and Europe
Due to this uncertain nature of rules for 6 GHz band makes it even more important that we should design channelization such that it is independent of rules to come.

## Slide 5: Current Channel Allocation in the 6 GHz in 11ax1
Starting frequency of 5940 MHz
  Only 10 MHz of Guard band for U-NII-5
  Challenging filter design
Channels can cross U-NII boundaries
In case U-NII-5 and 6 work under different regulatory rules
  No 80 MHz channel in U-NII-6
  Only one 40 MHz channel in U-NII-6
1 – Channel numbers in this Figure are shown as a continuation of 5GHz channel numbers.
U-NII-5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-6 |  |  |  |  |  |  |  |  |  | U-NII-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 5945 |  | 5965 |  | 5985 |  | 6005 |  | 6025 |  | 6045 |  | 6065 |  | 6085 |  | 6105 |  | 6125 |  | 6145 |  | 6165 |  | 6185 |  | 6205 |  | 6225 |  | 6245 |  | 6065 |  | 6285 |  | 6305 |  | 6325 |  | 6345 |  | 6365 |  | 6385 |  | 6405 |  | 6425 |  | 6445 |  | 6465 |  | 6485 |  | 6505 |  | 6525 |  | 6545 |  | 6565 |  | 6585 |  | 6605 |  | 6625 |  | 6645 |  | 6665 |  | 6685 |  | 6705 |  | 6725 |  | 6745 |  | 6765 |  | 6785 |  | 6805 |  | 6825 |  | 6845 |  | 6865 |  | 6885 |  | 6905 |  | 6925 |  | 6945 |  | 6965 |  | 6985 |  | 7005 |  | 7025 |  | 7045 |  | 7065 |  | 7085 |  | 7105 |  | 7125 | 
 | 189 |  | 193 |  | 197 |  | 201 |  | 205 |  | 209 |  | 213 |  | 217 |  | 221 |  | 225 |  | 229 |  | 233 |  | 237 |  | 241 |  | 245 |  | 249 |  | 213 |  | 257 |  | 261 |  | 265 |  | 269 |  | 273 |  | 277 |  | 281 |  | 285 |  | 289 |  | 293 |  | 297 |  | 301 |  | 305 |  | 309 |  | 313 |  | 317 |  | 321 |  | 325 |  | 329 |  | 333 |  | 337 |  | 341 |  | 345 |  | 349 |  | 353 |  | 357 |  | 361 |  | 365 |  | 369 |  | 373 |  | 377 |  | 381 |  | 385 |  | 389 |  | 393 |  | 397 |  | 401 |  | 405 |  | 409 |  | 413 |  | 417 |  | 421 |  |  | 
 | 191 |  |  |  | 199 |  |  |  | 207 |  |  |  | 215 |  |  |  | 223 |  |  |  | 231 |  |  |  | 239 |  |  |  | 247 |  |  |  | 215 |  |  |  | 263 |  |  |  | 271 |  |  |  | 279 |  |  |  | 287 |  |  |  | 295 |  |  |  | 303 |  |  |  | 311 |  |  |  | 319 |  |  |  | 327 |  |  |  | 335 |  |  |  | 343 |  |  |  | 351 |  |  |  | 359 |  |  |  | 367 |  |  |  | 375 |  |  |  | 383 |  |  |  | 391 |  |  |  | 399 |  |  |  | 407 |  |  |  | 415 |  |  |  |  |  |  | 
 | 195 |  |  |  |  |  |  |  | 211 |  |  |  |  |  |  |  | 227 |  |  |  |  |  |  |  | 243 |  |  |  |  |  |  |  | 259 |  |  |  |  |  |  |  | 275 |  |  |  |  |  |  |  | 291 |  |  |  |  |  |  |  | 307 |  |  |  |  |  |  |  | 323 |  |  |  |  |  |  |  | 339 |  |  |  |  |  |  |  | 355 |  |  |  |  |  |  |  | 371 |  |  |  |  |  |  |  | 387 |  |  |  |  |  |  |  | 403 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 203 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 235 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 267 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 299 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 331 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 363 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 395 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Center Frequency [MHz]
20 MHz Channels
40 MHz Channels
80 MHz Channels
160 MHz Channels

## Slide 6: Previously Proposed Channel Allocation in the 6 GHz in 11ax
Shifting the starting frequency from 5940 to 5950 MHz provides 20 MHz of Guard band and,
  More relaxed filter design
  Similar to the U-NII-1 band
  One complete 80 MHz channel in the U-NII-6 band
  Two 40 MHz channels in the U-NII-6 band
  The U-NII-5 band still has three 160 MHz channels
Note: In Europe 6 GHz band ends at 6425 MHz and shifting the channel by 10 MHz can impact the filter design on the higher end of the 6 GHz band in order to meet the European OOBE limits.
U-NII-5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-6 |  |  |  |  |  |  |  |  |  | U-NII-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5935 |  | 5955 |  | 5975 |  | 5995 |  | 6015 |  | 6035 |  | 6055 |  | 6075 |  | 6095 |  | 6115 |  | 6135 |  | 6155 |  | 6175 |  | 6195 |  | 6215 |  | 6235 |  | 6255 |  | 6075 |  | 6295 |  | 6315 |  | 6335 |  | 6355 |  | 6375 |  | 6395 |  | 6415 |  | 6435 |  | 6455 |  | 6475 |  | 6495 |  | 6515 |  | 6535 |  | 6555 |  | 6575 |  | 6595 |  | 6615 |  | 6635 |  | 6655 |  | 6675 |  | 6695 |  | 6715 |  | 6735 |  | 6755 |  | 6775 |  | 6795 |  | 6815 |  | 6835 |  | 6855 |  | 6875 |  | 6895 |  | 6915 |  | 6935 |  | 6955 |  | 6975 |  | 6995 |  | 7015 |  | 7035 |  | 7055 |  | 7075 |  | 7095 |  | 7115 |  | 
 |  | 191 |  | 195 |  | 199 |  | 203 |  | 207 |  | 211 |  | 215 |  | 219 |  | 223 |  | 227 |  | 231 |  | 235 |  | 239 |  | 243 |  | 247 |  | 251 |  | 215 |  | 259 |  | 263 |  | 267 |  | 271 |  | 275 |  | 279 |  | 283 |  | 287 |  | 291 |  | 295 |  | 299 |  | 303 |  | 307 |  | 311 |  | 315 |  | 319 |  | 323 |  | 327 |  | 331 |  | 335 |  | 339 |  | 343 |  | 347 |  | 351 |  | 355 |  | 359 |  | 363 |  | 367 |  | 371 |  | 375 |  | 379 |  | 383 |  | 387 |  | 391 |  | 395 |  | 399 |  | 403 |  | 407 |  | 411 |  | 415 |  | 419 |  | 423 |  | 
 |  | 193 |  |  |  | 201 |  |  |  | 209 |  |  |  | 217 |  |  |  | 225 |  |  |  | 233 |  |  |  | 241 |  |  |  | 249 |  |  |  | 217 |  |  |  | 265 |  |  |  | 273 |  |  |  | 281 |  |  |  | 289 |  |  |  | 297 |  |  |  | 305 |  |  |  | 313 |  |  |  | 321 |  |  |  | 329 |  |  |  | 337 |  |  |  | 345 |  |  |  | 353 |  |  |  | 361 |  |  |  | 369 |  |  |  | 377 |  |  |  | 385 |  |  |  | 393 |  |  |  | 401 |  |  |  | 409 |  |  |  | 417 |  |  |  |  |  | 
 |  | 197 |  |  |  |  |  |  |  | 213 |  |  |  |  |  |  |  | 229 |  |  |  |  |  |  |  | 245 |  |  |  |  |  |  |  | 261 |  |  |  |  |  |  |  | 277 |  |  |  |  |  |  |  | 293 |  |  |  |  |  |  |  | 309 |  |  |  |  |  |  |  | 325 |  |  |  |  |  |  |  | 341 |  |  |  |  |  |  |  | 357 |  |  |  |  |  |  |  | 373 |  |  |  |  |  |  |  | 389 |  |  |  |  |  |  |  | 405 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 205 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 237 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 269 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 301 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 333 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 365 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 397 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Efficient Channel Allocation in the 6 GHz in 11ax
In addition to shifting starting frequency by 10 MHz we propose to further perform channelization independently for each U-NII band.
This has multiple benefits
  Same channelization can be used worldwide, e.g. , FCC’s U-NII 5 seems to be EU’s 6 GHz band so it is beneficial to design channelization which can work for all regions
  If different bands are under different access rules (AFC control) this channelization still will perform better
  Overall, there are always same number of channels even with this optimized proposal
  Provides huge flexibility for U-NII 5 lower end and also facilitates the filter design for all different U-NII bands
U-NII-5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-6 |  |  |  |  |  |  |  |  |  | U-NII-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U-NII-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5935 |  | 5955 |  | 5975 |  | 5995 |  | 6015 |  | 6035 |  | 6055 |  | 6075 |  | 6095 |  | 6115 |  | 6135 |  | 6155 |  | 6175 |  | 6195 |  | 6215 |  | 6235 |  | 6255 |  | 6075 |  | 6295 |  | 6315 |  | 6335 |  | 6355 |  | 6375 |  | 6395 |  | 6415 |  | 6435 |  | 6455 |  | 6475 |  | 6495 |  | 6515 |  | 6535 |  | 6555 |  | 6575 |  | 6595 |  | 6615 |  | 6635 |  | 6655 |  | 6675 |  | 6695 |  | 6715 |  | 6735 |  | 6755 |  | 6775 |  | 6795 |  | 6815 |  | 6835 |  | 6855 |  | 6875 |  | 6895 |  | 6915 |  | 6935 |  | 6955 |  | 6975 |  | 6995 |  | 7015 |  | 7035 |  | 7055 |  | 7075 |  | 7095 |  | 7115 |  | 

## Slide 8: Newly Proposed Efficient Channel Allocation
No reduction is number of 20, 40, 80 or 160 MHz channels as compared to current channelization but in fact increase of those
It might look that U-NII 5 has two 160 MHz channels as compared to three, but with this channelization, U-NII 7 gets two 160 MHz channels instead of one
Furthermore, moving the 160 MHz channels into middle of U-NII 5 band provides huge flexibility for the design of TX and RX filters as opposed to current design where lower end 160 MHz channel tends to be useless anyways.

## Slide 9: Comparison of number of channels
Channel BW/ U-NII Band | U-NII-5 | U-NII-6 | U-NII-7 | U-NII-8
20 MHz | 24 | 4 | 17 | 12
40 MHz | 12 | 1 | 8 | 5
80 MHz | 6 | 0 | 3 | 2
160 MHz | 3 | 0 | 1 | 1
Channel BW/ U-NII Band | U-NII-5 | U-NII-6 | U-NII-7 | U-NII-8
20 MHz | 24 | 5 | 17 | 12
40 MHz | 12 | 2 | 8 | 6
80 MHz | 6 | 1 | 4 | 3
160 MHz | 2 | 0 | 2 | 1
Current
Newly Proposed

## Slide 10: Summary and Discussion
We raise an important point about channelization in the 6 GHz band
Current channelization is extremely in-efficient and is not fit for the future changes for the 6 GHz band
We propose to increase the guard-band on lower U-NII-5 from 10 to 20 MHz, shifting starting frequency from 5940 to 5950 MHz
Also we propose to have separate channelization for each U-NII band, thus introducing huge flexibility and addressing the uncertainties which are associated with Regulation of 6 GHz band worldwide.

## Slide 11: Strawpoll
Do you agree with the proposed channelization where we present an efficient channelization dedicated to each U-NII band for 6 GHz band?

## Slide 12: CID 21378